## AUTOMOTIVE INDUSTRY STANDARD

Information on Technical Specifications

to be submitted by

the Vehicle Manufacturer

(Revision 5)

PRINTED BY

THE AUTOMOTIVE RESEARCH ASSOCIATION OF INDIA

P.B. NO. 832, PUNE 411 004

ON BEHALF OF

AUTOMOTIVE INDUSTRY STANDARDS COMMITTEE

UNDER

CENTRAL MOTOR VEHICLE RULES – TECHNICAL STANDING COMMITTEE

SET-UP BY

MINISTRY OF  ROAD TRANSPORT and HIGHWAYS

(DEPARTMENT OF ROAD TRANSPORT and HIGHWAYS)

GOVERNMENT OF INDIA

June 2014

Status chart of the Standard to be used by the purchaser for updating the record

| Sr. No. | Corrigenda. | Amendment | Revision | Date | Remark | Misc. |
| --- | --- | --- | --- | --- | --- | --- |

General   remarks:

# Information on Technical Specifications to be submitted

# by the Vehicle Manufacturer

- INTRODUCTION:

This document consolidates the information to be provided by the motor vehicle manufacturer, construction equipment vehicle manufacturer and agricultural tractor manufacturer while applying for a certificate of Compliance to CMVR. Subsequent to the decisions of the CMVR – Technical Standing Committee, this standard was revised to take care of the new regulations and requirements in CMVR and to simplify the existing procedure. The panel constituting the testing agencies and the manufacturers discussed and decided upon the technical details that are required to be provided by the vehicle manufacturers at the time of applying for the type approval.   The AIS-007 (Revision 5) documents were finalized in the month of March 2014, taking into consideration the new standards that were decided to be implemented under CMVR, by Automotive Industry Standards Committee and CMVR-Technical Standing Committee. The revision of 2, 3 and 4 wheeler automotive vehicle specifications have been carried out considering the introduction of the following new standards which are under the process of getting notified under CMVR, namely,

- AIS-004(Part 3) – EMC

- AIS-091 – Mechanical Coupling Devices

- AIS-092 – Close Coupling Devices

- AIS-047 – Interior fittings for other than M1 vehicles.

- AIS-071(Part 1 & 2) – Controls , Tell tales  & Symbols

- AIS-075 – Vehicle Alarm Systems

- AIS-076 – Anti-theft devices

- AIS-072 – Child Restraint Systems

- AIS-096 – Head –On Collision

- AIS-098 – Offset frontal Collision

- AIS-099 – Lateral Collision

- AIS-100 – Pedestrian Protection

- AIS-102 (Part 1 & 2) – Hybrid vehicles

- AIS-110 –Temporary Use Spare Wheel

- AIS-084 (Part 1 & 2) – Defrost / Demist Systems

- AIS-083 – Headlamp Cleaning Devices

- AIS-052 (Rev. 1) – Bus Body Code

- AIS-093 – Truck Body Code

- AIS-063 – School Bus Code

- AIS-068 – Window Frames for buses

- OBD- II requirements for BS-IV Emission norms

- IS 14664- Brake 2 & 3 Wheeler with ABS

The technical specifications for the 2 & 3 wheelers (L1, L2 and L5 category) have been aligned to 2002/24/EC of 18th march 2002 repealing Council Directive 92/61/EEC, to the fullest extent possible. The Automotive Industry Standards Committee responsible for preparation of this standard is given in Annex I

- APPLICATION FOR TYPE APPROVAL:

2.1	Application for Type Approval of Automotive Vehicles:

While applying for the Type Approval, the application shall be accompanied by the following documents, as applicable to the provisions for which such compliance is sought:

- List of provisions for which compliance is sought to be established.

- The Technical Specifications as per formats given in Table 1 to 13 as applicable.

- Details of location of Chassis number and code for month and year of manufacture as per Rule 122 of CMVR, in Table –11.

- Copies of certificates or test reports of compliance to various provisions, which may have already been obtained from authorized Testing Agencies. This may be attached along with Table–8.

d)	Information indicated in Table-10, regarding the Criteria for Extension of Approval (CEA) for selecting the model/(s) to be tested, in case variant/(s) are to be approved.

- Copies of previous certificates or test reports for other models, if any, which can be used for establishing compliance of the model to be type approved, with a note explaining the details. (Refer Table-9)

- The details of CNG components for CNG OE vehicles as per Table-20.

- The details of LPG components for LPG OE vehicles as per Table-21.

- Publications available (Owner's Manual and service manual)

2.2   	Application for Type Approval of Construction Equipment Vehicles:

While 	applying for the Type Approval, the application shall be accompanied by the following documents, as applicable to the provisions for which such compliance is sought:

- List of provisions for which compliance is sought to be established.

- The Technical Specifications as per formats given in Table 14 & 15.

- Details of location of Chassis number and code for month and year of manufacture as per Rule 122 of CMVR, in Table –11.

- Copies of certificates or test reports of compliance to various provisions, which may have already been obtained from authorized Testing Agencies. This may be attached along with the Table-18. (Refer Table – 18).

- Copies of previous certificates or test reports for other models, if any, which can be used for establishing compliance of the model to be type approved, with a note explaining the details.(Refer Table - 19).

- Publications available (Owner’s Manual and service manual)

Note:  In case these publications are not available at the time of submitting the prototype vehicle, they shall be submitted by the manufacturer as and when they are ready but not later than beginning of commercial production. In case these publications are not available at the time of prototype testing, the relevant information required by the test agency, shall be provided by the manufacturer.

2.3   	Application for Type Approval of Agricultural Tractors:

While 	applying for the Type Approval, the application shall be accompanied by the following documents, as applicable to the provisions for which such compliance is sought:

- List of provisions for which compliance is sought to be established.

- The Technical Specifications of the agricultural tractor are as per formats given in  Table-16 & 17

- The technical details of the engine fitted to agricultural tractors shall be as per Table -4D.

- Details of location of Chassis number and code for month and year of manufacture as per Rule 122 of CMVR, in Table-11.

- Copies of certificates or test reports of compliance to various provisions, which may have already been obtained from authorized Testing Agencies. This may be attached along with the Table-18.             (Refer Table -18 )

- Copies of previous certificates or test reports for other models, if any, which can be used for establishing compliance of the model to be type approved, with a note explaining the details. (Refer Table- 9).

- Publications available (Owner’s Manual and service manual)

Note: In case these publications are not available at the time of submitting the prototype vehicle, they shall be submitted by the manufacturer as and when they are ready but not later than beginning of commercial production. In case these publications are not available at the time of prototype testing, the relevant information required by the test agency, shall be provided by the manufacturer.

- BRIEF TECHNICAL SPECIFICATION :

  - Motor Vehicles: The format for brief technical specifications to be submitted by the manufacturer is given in Table - 7, which is essentially an enclosure to the certificate of CMVR compliance. The details of all the  variant to be covered in one certificate shall be included in one document. In case more information is to be provided separate Tables and Annexures could be included.

  - Construction Equipment Vehicles: The format for brief technical specifications to be submitted by the construction equipment vehicle manufacturer is given in Table -14, which is essentially an enclosure to the certificate of CMVR compliance. The details of all the variant to be covered in one certificate shall be included in one document. In case more information is to be provided separate Tables and Annexures could be included.

  - Agricultural Tractors: The format for brief technical specifications to be submitted by the manufacturer is given in Table-16, which is essentially an enclosure to the certificate of CMVR compliance. The details of all the variant to be covered in one certificate shall be included in one document. In case more information is to be provided separate Tables and Annexures could be included.

- DETAILED  TECHNICAL  SPECIFICATIONS :

  - Motor vehicles: The format for detailed technical specifications for two and three wheelers is given in Table-1. The formats for detailed specifications for four wheelers and above are given in Tables-2 to 6. In case the application is being made for establishing conformity against specific provision, the details specified in the standard/document for that provision shall be submitted. This may be in the format specified in the applicable standard or a combination of Tables -2 and Tables - 3 to 6, as appropriate by which the information needed is complete.

  - Construction Equipment Vehicles: The format for detailed technical specifications for construction equipment vehicles are given in Table-15. In case the application is being made for establishing conformity against specific provision, like engine testing / type approval, the details specified as per this format shall be submitted to the testing agencies.

  - Agricultural Tractors: The format for detailed technical specifications for agricultural tractors is given in Table - 17. In case the application is being made for establishing conformity against specific provision, like engine testing / type approval, the details specified as per this format shall be submitted to the testing agencies. The details of the test reports of the safety critical components shall be submitted in Table -18 format to the testing agencies.

  - Application for approval of Bus bodies as per AIS-052 (Rev. 1) : The format of technical specifications to be submitted by the Bus Body Builder or the Bus Manufacturer for approval of the bus body are as given in Table - 22 and Table - 22A. The Original Equipment Manufacturers who have already submitted the component or system approval details during the certification of their Chassis variants (Drive Away Chassis / Cowl and Chassis/ Cabin and Chassis/ Chassis with Front End Structure etc.,) in        Table - 8 need not submit the information in Table - 22A format.

  - Additional specifications  for approval for Electric / Hybrid vehicles : The format of technical specifications to be submitted by the vehicle manufacturer for specific details of electric / hybrid vehicles  are as given in Table - 23.

- GENERAL  INFORMATION :

5.1		The above said technical information is to be submitted in sheets of A4 size or should be foldable in A4 size. The letter and figures shall be legible and in a minimum font size not less than 10.

5.2		Each of these documents should have a unique identification number, indicated on each sheet. Appropriate numbering scheme shall be used by the manufacturer to indicate the revision status also.

5.3		Information, for which the space provided in the format is not sufficient, may be submitted in a separate document. Such a document should have a unique identification number, indicating the modification status, and this number should be referred in the Technical Specifications appropriately.

5.4		The technical specification shall be submitted in the number of copies as desired by the testing agency. One set of the technical specifications shall be the original with the original signatures of the authorized person of the company and the other sets may be the Photostat copies of the original.

  - If the item in any clause is not applicable, for any particular model, the manufacturer should indicate “Not Applicable” or “NA” against the main heading and sub-clauses need not be answered in such cases. The serial numbers indicated against each entry shall not be changed.

  - The technical specifications of CNG and LPG kits shall be provided to the testing agencies as per the format specified in the relevant AIS-024 and                 AIS-025 standards respectively.

- OTHER INFORMATION :

  - The details of information to be submitted by the automotive vehicle manufacturer regarding test reports/certificates, already obtained, for establishing compliance of the model, sought to be type approved, are given in Table - 8 and Table - 8A. For construction equipment vehicles and agricultural tractors, the same information is given in Table -18.

6.2		The details of information to be submitted by the automotive vehicle manufacturer regarding test reports / certificates for other models which can be used as proof of compliance of the model which is sought to be type approved, are listed in Table - 9. For construction equipment vehicles and agricultural tractors, the same information is given in Table - 19.

6.3	     Information regarding the Worst Case Criteria for selecting the model/(s) to be tested, in case variant/(s) are to be approved, is given in Table -10. This would apply to the category of vehicles for which the worst case criteria is available as per the respective standards.

6.4	The format for declaring the location of chassis number and code for the year and month of manufacture is given in Table-11. This would apply to motor vehicles, construction equipment vehicles and agricultural tractors.

  - The changes in the technical specifications for the already certified models or new variants with slight engineering changes shall be intimated in the format given in Table -12 and Table -12 A.

  - The additional technical information to be submitted for the Battery Operated Vehicles is given in Table-13. This shall be given in addition to the other specifications wherever applicable.

6.7     The agricultural tractor manufacturer or the engine manufacturer shall submit their application to the test agency for testing or approval  of the agricultural tractor engine, as per Table-4D format.

- TRANSITORY PROVISIONS :

  - For all items, for which the compliance is to be established to the notified standard, the requirement of “Identification Number” has been called for. This may be filled up to the extent possible.

  - This revised format takes into account all the requisite technical parameters for the respective standards that were finalized by AISC and decided to be implemented by CMVR-Technical Standing Committee after April 2011. The vehicle manufacturer may not fill the data for those technical requirements which are not notified, as applicable at the time of submitting their application to the testing agencies.

Table 1 AIS-007 (Revision 5)

# DETAILED TECHNICAL SPECIFICATIONS

| INFORMATION RELATING JOINTLY TO L1, L2 AND L5 CATEGORY VEHICLES ( 2 and 3 Wheelers) |
| --- |
| 0.0 | General |
| 0.1 | Make | : |  |
| 0.2 | Type (state any possible variants and versions: each variant and each version must be identified by a code consisting of numbers or a combination of letters and numbers) | : |  |
| 0.2.1 | Commercial name (s) | : |  |  |  |
| 0.3 | Means of type identification if stated on vehicle | : |  |
| 0.3.1 | Location of that means of identification | : |  |
| 0.4 | Vehicle category (AIS-053) | : |  |
| 0.5 | Name and address of manufacturer with contact persons’ name, designation, e-mail, phone nos. etc. Provide details of importer, if applicable. | : |  |
| 0.5.1 | Name(s) and address (es) of assembly plants | : |  |  |  |
| 0.5.2 | Name and address of the vehicle importer |  |  |  |  |
| 0.6 | Name and address of manufacturer's authorized representative. if any | : |  |
| 0.7 | Method of inscription of VIN on the chassis | : |  |
| 0.7.1 | The serial numbering (of production vehicles) of the type begins with No | : |  |
| 0.8 | Position and method of affixing the component type-approval mark for components and separate technical units | : |  |
| 1.0 | General arrangement of the vehicle |
| 1.1 | Photos and/or drawings of a typical vehicle | : |  |  |  |

Table 1 AIS-007 (Revision 5)

| 1.2 | Drawing of the complete vehicle indicating overall length, width, track and height. | : |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 1.2.1 | Wheelbase | : |  |  |  |
| 1.3 | Number of axles and wheels (where appropriate. number of crawler tracks or belts): | : |  |
| 1.4 | Position and arrangement of engine | : |  |
| 1.5 | Number of seating positions | : |  |
| 2.0 | Weights (in kg) |
| 2.1 | Vehicle kerb weight(9) | : |  |  |  |
| 2.1.1 | Distribution of that weight between the axles | : |  |  |  |
| 2.2 | Vehicle kerb weight together with rider (reference weight) | : |  |  |  |
| 2.3 | Gross Vehicle Weight | : |  |  |  |
| 2.3.1 | Division of that weight between the axles | : |  |  |  |
| 2.3.2 | Maximum technically permissible weight (maximum permissible axle weight) on each of the axles |  |  |  |  |
| 2.3.2.1 | Front Axle | : |  |  |  |
| 2.3.2.2 | Rear Axle | : |  |  |  |
| 2.4 | Maximum hill-starting ability (Gradeability) at the maximum technically permissible mass declared by the manufacturer | : |  |  |  |
| 2.5 | Maximum towable weight (where applicable) | : |  |  |
| 2.6 | Maximum weight of the combination. | : |  |  |
| 3.0 | Engine(10) |
| 3.1 | Manufacturer | : |  |
| 3.1.1 | Make | : |  |
| 3.1.2 | Type (stated on the engine. or other means of identification): | : |  |
| 3.1.3 | Location of engine number (if applicable): | : |  |  |  |

Table 1 AIS-007 (Revision 5)

| 3.2 | Spark- or compression-ignition engine |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 3.2.1 | Specific characteristics of the engine |  |  |  |
| 3.2.1.1 | Operating cycle (four or two-stroke. spark or compression ignition) | : |  |  |
| 3.2.1.2 | Number. arrangement and firing order of cylinders | : |  |  |
| 3.2.1.2.1 | Bore: mm(6) | : |  |  |  |
| 3.2.1.2.2 | Stroke: mm(6) | : |  |  |  |
| 3.2.1.3 | Cylinder capacity(7): cm3 | : |  |  |  |
| 3.2.1.4 | Compression ratio | : |  |  |  |
| 3.2.1.5 | Drawings of cylinder head. piston(s). piston rings and cylinder(s) | : |  |  |  |
| 3.2.1.6 | Idling speed , min-1 (specify tolerance) | : |  |  |  |
| 3.2.1.7 | Maximum net power output: kW at min-1 (specify standard and tolerance) | : |  |  |  |
| 3.2.1.8 | Net maximum torque: Nm at min-1 (specify standard) | : |  |  |  |
| 3.2.1.9 | In case of compression ignition engines, the max power and max torque shall also be specified as per conditions given in MST/CMVR/TAP 115/116 | : |  |
| 3.2.2 | Fuel: diesel/petrol/mixture/LPG/other (1) | : |  |
| 3.2.3 | Fuel tank |  |  |  |  |
| 3.2.3.1 | Capacity (Nominal in liters) | : |  |  |  |
| 3.2.3.2 | Material used (Metallic/Nonmetallic) | : |  |
| 3.2.3.3 | Diagram clearly indicating the position of the tank on the vehicle | : |  |  |  |
| 3.2.3.4 | Type Approval number or BIS license no of the fuel tank fitted | : |  |  |  |

Table 1 AIS-007 (Revision 5)

| 3.2.4 | Fuel supply |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 3.2.4.1 | Via carburettor(s): yes/no | : |  |  |  |
| 3.2.4.1.1 | Make(s): | : |  |  |
| 3.2.4.1.2 | Type(s) and Identification mark: | : |  |  |  |
| 3.2.4.1.3 | Number fitted | : |  |
| 3.2.4.1.4 | Settings | : |  |  |
| 3.2.4.1.4.1 | Jets (indicate venture dia, main jet, pilot jet) | : |  |  |  |
| 3.2.4.1.4.2 | Maximum Level in float chamber | : |  |  |
| 3.2.4.1.4.3 | Mass of float | : |  |  |
|  | OR | : |  |  |
| 3.2.4.1.4.4 | Fuel curve as a function of the air flow and setting required in order to maintain that curve | : |  |  |
| 3.2.4.1.5 | Cold-starting system: manual/automatic | : |  |
| 3.2.4.1.5.1 | Operating principle(s): | : |  |  |
| 3.2.4.2 | By fuel injection : yes/no (For CI engines) | : |  |  |
| 3.2.4.2.1 | Description of system | : |  |  |
| 3.2.4.2.2 | Operating principle: direct/indirect/turbulence chamber injection | : |  |  |
| 3.2.4.2.3 | Injection pump | : |  |  |
|  | Either | : |  |  |
| 3.2.4.2.3.1 | Make(s): | : |  |  |
| 3.2.4.2.3.2 | Type(s): | : |  |  |
|  | or | : |  |  |
| 3.2.4.2.3.3 | Maximum fuel flow rate, mm3 per stroke or cycle(1) at a pump rotational speed of: min–l or characteristic diagram | : |  |  |
| 3.2.4.2.3.4 | Injection advance | : |  |  |
| 3.2.4.2.3.5 | Injection advance curve | : |  |  |
| 3.2.4.2.3.6 | Calibration procedure: test bench/engine | : |  |  |

| Table 1 AIS-007 (Revision 5) |
| --- |
| 3.2.4.2.4 | Regulator |  |  |  |
| 3.2.4.2.4.1 | Type | : |  |  |
| 3.2.4.2.4.2 | Cut-off point |  |  |  |
| 3.2.4.2.4.2.1 | Cut-off point under load: min- | : |  |  |
| 3.2.4.2.4.2.2 | Cut-off point under no load: min-1 | : |  |  |
| 3.2.4.2.4.3 | Idling speed: min-1 | : |  |  |  |
| 3.2.4.2.5 | Injection pipe work |  |  |  |
| 3.2.4.2.5.1 | Length: mm | : |  |  |
| 3.2.4.2.5.2 | Internal diameter: mm | : |  |  |
| 3.2.4.2.6 | Injector(s) |  |  |  |
|  | either | : |  |  |
| 3.2.4.2.6.1 | Make: | : |  |  |
| 3.2.4.2.6.2 | Type: | : |  |  |
|  | or | : |  |  |
| 3.2.4.2.6.3 | Description of system | : |  |  |
| 3.2.4.3 | By fuel injection (solely in the case of spark-ignition): yes/no | : |  |  |
|  | either: | : |  |  |
| 3.2.4.3.1 | Description of system | : |  |  |
| 3.2.4.3.2 | Operating principle: injection into induction manifold (single/multiple point) (1) /direct injection/other (state which) |  |  |  |
|  | or | : |  |  |
| 3.2.4.3.2.1 | Make(s) of the injection pump | : |  |  |
| 3.2.4.3.2.2 | Type(s) of the injection pump | : |  |  |
| 3.2.4.3.3 | Injectors: opening pressure (state tolerance) kPa | : |  |  |
|  | or characteristic diagram (state tolerance) | : |  |  |
| 3.2.4.3.4 | Injection advance | : |  |  |

Table 1 AIS-007 (Revision 5)

| 3.2.4.3.5 | Cold-starting system |  |  |  |
| --- | --- | --- | --- | --- |
| 3.2.4.3.5.1 | Operating principle(s): | : |  |  |
| 3.2.4.3.5.2. | Operating/setting limits (1) (state tolerance) | : |  |  |
| 3.2.4.4. | Fuel pump: yes/no(1) | : |  |  |
| 3.2.5. | Electrical equipment |  |  |  |
| 3.2.5.1. | Nominal voltage: ........ V, positive/negative earth(1) | : |  |  |
| 3.2.5.2. | Generator | : |  |  |
| 3.2.5.2.1. | Type | : |  |  |
| 3.2.5.2.2. | Nominal power: ........ W | : |  |  |
| 3.2.6. | Ignition | : |  |  |
| 3.2.6.1. | Make(s) | : |  |  |
| 3.2.6.2. | Type(s) | : |  |  |
| 3.2.6.3. | Operating principle | : |  |  |
| 3.2.6.4. | Ignition advance curve or operating set point (state tolerance) | : |  |  |
| 3.2.6.5. | Static timing (state tolerance): ........ before TDC | : |  |  |
| 3.2.6.6. | Points gap (state tolerance): ....... mm | : |  |  |
| 3.2.6.7. | Dwell angle (state tolerance) : ....... degrees | : |  |  |
| 3.2.6.8 | Spark plug | : |  |  |
| 3.2.6.8.1 | Make | : |  |  |
| 3.2.6.8.2 | Type and designation | : |  |  |
| 3.2.6.8.3 | Number of Spark Plug in each cylinder | : |  |  |
| 3.2.6.8.4 | Spark-gap setting | : |  |  |
| 3.2.6.8.5 | Nominal resistance (kilo ohm) (if resistive type) | : |  |  |
| 3.2.6.9 | Anti-radio interference system |  |  |  |
| 3.2.6.9.1. | Terminology and drawing of anti-radio interference equipment | : |  |  |
| 3.2.6.9.2. | Indication of the nominal DC resistance value and, in the case of resistive ignition leads, statement of nominal resistance per meter | : |  |  |

Table 1 AIS-007 (Revision 5)

| 3.2.6.10 | Ignition coil(if resistive) |  |  |  |
| --- | --- | --- | --- | --- |
| 3.2.6.10.1 | Make |  |  |  |
| 3.2.6.10.2 | Type |  |  |  |
| 3.2.6.10.3 | Type/Part no./Identification number(ID)/Drawing No. | : |  |  |
| 3.2.6.11 | Ignition condenser(If fitted) | : |  |  |
| 3.2.6.11.1 | Make | : |  |  |
| 3.2.6.11.2 | Type | : |  |  |
| 3.2.6.11.3 | Type/Part no./Identification number(ID)/Drawing No. | : |  |  |
| 3.2.6.12 | HT cable(if resistive) | : |  |  |
| 3.2.6.12.1 | Type/Part no./Identification number(ID)/Drawing No. | : |  |  |
| 3.2.6.12.2 | Nominal resistance per unit length | : |  |  |
| 3.2.6.12.3 | Nominal length with tolerance | : |  |  |
| 3.2.6.13 | Alternator/ Generator | : |  |  |
| 3.2.6.13.1 | Identification number(ID), if resistive type | : |  |  |
| 3.2.7. | Cooling system (liquid/air)(1) | : |  |  |
| 3.2.7.1. | Nominal setting for the engine-temperature control device | : |  |  |
| 3.2.7.2 | Cooling system temperatures permitted by the manufacturer |  |  |  |
| 3.2.7.3. | Liquid |  |  |  |
| 3.2.7.3.1. | Nature of liquid | : |  |  |
| 3.2.7.3.2. | Circulating pump(s): yes/no(1) | : |  |  |
| 3.2.7.3.3 | Maximum temperature at outlet: .... °C |  |  |  |
| 3.2.7.4. | Air |  |  |  |
| 3.2.7.4.1. | Blower: yes/no (1) | : |  |  |
| 3.2.7.4.2 | Reference point | : |  |  |
| 3.2.7.4.3 | Maximum temperature at reference point: …...°C | : |  |  |
| 3.2.7.4.4 | Max. Exhaust temperature ( Except Engine <200 cc) | : |  |  |
| 3.2.7.5 | Cooling Fan (if provided) | : |  |  |
| 3.2.7.5.1 | No of blades | : |  |  |
| 3.2.7.5.2 | Diameter of fan | : |  |  |

Table 1 AIS-007 (Revision 5)

| 3.2.7.5.3 | RPM of fan | : |  |  |
| --- | --- | --- | --- | --- |
| 3.2.7.5.4 | Material of fan | : |  |  |
| 3.2.8. | Induction system |  |  |  |
| 3.2.8.1. | Supercharging: yes/no(1) | : |  |  |
| 3.2.8.1.1. | Make(s) | : |  |  |
| 3.2.8.1.2. | Type(s) | : |  |  |
| 3.2.8.1.3. | Description of system [example: maximum boost pressure …..... kPa, waste gate (where appropriate)] | : |  |  |
| 3.2.8.2. | Intercooler: with/without(1) | : |  |  |
| 3.2.8.3. | Description and drawings of induction pipe work and accessories (plenum chamber, heating device, additional air intakes, etc.): | : |  |  |
| 3.2.8.3.1. | Description of induction manifold (with drawings and/or photos): | : |  |  |
| 3.2.8.3.2. | Air filter, | : |  |  |
| 3.2.8.3.2.1. | Make | : |  |  |
| 3.2.8.3.2.2. | Type | : |  |  |
| 3.2.8.3.2.3 | Part no./Identification number(ID)/Drawing No. | : |  |  |
| 3.2.8.3.2.4 | Schematic dimensional drawing | : |  |  |
| 3.2.8.3.3. | Inlet silencer, drawings | : |  |  |
|  | or | : |  |  |
| 3.2.8.3.3.1. | Make(s) | : |  |  |
| 3.2.8.3.3.2. | Type(s) | : |  |  |
| 3.2.9. | Exhaust system |  |  |  |
| 3.2.9.1. | Drawing of complete exhaust system with identification (if proprietary) or part no (if non-proprietary) | : |  |  |
| 3.2.9.2 | Silencer (if proprietary) | : |  |  |
| 3.2.9.2.1 | Make | : |  |  |
| 3.2.9.2.2 | Type | : |  |  |
| 3.2.9.2.3 | Number | : |  |  |
| 3.2.9.2.4 | Part no./Identification number (ID)/Drawing No. |  |  |  |

Table 1 AIS-007 (Revision 5)

| 3.2.10. | Minimum cross-section of the inlet and exhaust ports | : |  |  |
| --- | --- | --- | --- | --- |
| 3.2.11. | Induction system or equivalent data |  |  |  |
| 3.2.11.1. | Maximum valve lift, opening and closing angles in relation to the dead centers, or data concerning the settings of other possible systems | : |  |  |
| 3.2.11.2. | Reference and/or setting ranges(1) | : |  |  |
| 3.2.12. | Anti-air pollution measures adopted |  |  |  |
| 3.2.12.1. | Crankcase-gas recycling device, solely in the case of four-stroke engines description and drawings): | : |  |  |
| 3.2.12.2. | Additional anti-pollution devices, if any (where present and not included under another heading) | : |  |  |
| 3.2.12.2.1. | Catalytic converter make and identification | : |  |  |
| 3.2.12.2.1.1 | Type | : |  |  |
| 3.2.12.2.1.2 | Number of catalytic converters and elements | : |  |  |
| 3.2.12.2.1.3 | Dimensions, shape and volume of the catalytic converter(s) | : |  |  |
| 3.2.12.2.1.4 | Substrate(structure and material ) | : |  |  |
| 3.2.12.2.1.5 | Cell density | : |  |  |
| 3.2.12.2.1.6 | Type of casing for the catalytic converter(s) | : |  |  |
| 3.2.12.2.3 | Total charge of precious metal g/vehicle. | : |  |  |
| 3.2.12.2.4 | Relative concentration (%) of Pt : Rh : Pd | : |  |  |
| 3.2.12.2.5 | Diagram indicating the arrangement and position of catalyst w.r.t. exhaust manifold. | : |  |  |
| 3.2.13 | Secondary Air Injection (yes/no) (1) | : |  |  |
| 3.2.13.1 | Make and identification | : |  |  |

Table 1 AIS-007 (Revision 5)

| 3.2.14 | Fuel temperature 0C: (for diesel engines at the injection pump inlet) | : |  |  |
| --- | --- | --- | --- | --- |
| 3.2.14.1 | Minimum | : |  |  |
| 3.2.14.2 | Maximum | : |  |  |
| 3.2.15 | Lubricant Temperature 0C (Location of measurement be specified ) | : |  |  |
| 3.2.15.1 | Minimum | : |  |  |
| 3.2.15.2 | Maximum | : |  |  |
| 3.3. | Electric traction motor (yes / no) | : |  |  |
| 3.4. | Lubrication system |  |  |  |
| 3.4.1. | Description of system | : |  |  |
| 3.4.1.1 | Location of oil reservoir (if any) | : |  |  |
| 3.4.1.2 | Feed system (pump/injection into induction system/mixed with the fuel, etc.)(1) | : |  |  |
| 3.4.1.3 | Lubrication oil grade | : |  |  |
| 3.4.2. | Lubricant mixed with the fuel | : |  |  |
| 3.4.2.1. | Percentage | : |  |  |
| 3.4.3. | Oil cooler: yes/no(1) | : |  |  |
| 3.4.3.1. | Drawing(s): | : |  |  |
|  | Or | : |  |  |
| 3.4.3.1.1. | Make(s) | : |  |  |
| 3.4.3.1.2. | Type(s): | : |  |  |
| 3.5 | Electronic Control Unit (ECU) | : |  |  |
| 3.5.1 | Make | : |  |  |
| 3.5.2 | Type/Part no./Identification number(ID)/Drawing No. | : |  |  |
| 3.5.3 | Calibration Identification number(ID) (If applicable) | : |  |  |
| 3.5.4 | Adjustment possibilities ,( Yes / No ) | : |  |  |
| 3.6 | Exhaust Gas Re-circulating System | : |  |  |
| 3.6.1 | Brief description of the system | : |  |  |
| 3.6.2 | Type ( Cooled / Non-cooled/ Progressive/ On-Off/ Any Other ) | : |  |  |

Table 1 AIS-007 (Revision 5)

| 3.6.3 | EGR Valve | : |  |  |
| --- | --- | --- | --- | --- |
| 3.6.3.1 | Make | : |  |  |
| 3.6.3.2 | Type | : |  |  |
| 3.6.3.3 | Type/Part no./Identification number(ID)/Drawing No. | : |  |  |
| 3.7 | Canister | : |  |  |
| 3.7.1 | Working capacity | : |  |  |
| 3.7.2 | Make | : |  |  |
| 3.7.3 | Identification number(ID) / Part No./Drawing No | : |  |  |
| 3.7.4 | Schematic diagram | : |  |  |
| 3.7.5 | Canister bed volume (1) | : |  |  |
| 3.8 | Lambda Sensor (If provided) | : |  |  |
| 3.8.1 | Make | : |  |  |
| 3.8.2 | Identification number(ID) / Part No./Drawing No. | : |  |  |
| 3.8.3 | Location | : |  |  |
| 4.0 | Transmission(8) |
| 4.1. | Diagram of transmission system | : |  |  |
| 4.2. | Type (mechanical, hydraulic, electrical, etc.) (1): | : |  |  |
| 4.3. | Clutch (type) | : |  |  |
| 4.4. | Gearbox |  |  |  |
| 4.4.1. | Type: automatic/manual(1) | : |  |  |
| 4.4.2. | Method of selection: by hand/foot(1) | : |  |  |
| 4.4.2.1 | Gear shifting pattern | : |  |  |
| 4.4.3. | Gear ratios |  |  |  |
| 4.4.3.1 | Primary ratio | : |  |  |
| 4.4.3.2 | Secondary ratio | : |  |  |
| 4.4.3.3 | Individual and Overall ratios |  |  |  |
| 4.4.3.3.1 | First gear | : |  |  |
| 4.4.3.3.2 | Second gear | : |  |  |
| 4.4.3.3.3 | Third gear | : |  |  |
| 4.4.3.3.4 | Fourth gear | : |  |  |
| 4.4.3.3.5 | Fifth gear | : |  |  |

Table 1 AIS-007 (Revision 5)

| 4.4.3.3.6 | Sixth gear | : |  |  |
| --- | --- | --- | --- | --- |
| 4.4.3.4 | Minimum continuously Variable transmission | : |  |  |
| 4.4.3.5 | Maximum continuously Variable transmission | : |  |  |
| 4.4.3.6 | Reverse Gear | : |  |  |
| 4.5. | Brief description of the ECUs used in the transmission | : |  |  |
| 4.6. | Maximum speed of vehicle and gear in which it is reached (in km/h)(9) | : |  |  |
| 4.7. | Speedometer |  |  |  |
| 4.7.1 | Make(s) | : |  |  |
| 4.7.2. | Type(s) | : |  |  |
| 4.7.3. | Photographs and/or drawings of the complete system | : |  |  |
| 4.7.4. | Speed range displayed | : |  |  |
| 4.7.5. | Tolerance of the measuring mechanism of the speedometer | : |  |  |
| 4.7.6. | Technical constant of the speedometer | : |  |  |
| 4.7.7. | Method of operation and description of the drive mechanism | : |  |  |
| 4.7.8. | Overall transmission ratio of the drive mechanism or pulse / wheel revolution (in case of digital speedometer) | : |  |  |
| 5.0 | Suspension |
| 5.1 | Drawing of suspension arrangement | : |  |  |
| 5.1.1. | Brief description of the ECUs used in the suspension | : |  |  |
| 5.1.2 | Springs front and rear | : |  |  |
| 5.1.3 | Anti-roll bar | : |  |  |
| 5.1.4 | Shock Absorbers front and rear | : |  |  |

Table 1 AIS-007 (Revision 5)

| 5.2. | Tyres (standard type): (Enclose annexure, if required) |  |  |  |
| --- | --- | --- | --- | --- |
| Tyre Variant / version Type Size designation with speed category symbol and load capacity index Make (s) Type Approval Number or BIS license number or identification Dynamic Rolling Radius Front Rear Any other |
| 5.2.1 | Tyre pressures recommended by the manufacturer: | : |  |  |
| 5.2.1.1 | Laden ( kg/cm2 / kPa) | : |  |  |
| 5.2.1.2 | Unladen (with driver) ( kg/cm2 / kPa) | : |  |  |
| 5.2.2 | Tyre/wheel (rim) combinations | : |  |  |
| 5.2. 3 | Minimum-speed category symbol compatible with the theoretical maximum design speed of the vehicle | : |  |  |
| 5.2.4 | Minimum load-capacity index with the maximum load on each tyre: | : |  |  |
| 5.2.5 | Categories of use compatible for the vehicle | : |  |  |
| 5.3 | Wheel rims |  |  |  |
| 5.3.1 | Designation (front and rear) | : |  |  |
| 5.3.2 | Type (Alloy / Sheet metal / spoke) | : |  |  |
| 5.3.3 | Maximum design loading capacity | : |  |  |
| 6.0 | Steering |
| 6.1 | Steering gear and control | : |  |  |
| 6.1.1 | Type of steering control(handle bar/wheel) |  |  |  |
| 6.1.2 | Location of Steering Wheel ( centre / offset ) |  |  |  |
| 6.1.3 | Type of gear | : |  |  |
| 6.1.4 | Brief description of the ECUs used in the steering system | : |  |  |

Table 1 AIS-007 (Revision 5)

| 7.0 | Braking |
| --- | --- |
| 7.1 | Diagram of braking devices | : |  |  |
| 7.2 | Front and rear brakes, disc and/or drum (1) and their numbers | : |  |  |
| 7.2.1. | Make(s) | : |  |  |
| 7.2.2. | Type(s) ( Hydraulic / Mechanical / Other) | : |  |  |
| 7.3 | Drawing of parts of the brake system | : |  |  |
| 7.3.1 | Shoes and/or pads (1) | : |  |  |
| 7.3.2 | Linings and/or pads (Indicate make, grade of material or identification mark) (1) | : |  |  |
| 7.3.3 | Brake levers and/or pedals(1) | : |  |  |
| 7.3.4 | Hydraulic reservoirs (where applicable) | : |  |  |
| 7.3.5 | Front and rear pad/liner dimensions | : |  |  |
| 7.3.6 | Front and rear braking area | : |  |  |
| 7.3.7 | Diameter of front and rear disc or drum | : |  |  |
| 7.3.8 | ABS (Yes/No) | : |  |  |
| 7.3.8.1 | Directly controlled wheels (Front or rear) | : |  |  |
| 7.3.8.2 | Sensors (Make )(front /Rear) | : |  |  |
| 7.3.8.2.1 | Identification number(ID) / Part No./Drawing No. | : |  |  |
| 7.3.8.3 | Make of modulator(front /rear) | : |  |  |
| 7.3.8.3.1 | Identification number(ID) / Part No./Drawing No. | : |  |  |
| 7.3.8.4 | Make of ABS ECU | : |  |  |
| 7.3.8.4.1 | Make of controller | : |  |  |
| 7.3.8.5 | Identification number(ID) / Part No./Drawing No. | : |  |  |
| 7.4 | Other devices (parking brake, etc.) (where applicable): drawing and description | : |  |  |
| 7.5 | Brief description of the ECUs used in the braking system | : |  |  |
| 7.6 | Brake hose – make(s) and Type Approval Number or BIS license number or identification: | : |  |
| 7.7 | Brake fluid – make(s) | : |  |  |
| 7.8 | Control cables (in case of 2 wheelers below 50cc) |  |  |  |
| 7.8.1 | Make |  |  |  |
| 7.8.2 | Cable Diameter |  |  |  |
| 8.0 | Lighting and light-signaling devices |
| 8.1 | List of all devices (Enclose annexure, if required) | : |  |  |
| Device Variant / Version Number make Type Approval Number Lens Colour Tell-tale Colour Head Lamp High beam Head Lamp dipped beam Front position light Tail / stop light Number plate illumination light Direction indicator lights, front and rear Parking lights Reversing light(s) Reflex reflector rear Reflex reflector side(if provided) Hazard warning lamp (wherever applicable) |
| 8.1.1 | Maximum intensity of Head lamp | : |  |  |
| 8.2 | Diagram showing the location of the lighting and light-signaling devices on vehicle with relevant dimensions (see AIS-009) | : |  |  |
| 8.3 | Additional requirements relating to special vehicles | : |  |  |
| 8.4 | Brief description of the ECUs used in the lighting system and in the light-signaling system | : |  |

Table 1 AIS-007 (Revision 5)

| 8.5 | List of all bulbs (Enclose annexure, if required.) |  |  |  |
| --- | --- | --- | --- | --- |
| Bulb used for Variant / Version number make Type Approval Number colour Designation as per AIS-034 Head lamp high beam / low beam Front position light Tail / stop light Number plate illumination light Direction indicator lights Parking light Reversing light (s) Hazard warning lamp |
| 9.0 | Equipment |
| 9.1 | Coupling devices (where applicable) |  |  |  |
| 9.1.1 | Type: hook/ring/other(1) | : |  |  |
| 9.1.2 | Photograph and/or drawings showing the position and the construction of the coupling devices | : |  |  |
| 9.2 | Arrangement and identification of controls, tell-tales and indicators (as per AIS-071as applicable) |  |  |  |
| 9.2.1 | Photographs and/or drawings of the arrangement of the symbols, controls, tell-tales and indicators | : |  |  |
| 9.3 | Statutory inscriptions |  |  |  |
| 9.3.1 | Photographs and/or drawings showing the location of VIN. | : |  |  |
| 9.3.2 | Height of VIN characters. | : |  |  |
| 9.4 | Device(s) to protect against unauthorized use |  |  |  |
| 9.4.1 | Type of device(s) as per AIS-074 | : |  |  |
| 9.4.1.1 | Make(s) |  |  |  |

Table 1 AIS-007 (Revision 5)

| 9.4.2 | Summary description of device(s) used | : |  |  |
| --- | --- | --- | --- | --- |
| 9.5 | Audible warning device(s) | : |  |  |
| 9.5.1 | Summary description of device(s) used such as horn and their purpose | : |  |  |
| 9.5.2 | Make(s) | : |  |  |
| 9.5.3 | Type(s) | : |  |  |
| 9.5.3.1 | Operating voltage | : |  |  |
| 9.5.3.2 | Nos of audible warning devices installed | : |  |  |
| 9.5.4 | TAC No. / BIS license number/ "E" marking | : |  |  |
| 9.5.5 | Drawing(s) showing the location of the audible warning device(s) in relation to the structure of the vehicle | : |  |  |
| 9.5.6 | Dimensional & material Details of the part in front of the Horn(s) which may obstruct audibility | : |  |  |
| 10.0 | Rear-view mirrors (please provide the following information for each rear-view mirror) |  |  |  |
| 10.1 | Make (s) | : |  |  |  |
| 10.1.1 | Type Approval Number / E- marking / BIS License No. |  |  |  |  |
| 10.2 | Class of the Mirror as per AIS-002 | : |  |  |
| 10.3 | Drawing(s) showing the location & Installation Dimension Details of the rear-view mirror(s) in relation to the structure of the vehicle | : |  |  |
| 10.4 | Precise information concerning the type of attachment, including that part of the vehicle structure to which the rear-view mirror is attached | : |  |  |
| 11.0 | Provision for Devices for pillion rider and/or passenger(s) |  |  |  |
| 11.1 | Nos of Handholds for pillion Rider in case of 2 Wheeler | : |  |  |
| 11.1.1 | Type: strap and/or handle(1) | : |  |  |

Table 1 AIS-007 (Revision 5)

| 11.1.2 | Drawings showing dimensional and material details of strap / handhold(s) and its fixing / bolting details | : |  |  |
| --- | --- | --- | --- | --- |
| 11.1.3 | Nos. of Handholds for passenger(s) in case of 3 Wheeler |  |  |  |
| 11.2 | Foot rest for rider and pillion | : |  |  |
| 11.3 | Protective device covering half of the rear wheel.(as applicable) along with Schematic drawing. | : |  |  |
| 12.0 | Spray suppression device (as applicable) | : |  |  |
| 12.1 | Diagram showing general arrangement of spray suppression system, Angle θ and relevant dimensions as specified in AIS-103 :2009 |  |  |  |
| 12.2 | Tyre Overall Width (Maximum of variants and tyre makes) |  |  |  |
| 13.0 | List of Electrical/Electronic Systems which are not previously listed |  |  |  |
| 13.1 | List of all subassemblies, which includes an electronic oscillator or switching frequency greater than 9kHz (like ECU, instrument Cluster, Body Control Module etc.) |  |  |  |
| 13.1.1 | Device Name |  |  |  |
| 13.1.2 | Make |  |  |  |
| 13.1.3 | Identification number(ID) / Part No./Drawing No. |  |  |  |
| 13.2 | List of all Electrical components, which include Broadband EMI sources (like HAVC Motor, Wiper Motor and Horn etc.) |  |  |  |
| 13.2.1 | Device Name |  |  |  |
| 13.2.2 | Make |  |  |  |
| 13.2.3 | Identification number(ID) / Part No./Drawing No. |  |  |  |
| 14.0 | Any other features manufacturer desires to declare |  |  |  |

Table 1 AIS-007 (Revision 5)

|  | INFORMATION RELATING SOLELY TO L5 CATEGORY VEHICLES |
| --- | --- |
| 1.0 | Dimensions and weights (in mm and kg) (where necessary, refer to drawings) |
| 1.1. | Dimensions to be complied with when building un-bodied chassis | : |  |  |
| 1.1.1. | Length | : |  |  |
| 1.1.2. | Width | : |  |  |
| 1.1.3. | Unladen height | : |  |  |
| 1.1.4. | Front overhang | : |  |  |
| 1.1.5. | Rear overhang | : |  |  |
| 1.2. | Weights |  |  |  |
| 1.2.1. | Maximum payload declared by manufacturer | : |  |  |
| 2.0 | Equipment |
| 2.1 | Windscreen and other glazing | : |  |  |
| 2.1.1. | Windscreen | : |  |  |
| 2.1.1.1 | Make and Materials used | : |  |  |
| 2.1.1.2 | Type Approval Number/E-marking / BIS license number: | : |  |  |
| 2.1.2 | Other glazing | : |  |  |
| 2.1.2.1 | Make and Materials used | : |  |  |
| 2.1.2.2 | Type Approval Number/E-marking / BIS license number: | : |  |  |
| 2.2 | Windscreen wiper(s) | : |  |  |
| 2.2.1 | Detailed technical description : Layout including location of "R" Point, "H' Point and related dimensions of wiping area and related dimensions of wiper arm(s) and co-ordinates of mounting (see AIS-045) | : |  |  |
| 2.3 | Seats | : |  |  |
| 2.3.1 | Number | : |  |  |
| 2.3.2 | Location | : |  |  |
| 2.3.3 | Coordinates or drawing of the R point declared by manufacturer | : |  |  |
| 2.3.3.1 | Driving seat | : |  |  |

Table 1 AIS-007 (Revision 5)

| 2.3.4 | Intended seat-back inclination | : |  |  |
| --- | --- | --- | --- | --- |
| 2.3.4.1 | Driving seat | : |  |  |

Footnotes: -

- State as appropriate

# Where a device has been component type-approved, the description may be replaced by a reference to that component type-approval. Likewise, no description is needed where a component's structure is clear from the diagrams or drawings attached to the certificate. State the numbers of the corresponding Annexes for each heading where photographs and drawings must be attached.

# Where used, means of identification may appear only on vehicles, separate technical units or components falling within the scope of the AIS / IS governing components type-approval.

# Classification in accordance with AIS-053.

# Maximum payload declared by the manufacturer: - load obtained by subtracting the weight defined in 2.2, from the mass defined in 2.3.

# The mass of the rider is taken to be a round figure of 75 kg.

# This figure should be to the nearest tenth of a millimeter.

# This value should be calculated with pi = 3,1416 to the nearest cm3

# The information requested should be supplied for a possible variant.

# A tolerance of 5 % is permitted provided that the limit values pursuant to AIS-017 are not exceeded.

# Where unconventional engines and systems are fitted, information equivalent to that referred under this heading must be supplied by their manufacturer.

# In case of CNG / LPG vehicles the additional details in Table 21 format shall be applicable. In case BOV, additional details as per table 13 shall be applicable.

| Table 2 of AIS-007 (Revision 5) TECHNICAL SPECIFICATION – M & N CATEGORY OF VEHICLES (FOUR WHEELERS AND ABOVE) PART A – GENERAL |
| --- |
| Clause No. | Description |
| A1.0 | Details of Vehicle manufacturer : |
| A1.1 | Name & address of the manufacturer |
| A1.2 | Telephone No |
| A1.3 | Fax No. |
| A1.4 | E-mail address |
| A1.5 | Contact Person |
| A1.6 | Name of model and variants (Features differentiating the model and its variants to be given in a separate table) |
| A1.7 | Plant/(s) of manufacture |
| A1.7.1 | Name and address of vehicle manufacturing plant |
| A1.7.2 | Name and address of engine manufacturing plant In case of imported vehicles, above details shall be supplied for importer also. |
| A1.8 | Importer’s Name and address |
| A1.8.1 | Telephone No. |
| A1.8.2 | Fax. No. |
| A1.8.3 | E mail address |
| A1.8.4 | Contact person |
| A2.0 | Vehicle type: |
| A2.1 | Type of vehicle (Rigid / articulated / Tractor- Trailer combination / others |
| A2.1.1 | Usage (goods / passenger / others) |
| A2.1.2 | Control (Forward / semi-forward / normal / others) |
| A2.1.3 | Drive (4x2 or 4x4 or 6x2 or 6x4 or others) |
| A2.1.4 | Cab type (Fully built cab (Tiltable / Non-Tiltable) / sleeper cab / Front end structure / Cowl with wind shield / Cowl without wind shield) |
| A2.1.5 | Load body (fitted / not fitted) |
| A2.2 | Category of vehicle as per AIS-053 |
| A3.0 | Vehicle Performance: |
| A3.1 | Max. recommended gradeability (Stand-start) – in degrees |
| A3.2 | Max. design speed (km/h) |

| Table 3 of AIS-007 (Revision 5) TECHNICAL SPECIFICATION – FOUR WHEELERS AND ABOVE PART B – VEHICLE OVERALL |
| --- |
| Clause No. | Description |
| B1.0 | Vehicle Dimensions : |
| B1.1 | Length mm |
| B1.1.1 | Total length (mm) (for articulated/combination vehicles) |
| B1.2 | Width mm |
| B1.3 | Height (Unladen) (mm) |
| B1.4 | Wheel base (mm) |
| B1.4.1 | Axle spacing in case of multi axle vehicles. |
| B1.5 | Wheel track (mm) |
| B1.5.1 | Front |
| B1.5.2 | Rear |
| B1.5.3 | Other axles (for articulated/combination vehicles) |
| B1.6 | Body overhang (mm) |
| B1.6.1 | Front end |
| B1.6.2 | Rear end |
| B1.7 | Frame overhang mm (in case of vehicles without complete body) |
| B1.7.1 | Front end |
| B1.7.2 | Rear end |
| B1.8 | Inner dimensions of room or platform (For goods carriage vehicles only) |
| B1.8.1 | Length |
| B1.8.2 | Width |
| B1.8.3 | Height |
| B1.9 | Lateral projection |
| B2.0 | Weights : |
| B2.1 | Vehicle kerb weight kg |
| B2.1.1 | Front axle 1 |
| B2.1.2 | Front axle 2 |
| B2.1.3 | Rear axle |
| B2.1.4 | Trailer axle (applicable for articulated/combination vehicles) |
| B2.1.5 | Total |
| B2.2 | Gross vehicle weight kg ( for rigid vehicles ) |
| B2.2.1 | Maximum permissible axle weights (kg) |
| B2.2.2 | Front axle |
| B2.2.3 | Rear axle |
| B2.2.4 | Other axle |

Table 3 of AIS-007 (Revision 5)

| B2.3 | Gross combination weight kg (applicable for articulated / Tractor Trailer combination vehicles) |
| --- | --- |
| B2.3.1 | Front axle |
| B2.3.2 | Rear axle |
| B2.3.3 | Trailer axle / other axles |
| B2.4 | Reference mass (for vehicles with GVW less than or equal to 3.5 ton) (kg.) |
| B2.5 | Seating capacity |
| B2.5.1 | Maximum (Including driver) for completely built vehicles |
| B3.0 | Tyres : |
| B3.1 | Make |
| B3.2 | No. and arrangement of wheels |
| B3.2.1 | Front |
| B3.2.2 | Rear |
| B3.2.3 | Spare wheel |
| B3.2.4 | Others (for articulated/combination vehicles) |
| B3.3 | Tyre type (Radial/cross ply) (with Tube / Tube less), size designation including ply rating, speed rating, Load rating or Load index. Use symbols as per IS 15633 / IS 15636 as may be applicable. |
| B3.3.1 | Front wheel |
| B3.3.2 | Rear wheel |
| B3.3.3 | Spare wheel (Other than temporary use spare wheel) |
| B3.3.4 | Other (for articulated/combination vehicles) |
| B3.4 | Dynamic rolling radius, mm, as per IS 15633 / IS 15636 |
| B3.5 | Inflation pressure – Unladen (kg/cm2 / kPa) |
| B3.5.1 | Front |
| B3.5.2 | Rear |
| B3.5.3 | Other |
| B3.6 | Inflation pressure – Laden (kg/cm2 / kPa) |
| B3.6.1 | Front |
| B3.6.2 | Rear |
| B3.6.3 | Other |
| B3.7 | Tyre Pressure Monitoring System (TPMS) / Run Flat Warning System as applicable for Run-Flat tyres - as per AIS-110 (If Provided) |
| B3.7.1 | Make (If Applicable) |
| B3.7.2 | Brief Description of the system |

Table 3 of AIS-007 (Revision 5)

| B3.8 | Temporary Spare Wheel / RFT- as per AIS-110 (If Provided) |
| --- | --- |
| B3.8.1 | Type as per AIS-110 |
| B3.8.2 | Make |
| B3.8.3 | Size |
| B3.8.4 | Load and speed rating |
| B3.8.5 | Recommended max speed |
| B4.0 | Transmission : |
| B4.1 | Type (Manual/Automatic/semi-automatic) (Note: If automatic give all pertinent data) |
| B4.2 | Clutch Type (wet/Dry/Single plate/ Multi plate / Hydraulic) |
| B4.3 | Gear box |
| B4.3.1 | Type |
| B4.3.2 | Model name (if any) |
| B4.3.3 | Gear shifting control system (Sketch showing gear shifting arrangement) |
| B4.3.4 | No. of gears |
| B4.4 | Stall ratio of torque converter |
| B4.5 | Sub transmission |
| B4.5.1 | Type |
| B4.5.2 | Control system |
| B4.5.3 | Gear ratio High Low |
| B4.6 | Final Drive Front / Rear / Both |
| B4.6.1 | Type |
| B4.6.2 | Reduction ratio |
| B4.6.3 | Differential type |
| B4.6.4 | Final Drive ratio |
| B4.7 | Gear ratio Gear box ratio Overall ratio 1st 2nd 3rd 4th 5th 6th Over drive Reverse |

Table 3 of AIS-007 (Revision 5)

| B4.8 | Hydraulic transmission |
| --- | --- |
| B4.8.1 | Type |
| B5.0 | Number of axles : Steered Non-steered Driven Non-driven |
| B6.0 | Front axle : |
| B6.1 | Type ( Single / Multi / Retractable ) |
| B6.2 | Toe-in / Toe out (mm) |
| B6.3 | Camber angle |
| B6.4 | Caster angle |
| B6.5 | King pin angle |
| B7.0 | Rear axle : |
| B7.1 | Type ( Single / Tandem / Tridem / Multi/ Retractable ) |
| B7.2 | Toe-in/ Toe out mm, if applicable |
| B7.3 | Camber angle, if applicable |
| B7.4 | Caster angle, if applicable |
| B7.5 | King pin angle, if applicable |
| B8.0 | Steering system : |
| B8.1 | Make |
| B8.1.1 | Type (Manual / Power assisted – Hydraulic / Power assisted – Electric / Other) |
| B8.2 | Steering wheel |
| B8.2.1 | Identification Mark / Part No./Drawing No. |
| B8.2.2 | Position (center/offset) |
| B8.2.3 | Outside dia. (mm) |
| B8.2.4 | Steering column |
| B8.2.4.1 | Make |
| B8.2.4.2 | Type / Model |
| B8.2.4.3 | Detailed drawing with material specifications |
| B8.2.5 | Intermediate shaft |
| B8.2.5.1 | Make |
| B8.2.5.2 | Type / Model |
| B8.2.5.3 | Detailed drawing with material specifications |
| B8.3 | Maximum No. of rotation of steering wheel from lock to lock |

Table 3 of AIS-007 (Revision 5)

| B8.4 | Details of single / multiple combinations to be given in the form of an Annexure with reference to IS 11939:1996 |
| --- | --- |
| B8.5 | Detailed drawing of the mounting arrangement of Steering control assembly showing vertical / tilt / actual angle. |
| B8.6 | Offset of the steering column with respect to the seat |
| B8.7 | Steering Gear |
| B8.7.1 | Type of steering gear (Re-circulating ball / Worm & Roller / Rack & Pinion / Others) |
| B8.7.2 | Make |
| B8.7.3 | Steering gear ratio |
| B8.8 | Wheel lock angle (deg.) Inner Outer |
| B8.8.1 | Left |
| B8.8.2 | Right |
| B8.9 | Power Assistance |
| B8.9.1 | Type of assistance |
| B8.9.2 | Make |
| B8.9.3 | Identification No./ Part No. |
| B8.9.4 | Pressure setting (kg/cm2 / bar / kPa) |
| B8.10 | Min turning circle diameter (mm) (as per IS 12222) |
| B8.11 | Min. turning circle clearance diameter (mm) |
| B8.12 | Coordinates of point defining test turning circle. (Applicable in case of vehicles without complete body which does not cover this point) |
| B9.0 | Clearance (Requirement as per AIS-053, If applicable): |
| B9.1 | Minimum road clearance |
| B9.2 | Road clearance from floor (for buses) |
| B9.3 | Approach angle |
| B9.4 | Departure angle |
| B9.5 | Ramp-over angle |
| B9.6 | Minimum Ground Clearance as per IS 9435:2004 |
| B10.0 | Max. stable inclination (For buses as per AIS-031) : |
| B10.1 | Left |
| B10.2 | Right |
| B11.0 | Suspension : |
| B11.1 | Type and description (Leaf / Coil / Air / Semi-pneumatic / Torsion bar) |
| B11.1.1 | Front |
| B11.1.2 | Rear |

Table 3 of AIS-007 (Revision 5)

| B11.2 | Make |
| --- | --- |
| B11.2.1 | Front |
| B11.2.2 | Rear |
| B11.3 | Type of spring |
| B11.4 | If leaf spring |
| B11.4.1 | Main spring |
| B11.4.1.1 | Stack height, at center |
| B11.4.1.2 | Width at the center point / stack point |
| B11.4.1.3 | Flat length |
| B11.4.1.4 | Free camber |
| B11.4.1.5 | No. of leaves Left Right No. of leaves No. of spacers |
| B11.4.2 | Auxiliary Spring |
| B11.4.2.1 | Stack height at, at center |
| B11.4.2.2 | Width at the center point / stack point |
| B11.4.2.3 | Flat length |
| B11.4.2.4 | Free camber |
| B11.4.2.5 | No. of leaves Left Right No. of leaves No. of spacers |
| B12.0 | Suspension- Shock absorber : |
| B12.1 | Type and Number |
| B12.1.1 | Front |
| B12.1.2 | Rear |
| B13.0 | Suspension- Stabilizer : |
| B13.1 | Front |
| B13.2 | Rear |
| B14.0 | Chassis frame : |
| B14.1 | Type |
| B15.0 | Displays and tell tales (Indicate the type and if the tell tales provided and whether they are symbols or letter. (AIS-071 part 1 and 2 or corresponding Indian Standard)) |
| B15.1 | Head lamp – upper / lower control |
| B15.2 | Ignition cut-off |
| B15.3 | Turn signal |

Table 3 of AIS-007 (Revision 5)

| B15.4 | Fuel Gauge |
| --- | --- |
| B15.5 | Engine coolant temperature |
| B15.6 | Engine low oil pressure |
| B15.7 | High beam indicator |
| B15.8 | Electrical charge indicator (Battery charge) |
| B15.9 | Brake failure |
| B15.10 | Front fog light |
| B15.11 | Rear fog light |
| B15.12 | Horn |
| B15.13 | Others (such as ABS failure, Airbag, HVAC, Seat belt, Content gauge, LPG / CNG changeover switch etc.,) |
| B16.0 | Hood latch : |
| B16.1 | Make |
| B16.2 | Type |
| B16.3 | Identification No. / Part No. |
| B17.0 | Wheel guard (IS 13943 for passenger cars) |
| B17.1 | Dimension C |
| B17.2 | Dimension p |
| B17.3 | Dimension q |
| B18.0 | External Projections |
| B18.1 | Ornaments |
| B18.2 | Projection for head light |
| B18.3 | Radiator grills (Applicable of on external surface) |
| B18.3.1 | Gap between individual elements |
| B 18.3.2 | Radius of curvature of individual element |
| B18.4 | Body Panel ( In case of radius of curvature of folds in body panels are less than 2.5mm the scaled drawing of folds contour and H value as per IS 13942 is required to be submitted) |
| B18.5 | Radius of curvature of lateral Rain/Air deflector |
| B19.0 | Speedometer: |
| B19.1 | Type |
| B19.2 | Make, and Identification No. / Part No./ Drawing No. |
| B19.3 | Range |
| B19.4 | Major marking |
| B19.5 | Minor marking |
| B19.6 | Speedometer ratio |
| B19.7 | Ratio of Speedo drive |

Table 3 of AIS-007 (Revision 5)

| B20.0 | Odometer : (only in case of CNG buses) |
| --- | --- |
| B20.1 | Make |
| B20.2 | Type and Identification No. / Part No. |
| B21.0 | Safety belt anchorages – specifications |
| B21.1 | Design of the type of belts and retractors authorized for fit to the anchorages with which vehicle is equipped : |
| B21.2 | Section views of all the seat belt anchorages. Anchorage Position Anchorage on (*) Vehicle Structure Seat Structure Front Right-hand seat Lower anchorage Outboard Inboard Upper anchorage Middle seat Lower anchorage Right Left Lower anchorage Left-hand seat Lower anchorage Outboard Inboard Upper anchorage Rear |
| B21.3 | Reference point on body used for vehicle and seat co-ordinate measurement, X, Y, Z co-ordinates of all the seat belt anchorage points. |
| B21.4 | Weight of seats |
| B21.5 | C.G. of seats (Sketch, showing the C.G. location form reference point or from seat anchorage point). |
| B22.0 | Seats, their anchorages and head restraints |
| B22.1 | Seats, their anchorages and head restraints-specifications for M1 category. |
| B22.1.1 | Description of seats |
| B22.1.1.1 | Make |
| B22.1.1.2 | Number of seats fitted or capable of being fitted with head restraints, adjustable or not adjustable. |
| B22.1.1.3 | Description of the adjustment, displacement and locking systems of the seat or of its parts and a description of occupant protection system against displacement of luggage. |
| B22.1.2 | Description of seat anchorage |
| B22.1.2.1 | Longitudinal position of the seats during the tests. |

Table 3 of AIS-007 (Revision 5)

| B22.1.2.2 | Drawings, diagrams and plans of the seats, their anchorages on the vehicle, the adjustment and displacement system of the seats and their parts, and their locking devices and of additional occupant protection system against displacement of luggage. |
| --- | --- |
| B22.1.2.3 | In the case of seats fitted with head restraints, the head restraint shall be shown on all drawings, diagrams and photographs. |
| B22.1.3 | Seat Drawings showing ‘H point co-ordinates with respect to reference point on body shell |
| B22.1.4 | All designed positions i.e. Slider, Height Adjuster, Manikin settings, Torso Angle etc. |
| B22.1.5 | Seat Identification No. / Part No. |
| B22.2 | Seats, their anchorages and head restrains (for passenger vehicles of categories other than M1 and goods vehicles of category N). |
| B22.2.1 | Make |
| B22.2.2 | Brief description of the seat type, its attachment fittings and its adjustment, displacement and locking systems including the minimum distance between fitting points. |
| B22.2.3 | Position and arrangement of seats including seat layout. |
| B22.2.4 | Seats if any which incorporate a safety belt anchorage. |
| B22.2.5 | Seat Identification No./ Part No. |
| B23.0 | Rear Under run Protective device |
| B23.1 | Height of lower edge of the device from the ground (mm). |
| B23.2 | Width of the device (mm). |
| B23.3 | Drawing of the rear under-run protective device with dimensions. |
| B23.4 | Installation drawing showing rear extremity of vehicle, chassis rear overhang, chassis cross section details etc. |
| B23.5 | Material (Metal / Fibre / etc.) |
| B24.0 | Lateral Protection (Side Guards) |
| B24.1 | Height of the lower edge of the Side Guard. |
| B24.2 | Drawing of the lateral protection device with dimensions. |
| B24.3 | Installation drawing of the lateral protective device with dimensions. |
| B24.4 | Material (Metal / Fiber / etc.) |
| B25.0 | Controls - Specify method of operation, hand operated - left / right, foot operated - left / right Ref. SS 12.1 or corresponding Indian Standard). |
| B25.1 | Ignition |
| B25.2 | Horn |
| B25.3 | Lamps (Head lamp, Tail lamp, Parking lamp and Number plate lamp) |
| B25.4 | Turn signal |
| B25.5 | Transmission shift lever |

Table 3 of AIS-007 (Revision 5)

| B25.6 | Wind shield wiper |
| --- | --- |
| B25.7 | High beam/low beam |
| B25.8 | Parking brake |
| B25.9 | Master switch for electrical |
| B25.10 | Hazard warning signal |
| B25.11 | Service Brake |
| B25.12 | Accelerator Pedal (Floor hinged/hanging type) |
| B25.13 | Others |
| B26.0 | Safety glass |
| B26.1 | Front wind shield (laminated) |
| B26.1.1 | Make |
| B26.1.2 | Identification: TAC No. / BIS License No. / E- Marking |
| B26.1.3 | Type (flat/curved, clear/tinted) |
| B26.1.4 | Thickness (mm) |
| B26.1.5 | No. of pieces |
| B26.1.6 | Radius of curvature (if curved) |
| B26.1.7 | Method of fixing (for approval of Demisting / Defrosting system) |
| B26.2 | Side Windows (Left & Right) |
| B26.2.1 | Make |
| B26.2.2 | Identification: TAC No. / BIS License No. / E- Marking |
| B26.2.3 | Type(flat/curved, clear/tinted, toughened/laminated) |
| B26.2.4 | Thickness mm |
| B26.3 | Rear Window |
| B26.3.1 | Make |
| B26.3.2 | Identification: TAC No. / BIS License No. / E- Marking |
| B26.3.3 | Type(flat/curved, clear/tinted, toughened/laminated) |
| B26.3.4 | Thickness mm |
| B26.3.5 | Radius of curvature (if curved) |
| B27.0 | Rear view mirror : [ As applicable to the category of vehicle ] |
| B27.1 | Interior mirror (Class-I) |
| B27.1.1 | Make |
| B27.1.2 | Identification: TAC No. / BIS License No. / E- Marking |
| B27.1.3 | Area of mirror and radius of curvature of reflecting surface |

Table 3 of AIS-007 (Revision 5)

| B27.2 | Main mirror (Large) (Class-II) |
| --- | --- |
| B27.2.1 | Make |
| B27.2.2 | Identification: TAC No. / BIS License No. / E- Marking |
| B27.2.3 | Area and radius of curvature of the mirror glass reflecting surface |
| B27.3 | Main mirror (Small) (Class-III) |
| B27.3.1 | Make |
| B27.3.2 | Identification: TAC No. / BIS License No. / E- Marking |
| B27.3.3 | Area and radius of curvature of the mirror glass reflecting surface |
| B27.4 | Wide angle mirror (Class-IV) |
| B27.4.1 | Make |
| B27.4.2 | Identification: TAC No. / BIS License No. / E- Marking |
| B27.4.3 | Area and radius of curvature of the mirror glass reflecting surface |
| B27.5 | Close proximity mirror (Class-V) |
| B27.5.1 | Make |
| B27.5.2 | Identification: TAC No. / BIS License No. / E- Marking |
| B27.5.3 | Area and radius of curvature of the mirror glass reflecting surface |
| B27.6 | Front mirror (Class-VI) |
| B27.6.1 | Make |
| B27.6.2 | Identification: TAC No. / BIS License No. / E- Marking |
| B27.6.3 | Area and radius of curvature of the mirror glass reflecting surface |
| B27.7 | Devices for indirect vision other than mirrors: |
| B27.7.1 | Make |
| B27.7.2 | Identification: TAC No. / BIS License No. / E- Marking |
| B27.7.3 | Area and radius of curvature of the mirror glass reflecting surface |
| B27.8 | Brief drawing showing installation dimensions of all mirrors provided on the vehicle and drivers ocular point angle with RH mirror |
| B28.0 | Information on safety belt / restraint system : |
| B28.1 | Safety belt |
| B28.1.1 | Make of seat belt |
| B28.1.2 | Type and configuration |
| B28.1.3 | Identification No. / Part No. |
| B28.2 | Restraint system |
| B28.2.1 | Make |
| B28.2.2 | Type and configuration |
| B28.2.3 | Identification No. / Part No. |

Table 3 of AIS-007 (Revision 5)

| B28.2.4 | Drawings of the relevant parts of the vehicle structure and any seat anchorage reinforcements |
| --- | --- |
| B28.2.5 | Drawings of the seat, showing its structure, adjustment system and fixing components, with an indication of the materials used. |
| B28.2.6 | Drawing or photograph of the restraint system as installed. |
| B28.2.7 | Drawing showing the installation of belts on the vehicle. |
| B28.3 | Safety belts and / or other restraint systems : |
| B28.3.1 | Number and position of safety belts and restraint systems and seats on which they can be used Row of Seat Location* Type of seat belt Variant (if applicable) Belt adjustment device for height (indicate yes/no/optional) First row of seats L C R Second row of seats L C R The table may be extended as necessary for vehicles with more than two rows of seats there are more than three seats across the width of the vehicle. *(L = left-hand side, R= right-hand side, C = centre) |
| B28.4 | Emergency exit |
| B28.4.1 | Position |
| B28.4.2 | Size |
| 29.0 | Fuel tank : |
| B29.1 | Make |
| B29.2 | Material (Metallic / Plastic etc.) |
| B29.3 | Nominal thickness mm |
| B29.4 | Capacity, litre |
| B29.5 | Detailed drawing of the fuel tank assembly with material specifications |
| B29.6 | Detailed drawing indicating the position / location of the fuel tank (s) in the vehicle. |
| B29.7 | Identification No. / Part No. |
| B30.0 | Wheel rim |
| B30.1 | Size |
| B30.1.1 | Front |
| B30.1.1.1 | Make |
| B30.1.2 | Rear |
| B30.1.2.1 | Make |

Table 3 of AIS-007 (Revision 5)

| B30.1.3 | Others |
| --- | --- |
| B30.2 | Make |
| B30.3 | Identification No. / Part No. |
| B31.0 | Door, Door locks and hinges : |
| B31.1 | Doors |
| B31.1.1 | No. of doors |
| B31.1.2 | Position and type of door |
| B31.1.3 | Detailed drawing of the door including location of the door strengthening bars, cross section of the bars, material specification of the bar and door sheet metal, number of reinforcements and details of welding / bolting etc.,( for side door impact test ) |
| B31.2 | Door lock / latch |
| B31.2.1 | Front |
| B31.2.1.1 | Make |
| B31.2.1.2 | Identification No. / Part No. |
| B31.2.2 | Rear |
| B31.2.2.1 | Make |
| B31.2.2.2 | Identification No. / Part No. |
| B31.3 | Door hinge |
| B31.3.1 | Front |
| B31.3.1.1 | Make |
| B31.3.1.2 | Identification No. / Part No. |
| B31.3.2 | Rear |
| B31.3.2.1 | Make |
| B31.3.2.2 | Identification No. / Part No. |
| B32.0 | Wheel Fastener(s) and Hub cap : |
| B32.1 | Wheel Nut (s) / Bolt (s) |
| B32.1.1 | Make |
| B32.1.2 | Size |
| B32.1.3 | No. per wheel |
| B32.1.4 | Tightening torque on vehicle ( recommended by Vehicle Manufacturer ) |
| B32.1.5 | Detailed dimensional drawing along with material specifications |
| B32.2 | Wheel cap ( if provided ) |
| B32.2.1 | Detailed dimensional drawing along with press fit diameter as applicable |

Table 3 of AIS-007 (Revision 5)

| B32.3 | Hub cap |
| --- | --- |
| B32.3.1 | Make |
| B32.3.2 | Method of fitment (Press/bolted/others) |
| B32.3.3 | Brief dimensional drawing along with pressfit diameter as applicable |
| B33.0 | Towing devices : |
| B33.1 | Type |
| B33.2 | Make |
| B33.3 | Capacity |
| B34.0 | Coupling devices (for trailers) : |
| B34.1 | Make |
| B34.2 | Identification mark |
| B34.3 | Type of coupling device for mechanical |
| B34.4 | Type of coupling device for electrical |
| B34.5 | Type of coupling device for brake |
| B34.6 | Dia. Of king pin (mm) |
| B35.0 | Spray Suppression System |
| B35.1 | Make |
| B35.2 | Type (Water separator / Pulveriser) |
| B35.3 | Identification No. / Part |
| B35.4 | Size |
| B35.5 | Detailed engineering drawing as specified in AIS-013 or photographs showing the mounting details with dimensions. |
| B36.0 | Interior Fittings as per IS 15223 or AIS-047, as applicable |
| B36.1 | Instrument Panel (Dash Board) |
| B36.2 | Make |
| B36.3 | Identification No. / Part No. |
| B36.4 | Drawing showing the mounting details, overall size and all control switches with dimensions |
| B36.5 | Additional details for interior fitting tests to be given (if test is already conducted, this information need not be submitted). |
| B36.5.1 | Instrument Panel Variants with photographs (With / without Airbag, Music system, AC) |
| B36.5.2 | Material used for instrument Panel |
| B36.5.3 | Drawings |
| B36.5.3.1 | Instrument Panel mounting (With hardware details) |
| B36.5.3.2 | ‘H’ point co-ordinates for each seating position |
| B36.5.3.3 | Cross sectional drawings for each projection more than 3.2 |

Table 3 of AIS-007 (Revision 5)

| B36.5.3.4 | Cross sectional Drawing of Gear shift lever |
| --- | --- |
| B36.5.3.5 | Drawing of Grab handle with cross section |
| B36.5.3.6 | Drawing of Sun visor with details of metal wire used |
| B36.5.3.7 | Drawing of lamp assembly mounted at roof |
| B37.0 | Bumper (for M1 category vehicle) : |
| B37.1 | Make |
| B37.2 | Identification No. / Part No./Drawing No. |
| B37.3 | Installation drawing showing location of Bumper in the front and rear, fitment of the Bumper, dimensions of Bumper, mounting points, details of mounting fasteners and additional fitments on it. |
| B37.4 | Material of Bumper with details (metallic / non-metallic) |
| B37.5 | Test method to be adopted by the test agency (Pendulum impact test, Component level vibration test, or Vehicle level four poster test ) |
| B 38.0 | Flammability requirements of interior materials as per IS 15061, as applicable. |
| B 38.1 | Seat Upholstery |
| B 38.1.1 | Make |
| B 38.1.2 | Material and Composition |
| B 38.1.3 | Identification No. / Part No./Drawing No. |
| B 38.2 | Roof lining |
| B 38.2.1 | Make |
| B 38.2.2 | Material and Composition |
| B 38.2.3 | Identification No. / Part No./Drawing No. |
| B 38.3 | Floor lining |
| B 38.3.1 | Make |
| B 38.3.2 | Material and Composition |
| B 38.3.3 | Identification No. / Part No./Drawing No. |
| B 38.4 | Side wall lining |
| B 38.4.1 | Make. |
| B 38.4.2 | Material and Composition |
| B 38.4.3 | Identification No. / Part No./Drawing No. |
| B 38.5 | Rear wall lining |
| B 38.5.1 | Make |
| B 38.5.2 | Material and Composition |
| B 38.5.3 | Identification No. / Part No./Drawing No. |
| B 38.6 | Interior lining of luggage racks |
| B 38.6.1 | Make |
| B 38.6.2 | Material and Composition |
| B 38.6.3 | Identification No. / Part No./Drawing No. |

Table 3 of AIS-007 (Revision 5)

| B 38.7 | Heating and ventilation pipe |
| --- | --- |
| B 38.7.1 | Make |
| B 38.7.2 | Material and Composition |
| B 38.7.3 | Identification No. / Part No./Drawing No. |
| B 38.8 | Curtain / Blinds / Hanging material |
| B 38.8.1 | Make |
| B 38.8.2 | Material and Composition |
| B 38.8.3 | Identification No. / Part No./Drawing No. |
| B 38.9 | Material for Luminaries |
| B 38.9.1 | Make |
| B 38.9.2 | Material and Composition |
| B 38.9.3 | Identification No. / Part No./Drawing No. |
| B 38.10 | Separation wall |
| B 38.10.1 | Make |
| B 38.10.2 | Material and Composition |
| B 38.10.3 | Identification No. / Part No./Drawing No. |
| B39.0 | Hand holds (as per AIS-046) |
| B39.1 | No. of hand holds |
| B39.2 | Details and dimension of hand hold indicating length, clearance between the hand hold and body and cross sectional area. Of every hand hold (if required , details may be provided as a separate Annexure) |
| B39.2.1 | Make |
| B39.2.2 | Identification No. / Part No./Drawing No. |
| B39.2.3 | Type (Grab handle / Strap / Hand Rail) |
| B39.2.4 | Material |
| B39.2.5 | Size |
| B39.3 | Installation drawing of hand hold, showing location of mounting for every seating position, passengers details of mounting fasteners and additional fitments on it |
| B 40.0 | Arrangement of foot controls ( For M1 category as per AIS-035 ) |
| B 40.1 | Distance between the contour points of the orthogonal projections on to plane “P” of the accelerator pedal and service brake pedal bearing surfaces, “E” in mm. |
| B 40.2 | Distance between the projection of the service brake pedal on to the reference plane “P”, to the right, “H” in mm. |
| B 40.3 | Distance between the projection of the service brake pedal on to the reference plane “P”, to the left, “J” in mm. |
| B 40.4 | Drawing showing the parts and arrangement of the foot controls along with dimensions “E”, “H” and “J” |

Table 3 of AIS-007 (Revision 5)

| B41.0 | Statutory Plates – Vehicle Identification Number (As per AIS-065) |
| --- | --- |
| B41.1 | Drawings and/or photographs of the locations of the statutory plates and inscriptions and of the vehicle identification number |
| B41.2 | Drawings and / or photographs of the official part of the plates and inscriptions (completed example with dimensions) |
| B41.3 | Drawings and / or photographs of the Body Builder’s Plates and its location on the vehicle |
| B41.4 | World Manufacturer’s Identifier (WMI) code and its location in Vehicle Identification Number (VIN) |
| B41.5 | Location of Vehicle Descriptor Section (VDS) in Vehicle Identification Number (VIN) |
| B41.6 | Location of Vehicle Indicator Section (VIS) in Vehicle Identification Number (VIN) |
| B41.7 | Height of characters in VIN (mm) |
| B42.0 | Window retention and release for Buses as per IS 13944 |
| B42.1 | Window safety glass |
| B42.1.1 | Method of Window Fixing (sliding or sealed or opening outside etc.) |
| B42.1.2 | Brief description of the Provision for emergency exit provided in case of sealed windows |
| B42.1.3 | Name of the Window Manufacturer |
| B42.2 | Drawing (including Drawing no. & Revision no.) including Plan view, Elevation, LH, RH view of Vehicle showing the dimensions of all windows, seating layout and location of emergency exit. |
| B42.3 | Detailed Brief dimensional drawing of emergency exit indicating its location(s) |
| B42.4 | Number of passenger compartment doors provided in addition to driver’s door. |
| B42.5 | Dimensions Emergency exit identification |
| B42.5.1 | Number(s) and Dimensions of Roof Exit (if provided) |
| B42.6 | Dimensions of the instructions describing each motion necessary to unlatch and open the exit are provided from the release mechanism. |
| B 43.0 | Front Under run Protective devices as per AIS-069 |
| B 43.1 | Drawing of the vehicle parts relevant to the front under run protection, i.e, drawing of the vehicle and/or chassis with position and mounting and/or fitting of the front under run protective device. If the under run protection is by no special device, the drawing should clearly show as how the required dimensions are met. |
| B 43.2 | In the case of special device, full description and/or drawing of the front under run protection (including mountings and fittings). |

Table 3 of AIS-007 (Revision 5)

| B 44.0 | Coupling Device (for T Category) |
| --- | --- |
| B 44.1 | Trade name or mark / approval No(s): |
| B 44.2 | Type (Mechanical / Close): |
| B 44.3 | Class of coupling device |
| B 44.4 | Maximum permissible static mass on coupling ball (kg) |
| B 44.5 | Maximum permissible static vertical load on coupling ball (kgf) |
| B 44.6 | Drawing showing details of mounting points on the vehicle |
| B 44.7 | D.............. kN Dc................ kN S............... kg U...............tonnes V.............. …kN |
| B 45.0 | Make of the rear marking plate: |
| B 45.1 | Rear marking plate type: |
| B 45.2 | Rear marking plate class: |
| B 45.3 | Position and nature of the marking: |
| B 46.0 | Anti-theft devices ( Mechanical / Retro-mechanical devices as per AIS-075 ) |
| B 46.1 | Make |
| B 46.2 | Identification No. / Part No./Drawing No. |
| B 46.3 | Type of protective device (s) ( Ref. Clause No. 10.3 of AIS-075) |
| B 46.4 | No. of combinations used in the protective device |
| B 46.5 | Description of device or sketch drawing location, relevant dimension of protective device, material and physical property of the locking element of the device which engages with the steering / transmission / gearshift (as the case may be) |
| B 46.6 | Any device specific information ( As per Clause 13.0 ) |
| B 46.7 | Devices provided additionally, acoustic or visual ( if visual, duration and type of optical signal be specified ) |
| B 47.0 | Vehicle Alarm Systems and Immobilisers (as per AIS-076, for M1 & N1 Category Vehicles ) |
| B 47.1 | Make |
| B 47.2 | Type |
| B 47.3 | Identification No. / Part No./Drawing No. |
| B 47.4 | A detailed description of the alarm system and of the vehicle parts related to alarm system installed. |
| B 47.5 | A list of main components comprising the alarm system |
| B 47.6 | Measures against false alarm |
| B 47.7 | Range of protection offered by the device |

Table 3 of AIS-007 (Revision 5)

| B 47.8 | Method of setting / unsetting the device |
| --- | --- |
| B 47.9 | Number of interchangeable codes, if applicable |
| B 47.10 | List of main components comprising the device |
| B 47.11 | Description of the method of installation illustrated by photographs and / or drawings. |
| B 48.0 | Child Restraint system (CRS) ; |
| B 48.1 | Seating Positions for Child restraint system (As per AIS-072) |
| B 48.2 | Details of CRS (To be provided if the CRS is not of Universal category (U/UF)) |
| B 48.3 | Category of CRS(Semi Universal, Restricted or specific vehicle) |
| B 48.4 | Belt type: (adult) three-point belt (adult) lap belt/ special type belt/retractor; |
| B 48.5 | Trade name or mark |
| B 48.6 | Drawings, Diagrams and plans of the child restraint, including any retractor, chair assembly, impact shield fitted |
| B 48.7 | Drawings, Diagrams and plans of the child restraint, including any retractor, chair assembly, impact shield fitted; |
| B 48.8 | Drawings, Diagrams and plans of the vehicle structure and the seat structure, as well as of the adjustment system and the attachments, including any energy absorber fitted; |
| B 48.9 | Photographs of the child restraint and/or vehicle structure and seat structure; |

Table 3 of AIS-007 (Revision 5)

| B 49.0 | Head-On Collision as per AIS-096 and Off-set frontal collision as per AIS-098 |
| --- | --- |
| B 49.1 | Brief description of the vehicle type as regards its structure, dimensions, lines and constituent materials: |
| B 49.2 | Description of the protective system installed in the vehicle: |
| B 49.3 | Description of interior arrangements or fittings that might affect the tests: |
| B 49.4 | (Photographs and/or diagrams and drawings permitting the basic identification of the type(s) of vehicle and its possible variants which are covered by the approval) |
| B 50.0 | Side-Impact resistance as per AIS-099 |
| B 50.1 | A detailed description, including photographs and/or drawings, of the vehicle type with respect to the structure, the dimensions, the design and the constituent materials, the side walls of the passenger compartment (exterior and interior), including specific details of the protection system, where applicable: |
| B 51.0 | Pedestrian protection as per AIS-100 : |
| B 51.1 | A detailed description, including photographs and/or drawings, of the vehicle with respect to the structure, the dimensions, the relevant reference lines and the constituent materials of the frontal part of the vehicle (interior and exterior) shall be provided. This description should include detail of any active protection system installed. |
| B 52.0 | Speed Governor (As applicable) |
| B 52.1 | Type of Speed Governer (SLD / SLF) |
| B 52.2 | Speed Limiting Device (SLD) [ For vehicles with max. speed above 80 kmph in unladen condition as per AIS-018 ] |
| B 52.3 | Make |
| B 52.4 | Model |
| B 52.5 | Identification: TAC No. / BIS License No. |
| B 52.6 | SLD approved for speed/s ( Annexure to be provided including information for every Vehicle Model / Variants indicating various SLD approved speeds contributed due to declared transmission options ) |
| B 53.0 | Temporary Cabin for drive away chassis : |
| B 53.1 | Width of the temporary cabin (mm) |
| B 53.2 | Height of the temporary cabin (from seat top surface to canopy) (mm) |
| B 53.3 | Depth or Length of the temporary cabin (Clearance from the rear most back rest when the seat is taken at the rear-most position) (mm) |
| B 53.4 | Windshield type |
| B 53.5 | Drawing showing the mounting and relevant dimensions |

| Table 4 of AIS-007 (Revision 5) TECHNICAL SPECIFICATION – FOUR WHEELERS AND ABOVE PART C - ENGINE |
| --- |
| Clause No. | Description |
| C1.0 | Description of Engine: |
| C1.1 | Type (Compression Ignition / Positive Ignition) |
| C1.1.1 | Compliance sought for emission norms (BS-III /BS -IV /Any other) |
| C1.2 | Make |
| C1.3 | Name and address of the engine manufacturing plant |
| C1.4 | Working principle: (Four / two stroke), (DI / IDI ) (NA/TC/TCIC/ Any other ) |
| C1.5 | Model name and identification |
| C1.6 | Type of fuel used |
| C1.7 | No.& Layout of cylinders & firing order |
| C1.8 | Swept volume cc |
| C1.9 | Bore (mm) |
| C1.10 | Stroke (mm) |
| C1.11 | Compression ratio (specify tolerance) |
| C1.12 | Engine performance (declared by the manufacturer): |
| C1.12.1 | Max. Net power of engine on bench (kW @ rpm)(Specify standard and tolerance) |
| C1.12.2 | Maximum net torque on bench (Nm @ rpm) Note : In case of diesel engines the max. Power and max. Torque shall be specified as per conditions given in Chapter 6 of Part IV of Doc. MoRTH / CMVR / TAP-115 / 116 Issue No.3 |
| C1.13 | Location of engine (Front / Rear) |
| C2.0 | Combustion System: |
| C2.1 | Type of combustion chamber (Hemispherical/ squish/others) |
| C2.2 | Drawing(s) of combustion chamber and piston crown (Enclose the drawing & Mention the drawing no. & Part no.) |
| C2.3 | Minimum cross section area of ports |
| C2.3.1 | Inlet (cm2) |
| C2.3.2 | Outlet (cm2) |
| C3.0 | Ignition System (Spark Ignition engines only): |
| C3.1 | Type |
| C3.2 | Nominal Voltage |
| C3.3 | Operating Principle |
| C3.4 | CDI |
| C3.5 | Table of Combination for EMI test |

Table 4 of AIS-007 (Revision 5)

| C3.6 | Ignition advance curve (specify tolerance) & enclose the curve |
| --- | --- |
| C3.7 | Ignition timing (specify tolerance) |
| C3.8 | Contact point gap and dwell angle (specify tolerance) |
| C3.9 | Type and make of distributor |
| C3.10 | Sparking plugs |
| C3.10.1 | Make |
| C3.10.2 | Type and designation |
| C3.10.3 | Spark-gap setting |
| C3.10.4 | Nominal resistance (kilo ohm) (if resistive type) |
| C3.11 | Ignition coil |
| C3.11.1 | Make |
| C3.11.2 | Type |
| C3.11.3 | Identification |
| C3.12 | Ignition condenser |
| C3.12.1 | Make |
| C3.12.2 | Type |
| C3.12.3 | Identification |
| C3.13 | EMI suppressor cap / Device / Electronic unit |
| C3.13.1 | Make |
| C3.13.2 | Type (Resistive/Capacitive) |
| C3.13.3 | identification |
| C3.13.4 | Nominal resistance (kilo ohm) |
| C3.13.5 | Terminology and Drawing of interference Suppression equipment |
| C3.14 | H.T. Cable |
| C3.14.1 | Make and Place |
| C3.14.2 | Type (Resistive/Non-resistive) |
| C3.14.3 | Length mm (if resistive type) |
| C3.14.4 | Outside dia. mm (if resistive type) |
| C3.14.5 | Nominal resistance kilo ohm, (if resistive type) |
| C4.0 | Cooling system : |
| C4.1 | Liquid cooling system |
| C4.1.1 | Nature of liquid |
| C4.1.2 | Circulating pump yes/no |

Table 4 of AIS-007 (Revision 5)

| C4.1.3 | Characteristics of Circulating pump or make(s) & type(s) |
| --- | --- |
| C4.1.3.1 | Drive ratio |
| C4.1.4 | Nominal temperature setting of the engine temperature control mechanism |
| C4.1.5 | Radiator drawing(s) |
| C4.1.5.1 | Make(s) |
| C4.1.5.2 | Type(s) |
| C4.1.5.3 | Relief valve pressure setting |
| C4.1.6 | Fan characteristics (Fan power, kW) Enclose the fan power curve corresponding to full load (v/s engine speed) of viscous fan. |
| C4.1.6.1 | Make(s) |
| C4.1.6.1.1 | No. of blades |
| C4.1.6.1.2 | Material of blades ( metal / plastic ) |
| C4.1.6.2 | Type(s) [Fixed / Viscous / Electrical driven] |
| C4.1.6.3 | Drive ratio |
| C4.1.6.4 | Fan diameter (mm) |
| C4.1.6.5 | Max. Speed of fan (in rev/min) |
| C4.1.7 | Radiator core open area (cm²) |
| C4.2 | Air Cooling system |
| C4.2.1 | Blower characteristics |
| C4.2.1.1 | Make |
| C4.2.1.2 | Type(s) |
| C4.2.1.3 | Drive ratio(s) |
| C4.2.2 | Air ducting (std production) |
| C5.0 | Temperature permitted by manufacturer in 0C for liquid cooling (Location of measurement be specified) |
| C5.1 | Max. temp. at engine outlet |
| C6.0 | Temperature permitted by manufacturer in 0C for Air cooling (Location of measurement be specified ) |
| C6.1 | Reference point |
| C6.2 | Max. temperature at reference point |
| C6.3 | Max. Temperature of the intercooled-air (Location of measurement be specified) |
| C6.4 | Max. Exhaust temperature (in case of diesel engines, at the point in the exhaust pipe(s) adjacent in outlet flange(s) of exhaust manifolds), Specify the distance from the outlet flange. |

Table 4 of AIS-007 (Revision 5)

| C7.0 | Fuel temperature 0C: (for diesel engines at the injection pump inlet) |
| --- | --- |
| C7.1 | Minimum |
| C7.2 | Maximum |
| C8.0 | Lubricant Temperature 0C (Location of measurement be specified ) |
| C8.1 | Minimum |
| C8.2 | Maximum |
| C9.0 | Intake system : (Attach drawing, mention Drawing No. & Part No.) |
| C9.1 | Supercharger / Turbocharger - yes/no |
| C9.1.1 | Description of system |
| C9.1.2 | Make(s) |
| C9.1.3 | Type(s) |
| C9.1.4 | Description of system (e.g. Charge pressure @ max. power and torque speed, waste gate, if applicable) |
| C9.2 | Intake manifold (Enclose drawing with drawing No. & Part No.) |
| C9.2.1 | Description |
| C9.2.2 | Identification No / Part No./ Drawing No. |
| C9.2.3 | Schematic dimensional drawing |
| C9.3 | Air filter |
| C9.3.1 | Make |
| C9.3.2 | Type |
| C9.3.3 | Identification No / Part No./ Drawing No. |
| C9.3.4 | Schematic dimensional drawing |
| C9.4 | Intake silencer |
| C9.4.1 | Make |
| C9.4.2 | Type / Description |
| C9.4.3 | Identification No / Part No./ Drawing No. |
| C9.4.4 | Schematic dimensional drawing of inlet pipe and their accessories (dash pot, heating devices, additional air intake etc.) |
| C9.5 | Inter cooler |
| C9.5.1 | Make |
| C9.5.2 | Identification No / Part No./ Drawing No. |
| C9.5.3 | Air pressure drop across the inter-cooler |
| C10.0 | Fuel feed: (By carburetor) |
| C10.1 | Number |
| C10.2 | Make |
| C10.3 | Type |

Table 4 of AIS-007 (Revision 5)

| C10.4 | Adjustments (specify tolerance) |
| --- | --- |
| C10.4.1 | Jets |
| C10.4.2 | Venturies |
| C10.4.3 | Float-chamber level |
| C10.4.4 | Mass of float |
| C10.4.5 | Float needle |
| C10.5 | Dimensions of mixture duct |
| C10.6 | Choke: Type (Manual/automatic) and closure setting |
| C10.7 | Feed pump |
| C10.7.1 | Pressure (specify tolerance) or characteristic diagrams |
| C10.7.2 | Type of fuel feed pump |
| C11.0 | Fuel feed: {By fuel injection} |
| C11.1 | Injection system description |
| C11.2 | Working principle: intake manifold/ direct injection / indirect injection / swirl chamber/others |
| C11.3 | Fuel Pump |
| C11.3.1 | Make(s) |
| C11.3.2 | Type(s) |
| C11.3.3 | Pressure / characteristic diagram |
| C11.4 | Delivery mm3/ per stroke at max net power speed in case of Diesel Engine & specify delivery in kg/h at max net power speed in case of gas engines (specify tolerance) and enclose characteristic diagram (specify tolerance). If boost control is supplied, state the characteristics fuel delivery and boost pressure versus engine speed. |
| C11.5 | Calibration Method (on engine/pump bench) |
| C11.6 | Static Injection timing |
| C11.7 | Injection advance curve (Diagram be enclosed) |
| C11.8 | Injection advance (specify the tolerance) |
| C11.9 | Injector (s) |
| C11.9.1 | Type (s) (mention holder, nozzle and assembly no(s)) |
| C11.9.2 | Make (s) |
| C11.9.3 | Opening pressure (specify tolerance) or characteristic diagram |
| C11.9.4 | Injection piping |
| C11.9.4.1 | Length mm |
| C11.9.4.2 | Internal diameter mm |
| C 12.0 | Device for recycling crank-case gases |
| C12.1 | Description & drawings |

Table 4 of AIS-007 (Revision 5)

| C13.0 | Governor |
| --- | --- |
| C13.1 | Type(s) |
| C13.2 | Speed at which Cut off starts under load (rev/min) |
| C13.3 | Max. speed without load (rev/min) |
| C13.4 | Idle Speed (rev/min) |
| C14.0 | Cold start device (starting aid) |
| C14.1 | Make |
| C14.2 | Type(s) |
| C14.3 | System description |
| C15.0 | Starting System : |
| C15.1 | Type(s) |
| C15.2 | System description |
| C16.0 | Valve timing / Port timing or equivalent data |
| C16.1 | Max. lift of valves |
| C16.1.1 | Inlet mm |
| C16.1.2 | Exhaust mm |
| C16.2 | Angle of valves / port (w.r.t. top dead center) |
| C16.3 | Inlet |
| C16.3.1 | Opening |
| C16.3.2 | Closing |
| C16.4 | Exhaust |
| C16.4.1 | Opening |
| C16.4.2 | Closing |
| C16.5 | Transfer |
| C16.5.1 | Opening |
| C16.5.2 | Closing |
| C16.6 | Reference or setting ranges |
| C16.7 | Valve gap (Hot or Cold as applicable) |
| C16.7.1 | Inlet |
| C16.7.2 | Exhaust |
| C16.8 | Distribution by ports |
| C16.8.1 | Volume of crank-case cavity with piston at TDC |
| C16.8.2 | Reed valve fitted ( Yes / No ) |
| C16.8.3 | Description of inlet ports, scavenging and exhaust ports with corresponding timing. |

Table 4 of AIS-007 (Revision 5)

| C17.0 | Lubrication system |
| --- | --- |
| C17.1 | Description of system |
| C17.2 | Position of lubricant reservoir |
| C17.3 | Feed system (pump, injection in to intake mixing with fuel etc.,) |
| C17.4 | Lubricating pump |
| C17.4.1 | Type |
| C17.5 | Mixture with fuel: yes/no, and if yes % ( for 2 stroke engines ) |
| C17.6 | Oil cooler : yes/no, and if yes Enclose dimensional drawings, make(s) & type(s) |
| C18.0 | Electrical equipment |
| C18.1 | Generator/alternator characteristics (specify tolerance) or |
| C18.1.1 | Make |
| C18.1.2 | Identification No / Part No./ Drawing No. |
| C19.0 | Other engine driven auxiliaries |
| C19.1 | Enumeration & brief description, if necessary |
| C20.0 | Idling System: |
| C20.1 | Idling speed (rpm) (specify the tolerance) |
| C20.2 | Description of settings and relevant requirements |
| C20.3 | Carbon monoxide and HC content by volume in the exhaust gas with the engine idling, per cent (for SI engines only) (manufacturer’s standard) |
| C20.4 | High Idle (2500 ± 200 rpm) Lambda value(For petrol driven four wheeled vehicles only) (1± 0.03 or as specified by the vehicle manufacturer) |
| C 21.0 | Requirements for engine test |
| C21.1 | Maximum permitted depression of air intake at characteristic place in kPa (Specify location of measurement)) |
| C21.2 | Exhaust back pressure at maximum net power and location of measurement (kPa) |
| C21.3 | Effective volume of exhaust-system (specify the tolerance & range) in liters (from exhaust manifold / TC outlet to tail pipe end), Enclose the exhaust system dimensional drawing and indicate the volume of each parts clearly. |
| C21.4 | Moment of inertia of combined flywheel & transmission at condition when no gear is engaged |
| C21.5 | Maximum rated speed (Specify the tolerance) |
| C21.6 | Minimum rated speed (Specify the tolerance) |
| C21.7 | Max. Net Torque on bench ……. Nm at ……..rpm ( specify tolerance ) |
| C21.8 | Max. net Power on bench, ……. Nm at ……..rpm ( specify tolerance ) |

Table 4 of AIS-007 (Revision 5)

| C21.9 | Engine Performance Declared speed and powers of the engine submitted for type approval) (Speeds to be agreed with the testing agency) |
| --- | --- |
| C21.9.1 | Engine Speeds (For ESC & ELR cycles) |
| C21.9.2 | Low Speed (nlo) (rpm) |
| C21.9.3 | High Speed (nhi) (rpm) |
| C21.9.4 | Speed A (rpm) |
| C21.9.5 | Speed B (rpm) |
| C21.9.6 | Speed C (rpm) |
| C21.9.7 | Engine Power Table Measurement point* Engine speed rpm New Power kW** (1) (2) (3) (4) (5) (6) * See Chapter 3 of Part IV of Doc.MoRTH/CMVR/TAP115/116 Issue No.4 ** Net power according to Chapter 6 of Part IV of Doc. MoRTH/CMVR/TAP115/116 Issue No.4. Note: In case, if data regarding the Moment of Inertia, is required by the test agency for carrying out the Full Throttle performance test for both the CI / SI engines, the same shall be provided by the manufacturer. |
| C22.0 | Exhaust system |
| C22.1 | Silencer |
| C22.1.1 | Type |
| C22.1.2 | Make |
| C22.1.3 | Number |
| C22.1.4 | Silencer identification No. / Part No. |
| C22.2 | Internal diameter of exhaust pipe (mm) |
| C22.3 | Description with general arrangement of exhaust system along with its routing indicating the lengths of exhaust pipe, tail pipe and exhaust outlet location, indicated in a Schematic dimensional drawing. |
| C22.4 | Minimum distance between exhaust pipe(s) and the fuel line |
| C22.5 | Auxiliary Noise shields for compliance to IS 3028 and / OR AIS-020 (If Provided) |
| C22.5.1 | Material |
| C22.5.2 | Layout of noise shield / Photographs / Diagram Showing arrangements indicating fitment on vehicle. |

Table 4 of AIS-007 (Revision 5)

| C23.0 | Additional emission control devices, such as catalytic converter etc. (if any & if not covered by another heading) |
| --- | --- |
| C23.1 | Catalyser make, number |
| C23.2 | Identification No / Part No./ Drawing No. |
| C23.3 | Type of catalytic action (One/two/three way) |
| C23.4 | Total charge of precious metal (g/vehicle) |
| C23.5 | Relative concentration (%) |
| C23.5.1 | Platinum |
| C23.5.2 | Rhodium |
| C23.5.3 | Palladium |
| C23.6 | Substrate (Monolithic metal/ Ceramic/ honeycomb) |
| C23.6.1 | Cell density (cells per sq. inch / cm) |
| C23.7 | Type of casing for catalyser |
| C23.8 | Diagram indicating the arrangement and position of catalytic converter w.r.t. exhaust manifold) |
| C23.9 | Lambda Sensor |
| C23.9.1 | Make |
| C23.9.2 | Type / Part No. |
| C23.9.3 | Identification No / Part No./ Drawing No. |
| C23.9.4 | Location |
| C 23.10 | Regeneration systems/method of exhaust after-treatment systems, description: |
| C 23.10.1 | The number of Type I operating cycles, or equivalent engine test bench cycles, between two cycles where regenerative phases occur under the conditions equivalent to Type I test (Distance "D" in figure 1 in Chapter 15 of TAP Document) : |
| C 23.10.2 | Description of method employed to determine the number of cycles between two cycles where regenerative phases occur: |
| C23.10.3 | Parameters to determine the level of loading required before regeneration occurs (i.e. temperature, pressure etc.): |
| C23.10.4 | Description of method used to load system in the test procedure described in paragraph 3.1., ( Refer Chapter 15 of TAP Document) : |
| C 23.11 | Oxygen sensor: type |
| C 23.11.1 | Location of oxygen sensor: |
| C23.11.2 | Control range of oxygen sensor: |
| C 23.11.3 | Regeneration system/method - Description and drawing: |
| C23.12 | Electronic Control Unit (ECU) |
| C23.12.1 | Make |
| C23.12.2 | Identification mark |
| C23.12.3 | Calibration Identification No. |
| C23.12.4 | Adjustment possibilities ( Yes / No ) |

Table 4 of AIS-007 (Revision 5)

| C23.13 | Secondary Air Injection |
| --- | --- |
| C23.13.1 | Make |
| C23.13.2 | Identification mark |
| C23.14 | Exhaust Gas Re-circulating System |
| C23.14.1 | Brief description of the system |
| C23.14.2 | Type ( Cooled / Non-cooled/Progressive/ On-Off/ Any Other ) |
| C23.14.3 | EGR Valve |
| C23.14.3.1 | Make |
| C23.14.3.2 | Type |
| C23.14.3.3 | Identification No / Part No./ Drawing No. |
| C23.14.4 | EGR Electronic Control Unit |
| C23.14.4.1 | Make |
| C23.14.4.2 | Identification No / Part No./ Drawing No. |
| C24.0 | Additional information for evaporative emission |
| C24.1 | Evaporative emission control system |
| C24.2 | Type |
| C24.3 | Make |
| C24.4 | Complete detailed description of devices and their state of tune |
| C24.5 | Drawing of the evaporative control system |
| C24.6 | Drawing of the fuel tank with indication of capacity and material |
| C24.7 | Canister |
| C24.7.1 | Working capacity |
| C24.7.2 | Make |
| C24.7.3 | Identification No / Part No./ Drawing No. |
| C24.7.4 | Schematic diagram |
| C24.7.5 | Canister bed volume (1) |
| C 25.0 | On Board Diagnosis (OBD ) |
| C 25.1 | Written description and/or drawing of the Malfunction Indicator(MI). |
| C 25.2 | List and purpose of all components monitored by the OBD system. |
| C 25.3 | Written description (general working principles) for ; |
| C 25.3.1 | Positive-ignition engines. |
|  | Catalyst monitoring |
| C 25.3.1.1 | Misfire detection |
| C 25.3.1.2 | Oxygen sensor monitoring |
| C 25.3.1.3 | Other components monitored by the OBD system |

Table 4 of AIS-007 (Revision 5)

| 25.3.2 | Compression-ignition engines |
| --- | --- |
|  | Catalyst Monitoring |
| C 25.3.2.1 | Particulate trap monitoring |
| C 25.3.2.2 | Electronic fuelling system monitoring |
| C 25.3.2.3 | deNox system monitoring |
| C 25.3.2.4 | Other components monitored by the OBD system |
| C 25.4 | Criteria for MI activation (fixed number of driving cycles or statistical method) |
| C 25.5 | List of all OBD output codes and formats used (with explanation of each). |
| C 25.6 | The following additional information shall be provided by the vehicle manufacturer for the purposes of enabling the manufacture of OBD-compatible replacement or service parts and diagnostic tools and test equipment, unless such information is covered by intellectual property rights or constitutes specific know-how of the manufacturer or the OEM supplier(s). |
| C 25.6.1 | A description of the type and number of the pre-conditioning cycles used for the original type approval of the vehicle. |
| C 25.6.2 | A description of the type of the OBD demonstration cycle used for the original type-approval of the vehicle for the component monitored by the OBD system. |
| C 25.6.3 | A comprehensive document describing all sensed components with the strategy for fault detection and MI activation (fixed number of driving cycles or statistical method), including a list of relevant secondary sensed parameters for each component monitored by the OBD system. A list of all OBD output codes and format used (with an explanation of each) associated with individual emission related power-train components and individual non-emission related components, where monitoring of the component is used to determine MI activation. In particular, a comprehensive explanation for the data given in service $05 Test ID $21 to FF and the data given in service $06 must be provided. In the case of vehicle types that use a communication link in accordance with ISO 15765-4 “Road vehicles, diagnostics on controller area network (CAN) – part 4: requirements for emissions-related systems”, a comprehensive explanation for the data given in service $06 Test ID $00 to FF, for each OBD monitor ID supported, must be provided. This information may be defined in the form of a table, as follows: Component Fault code Monitoring strategy MI activation criteria Secondary parameters Pre-conditioning Demon-stration test Catalyst P0420 Oxygen sensor 1 and 2 signals 3rd cycle Engine speed, engine load, A/F mode, catalyst temperature Two type 1 cycles Type 1’ |

Table 4 of AIS-007 (Revision 5)

| C 25.7 | Torque limiter (yes/No) (for vehicles with GVW above 3500 kg) |
| --- | --- |
| C25.7.1 | Description of the torque limiter activation |
| C25.7.2 | Description of the full load curve limitation |
| C 26.0 | Particulate trap ( Yes / No) |
| C 26.1 | Dimensions and shape of the particulate trap (capacity): |
| C 26.2 | Type of particulate trap and design: |
| C 26.3 | Location of the particulate trap (reference distances in the exhaust system): |
| C 26.4 | Regeneration system/method - Description and Drawing: |
| C 26.4.1 | The number of Type I operating cycles, or equivalent engine test bench cycle, between two cycles where regeneration phases occur under the conditions equivalent to Type I test (Distance 'D' in figure 1 in Chapter 15 of TAP Document) : |
| C 26.4.2 | Description of method employed to determine the number of cycles between two cycles where regenerative phases occur: |
| C 26.4.3 | Parameters to determine the level of loading required before regeneration occurs (i.e. temperature, pressure, etc.): |
| C 26.4.4 | Description of method used to load system in the test procedure described in paragraph 3.1., Chapter 15 of TAP Document : |

| Table 4A of AIS-007 (Revision 5) |
| --- |
| Essential Characteristics of the Engine family–For Engines fitted on vehicles with GVW greater than 3500 kg specifically for BS-IV compliance |
| C 1.0 | Common parameters |  |
| C 1.1 | Combustion Cycle |  |
| C 1.2 | Cooling Medium |  |
| C 1.3 | Number of cylinders |  |
| C 1.4 | Individual cylinder displacement |  |
| C 1.5 | Method of air aspiration |  |
| C 1.6 | Combustion chamber type /design |  |
| C 1.7 | Valve and Porting – Configuration, size and number |  |
| C 1.8 | Fuel System |  |
| C 1.9 | Ignition System ( gas engines) |  |
| C 1.10 | Miscellaneous features |  |
| C 1.10.1 | Charge Cooling System |  |
| C 1.10.2 | Exhaust gas Recirculation |  |
| C 1.10.3 | Water Injection Emulsion |  |
| C 1.10.4 | Air Injection |  |
| C 1.11 | Exhaust After treatment – Proof of identical (or lowest for the parent engine) ratio: system capacity/fuel delivery per stroke, pursuant to diagram number |  |
| C 2.0 | Engine family listing |  |
| C 2.1 | Name of diesel engine family |  |

Table 4A of AIS-007 (Revision 5)

| C 2.1.1 | Specifications of engines within the family |
| --- | --- |
|  |  | Parent engine |
|  | Engine type |  |  |  |  |  |
|  | Number of cylinders |  |  |  |  |  |
|  | Rated speed (rpm) |  |  |  |  |  |
|  | Fuel delivery per stroke(mm3) |  |  |  |  |  |
|  | Rated net Power(kW) |  |  |  |  |  |
|  | Maximum torque speed(rpm) |  |  |  |  |  |
|  | Fuel delivery per stroke (mm3) |  |  |  |  |  |
|  | Max torque (Nm) |  |  |  |  |  |
|  | Low idle speed(rpm) |  |  |  |  |  |
|  | Cylinder displacement (in % of parent engine) |  |  |  |  |  |
| C 2.2 | Name of gas engine family |  |
| C 2.2.1 | Specifications of engine within the family |  |
|  |  | Parent engine |
|  | Engine type |  |  |  |  |  |
|  | Number of cylinders |  |  |  |  |  |
|  | Rated speed (rpm) |  |  |  |  |  |
|  | Fuel delivery per stroke(mm3) |  |  |  |  |  |
|  | Rated net Power(kW) |  |  |  |  |  |
|  | Maximum torque speed(rpm) |  |  |  |  |  |
|  | Fuel delivery per stroke (mm3) |  |  |  |  |  |
|  | Max torque (Nm) |  |  |  |  |  |
|  | Low idle speed(rpm) |  |  |  |  |  |
|  | Cylinder displacement (in % of parent engine) |  |  |  |  |  |
|  | Spark timing |  |  |  |  |  |
|  | EGR flow |  |  |  |  |  |
|  | Air pump (yes/ no) |  |  |  |  |  |
|  | Air pump actual flow |  |  |  |  |  |

| Table 4B of AIS-007 (Revision 5) TECHNICAL SPECIFICATION – FOUR WHEELERS AND ABOVE PART C - Technical specification of the Parent Engine fitted on vehicles with GVW greater than 3500 kg |
| --- |
| Clause No. | Description |
| C1.0 | Description of Engine: |
| C1.1 | Type (Compression Ignition / Positive Ignition) |
| C1.2 | Make |
| C1.3 | Name and address of the engine manufacturing plant |
| C1.4 | Working principle: (Four / two stroke), (DI / IDI ) (NA/TC/TCIC/ Any other ) |
| C1.5 | Model name and identification |
| C1.6 | Type of fuel used |
| C1.7 | No.& Layout of cylinders & firing order |
| C1.8 | Swept volume cc |
| C1.9 | Bore (mm) |
| C1.10 | Stroke (mm) |
| C1.11 | Compression ratio (specify tolerance) |
| C1.12 | Engine performance (declared by the manufacturer): |
| C1.12.1 | Max. Net power of engine on bench (kW @ rpm)(Specify standard and tolerance) |
| C1.12.2 | Maximum net torque on bench (Nm @ rpm) Note : In case of diesel engines the max. Power and max. Torque shall be specified as per conditions given in Chapter 6 of Part IV of Doc. MoSRTH / CMVR / TAP-115 / 116 Issue No.3 |
| C1.13 | Location of engine (Front / Rear) |
| C2.0 | Combustion System: |
| C2.1 | Type of combustion chamber (Hemispherical/ squish/others) |
| C2.2 | Drawing(s) of combustion chamber and piston crown (Enclose the drawing & Mention the drawing no. & Part no.) |
| C2.3 | Minimum cross section area of ports |
| C2.3.1 | Inlet (cm2) |
| C2.3.2 | Outlet (cm2) |
| C3.0 | Ignition System (Spark Ignition engines only): |
| C3.1 | Make |
| C3.2 | Type |
| C3.3 | Nominal Voltage |
| C3.4 | Operating Principle |

Table 4B of AIS-007 (Revision 5)

| C3.5 | CDI |
| --- | --- |
| C3.6 | Table of Combination for EMI test |
| C3.7 | Ignition advance curve (specify tolerance) & enclose the curve |
| C3.8 | Ignition timing (specify tolerance) |
| C3.9 | Contact point gap and dwell angle (specify tolerance) |
| C3.10 | Type and make of distributor |
| C3.11 | Sparking plugs |
| C3.11.1 | Make |
| C3.11.2 | Type and designation |
| C3.11.3 | Spark-gap setting |
| C3.11.4 | Nominal resistance (kilo ohm) (if resistive type) |
| C3.12 | Ignition coil |
| C3.12.1 | Make |
| C3.12.2 | Type |
| C3.12.3 | Identification |
| C3.13 | Ignition condenser |
| C3.13.1 | Make |
| C3.13.2 | Type |
| C3.13.3 | Identification |
| C3.14 | EMI suppressor cap / Device / Electronic unit |
| C3.14.1 | Make |
| C3.14.2 | Type (Resistive/Capacitive) |
| C3.14.3 | identification |
| C3.14.4 | Nominal resistance (kilo ohm) |
| C3.14.5 | Terminology and Drawing of interference Suppression equipment |
| C3.15 | H.T.Cable |
| C3.15.1 | Make and Place |
| C3.15.2 | Type (Resistive/Non-resistive) |
| C3.15.3 | Length mm (if resistive type) |
| C3.15.4 | Outside dia. mm (if resistive type) |
| C3.15.5 | Nominal resistance kilo ohm, (if resistive type) |
| C3.16 | Systems incorporating electronic oscillator with an operating frequency greater than 9 kHz |

Table 4B of AIS-007 (Revision 5)

| C4.0 | Cooling system : |
| --- | --- |
| C4.1 | Liquid cooling system |
| C4.1.1 | Nature of liquid and capacity |
| C4.1.2 | Circulating pump yes/no |
| C4.1.3 | Characteristics of Circulating pump or make(s) & type(s) |
| C4.1.3.1 | Drive ratio |
| C4.1.4 | Thermostat type and setting |
| C4.1.5 | Radiator drawing(s) |
| C4.1.5.1 | Make(s) and Place |
| C4.1.5.2 | Type(s) |
| C4.1.5.3 | Relief valve pressure setting |
| C4.1.6 | Fan characteristics (Fan power, kW) Enclose the fan power curve corresponding to full load (v/s engine speed) of viscous fan. |
| C4.1.6.1 | Make(s) |
| C4.1.6.1.1 | No. of blades |
| C4.1.6.1.2 | Material of blades ( metal / plastic ) |
| C4.1.6.2 | Type(s) [Fixed / Viscous / Electrical driven] |
| C4.1.6.3 | Fan drive system |
| C4.1.6.4 | Drive ratio |
| C4.1.6.5 | Fan cowl |
| C4.1.6.6 | Fan diameter (mm) |
| C4.1.6.7 | Max. Speed of fan (in rev/min) |
| C4.1.7 | Radiator core open area (cm²) |
| C4.2 | Air Cooling system |
| C4.2.1 | Blower characteristics |
| C4.2.1.1 | Make |
| C4.2.1.2 | Type(s) |
| C4.2.1.3 | Drive ratio(s) |
| C4.2.2 | Air ducting (std production) |
| C5.0 | Temperature permitted by manufacturer in 0C for liquid cooling (Location of measurement be specified) |
| C5.1 | Max. temp. at engine outlet |
| C6.0 | Temperature permitted by manufacturer in 0C for Air cooling (Location of measurement be specified ) |
| C6.1 | Reference point |
| C6.2 | Max. temperature at reference point |
| C6.3 | Max. Temperature of the intercooled-air (Location of measurement be specified) |
| C6.4 | Max. Exhaust temperature (in case of diesel engines, at the point in the exhaust pipe(s) adjacent in outlet flange(s) of exhaust manifolds), Specify the distance from the outlet flange. |

Table 4B of AIS-007 (Revision 5)

| C7.0 | Fuel temperature 0C: (for diesel engines at the injection pump inlet) |
| --- | --- |
| C7.1 | Minimum |
| C7.2 | Maximum |
| C8.0 | Lubricant Temperature 0C (Location of measurement be specified ) |
| C8.1 | Minimum |
| C8.2 | Maximum |
| C9.0 | Intake system : (Attach drawing, mention Drawing No. & Part No.) |
| C9.1 | Supercharger / Turbocharger - yes/no |
| C9.1.1 | Description of system |
| C9.1.2 | Make(s) , |
| C9.1.3 | Type(s) and part no. |
| C9.1.4 | Description of system (e.g. Charge pressure @ max. power and torque speed, waste gate, if applicable) |
| C9.2 | Intake manifold (Enclose drawing with drawing No. & Part No.) |
| C9.2.1 | Description |
| C9.2.2 | Identification No / Part No./ Drawing No. |
| C9.2.3 | Schematic dimensional drawing |
| C9.3 | Air filter |
| C9.3.1 | Make |
| C9.3.2 | Type |
| C9.3.3 | Identification No / Part No./ Drawing No. |
| C9.3.4 | Schematic dimensional drawing |
| C9.4 | Intake silencer |
| C9.4.1 | Make |
| C9.4.2 | Type / Description |
| C9.4.3 | Identification No / Part No./ Drawing No. |
| C9.4.4 | Schematic dimensional drawing of inlet pipe and their accessories (dash pot, heating devices, additional air intake etc.) |
| C9.5 | Inter cooler |
| C9.5.1 | Make |
| C9.5.2 | Identification No / Part No./ Drawing No. |
| C9.5.3 | Air pressure drop across the inter-cooler |
| C10.0 | Fuel feed: (By carburetor) |
| C10.1 | Number |
| C10.2 | Make |
| C10.3 | Type |

Table 4B of AIS-007 (Revision 5)

| C10.4 | Adjustments (specify tolerance) |
| --- | --- |
| C10.4.1 | Jets |
| C10.4.2 | Venturies |
| C10.4.3 | Float-chamber level |
| C10.4.4 | Mass of float |
| C10.4.5 | Float needle |
| C10.5 | Dimensions of mixture duct |
| C10.6 | Choke: Type (Manual/automatic) and closure setting |
| C10.7 | Feed pump |
| C10.7.1 | Pressure (specify tolerance) or characteristic diagrams |
| C10.7.2 | Type of fuel feed pump |
| C11.0 | Fuel feed: {By fuel injection} |
| C11.1 | Injection system description |
| C11.2 | Working principle: intake manifold/ direct injection / indirect injection / swirl chamber/others |
| C11.3 | Fuel Pump |
| C11.3.1 | Make(s) |
| C11.3.2 | Type(s) |
| C11.3.3 | Pressure / characteristic diagram |
| C11.4 | Delivery mm3/ per stroke at max net power speed in case of Diesel Engine & specify delivery in kg/h at max net power speed in case of gas engines (specify tolerance) and enclose characteristic diagram (specify tolerance). If boost control is supplied, state the characteristics fuel delivery and boost pressure versus engine speed. |
| C11.5 | Calibration Method (on engine/pump bench) |
| C11.6 | Static Injection timing |
| C11.7 | Injection advance curve (Diagram be enclosed) |
| C11.8 | Injection advance (specify the tolerance) |
| C11.9 | Injector (s) |
| C11.9.1 | Type (s) (mention holder, nozzle and assembly no(s)) |
| C11.9.2 | Make (s) |
| C11.9.3 | Opening pressure (specify tolerance) or characteristic diagram |
| C11.9.4 | Injection piping |
| C11.9.4.1 | Length mm |
| C11.9.4.2 | Internal diameter mm |
| C 12.0 | Device for recycling crank-case gases |
| C 12.1 | Description & drawings |

Table 4B of AIS-007 (Revision 5)

| C13.0 | Governor |
| --- | --- |
| C13.1 | Make(s) |
| C13.2 | Type(s) |
| C13.3 | Speed at which Cut off starts under load (rev/min) |
| C13.4 | Max. speed without load (rev/min) |
| C13.5 | Idle Speed (rev/min) |
| C14.0 | Cold start device (starting aid) |
| C14.1 | Make |
| C14.2 | Type(s) |
| C14.3 | System description |
| C15.0 | Starting System : |
| C15.1 | Make |
| C15.2 | Type(s) |
| C15.3 | System description |
| C16.0 | Valve timing / Port timing or equivalent data |
| C16.1 | Max. lift of valves |
| C16.1.1 | Inlet mm |
| C16.1.2 | Exhaust mm |
| C16.2 | Angle of valves / port (w.r.t. top dead center) |
| C16.3 | Inlet |
| C16.3.1 | Opening |
| C16.3.2 | Closing |
| C16.4 | Exhaust |
| C16.4.1 | Opening |
| C16.4.2 | Closing |
| C16.5 | Transfer |
| C16.5.1 | Opening |
| C16.5.2 | Closing |
| C16.6 | Reference or setting ranges |
| C16.7 | Valve gap (Hot or Cold as applicable) |
| C16.7.1 | Inlet |
| C16.7.2 | Exhaust |
| C16.8 | Distribution by ports |
| C16.8.1 | Volume of crank-case cavity with piston at TDC |
| C16.8.2 | Reed valve fitted ( Yes / No ) |
| C16.8.3 | Description of inlet ports, scavenging and exhaust ports with corresponding timing. |

Table 4B of AIS-007 (Revision 5)

| C17.0 | Lubrication system |
| --- | --- |
| C17.1 | Description of system |
| C17.2 | Lubrication oil capacity lit |
| C17.3 | Position of lubricant reservoir |
| C17.4 | Lubricating oil grade |
| C17.5 | Feed system (pump, injection in to intake mixing with fuel etc.,) |
| C17.6 | Lubricating pump |
| C17.6.1 | Make |
| C17.6.2 | Type |
| C17.7 | Mixture with fuel: yes/no, and if yes % ( for 2 stroke engines ) |
| C17.8 | Oil cooler : yes/no, and if yes Enclose dimensional drawings, make(s) & type(s) |
| C18.0 | Electrical equipment |
| C18.1 | Generator/alternator characteristics (specify tolerance) or |
| C18.1.1 | Make |
| C18.1.2 | Type |
| C18.1.3 | Identification No / Part No./ Drawing No. |
| C19.0 | Other engine driven auxiliaries |
| C19.1 | Enumeration & brief description, if necessary |
| C20.0 | Idling System: |
| C20.1 | Idling speed (rpm) (specify the tolerance) |
| C20.2 | Description of settings and relevant requirements |
| C20.3 | Carbon monoxide and HC content by volume in the exhaust gas with the engine idling, per cent (for SI engines only) (manufacturer’s standard) |
| C20.4 | High Idle (2500 ± 200 rpm) Lambda value(For petrol driven four wheeled vehicles only) (1± 0.03 or as specified by the vehicle manufacturer) |
| C 21.0 | Requirements for engine test |
| C21.1 | Maximum permitted depression of air intake at characteristic place in kPa (Specify location of measurement)) |
| C21.2 | Exhaust back pressure at maximum net power and location of measurement (kPa) |
| C21.3 | Effective volume of exhaust-system (specify the tolerance & range) in liters (from exhaust manifold / TC outlet to tail pipe end), Enclose the exhaust system dimensional drawing and indicate the volume of each parts clearly. |
| C21.4 | Moment of inertia of combined flywheel & transmission at condition when no gear is engaged |
| C21.5 | Maximum rated speed (Specify the tolerance) |
| C21.6 | Minimum rated speed (Specify the tolerance) |
| C21.7 | Max. Net Torque on bench ……. Nm at ……..rpm ( specify tolerance ) |
| C21.8 | Max. net Power on bench, ……. Nm at ……..rpm ( specify tolerance ) |

Table 4B of AIS-007 (Revision 5)

| C21.9 | Engine Performance Declared speed and powers of the engine submitted for type approval) (Speeds to be agreed with the testing agency) |
| --- | --- |
| C21.9.1 | Engine Speeds (For ESC & ELR cycles) |
| C21.9.2 | Low Speed (nlo) (rpm) |
| C21.9.3 | High Speed (nhi) (rpm) |
| C21.9.4 | Speed A (rpm) |
| C21.9.5 | Speed B (rpm) |
| C21.9.6 | Speed C (rpm) |
| C21.9.7 | Engine Power Table Measurement point* Engine speed rpm New Power kW** (1) (2) (3) (4) (5) (6) * See Chapter 3 of Part IV of Doc. MoRTH/CMVR/TAP115/116 Issue No.4 ** Net power according to Chapter 6 of Part IV of Doc MoRTH/CMVR/TAP115/116 Issue No.4. Note: In case, if data regarding the Moment of Inertia, is required by the test agency for carrying out the Full Throttle performance test for both the CI / SI engines, the same shall be provided by the manufacturer. |
| C22.0 | Exhaust system |
| C22.1 | Silencer |
| C22.1.1 | Type |
| C22.1.2 | Make |
| C22.1.3 | Number |
| C22.1.4 | Silencer identification No. (if proprietary) / Part No. (if not proprietary) |
| C22.2 | Internal diameter of exhaust pipe (mm) |
| C22.3 | Description with general arrangement of exhaust system along with its routing indicating the lengths of exhaust pipe, tail pipe and exhaust outlet location, indicated in a Schematic dimensional drawing. |
| C22.4 | Minimum distance between exhaust pipe(s) and the fuel line |

Table 4B of AIS-007 (Revision 5)

| C23.0 | Additional emission control devices, such as catalytic converter etc. (if any & if not covered by another heading) |
| --- | --- |
| C23.1 | Catalyser make, number |
| C23.2 | Identification Mark / Part No. / Drawing No. |
| C23.3 | Type of catalytic action (One/two/three way) |
| C23.4 | Total charge of precious metal (g/vehicle) |
| C23.5 | Relative concentration (%) |
| C23.5.1 | Platinum |
| C23.5.2 | Rhodium |
| C23.5.3 | Palladium |
| C23.6 | Substrate (Monolythic metal/ Ceramic/ honeycomb) |
| C23.6.1 | Cell density (cells per sq. inch / cm) |
| C23.7 | Type of casing for catalyser |
| C23.8 | Diagram indicating the arrangement and position of catalytic converter w.r.t. exhaust manifold) |
| C23.9 | Lamda Sensor |
| C23.9.1 | Make |
| C23.9.2 | Type / Part No. |
| C23.9.3 | Identification No. / Part No. / Drawing No. |
| C23.9.4 | Location |
| C 23.10 | Regeneration systems/method of exhaust after-treatment systems, description: |
| C 23.10.1 | The number of Type I operating cycles, or equivalent engine test bench cycles, between two cycles where regenerative phases occur under the conditions equivalent to Type I test (Distance "D" in figure 1 in Chapter 15 of TAP Document) : |
| C 23.10.2 | Description of method employed to determine the number of cycles between two cycles where regenerative phases occur: |
| C23.10.3 | Parameters to determine the level of loading required before regeneration occurs (i.e. temperature, pressure etc.): |
| C23.10.4 | Description of method used to load system in the test procedure described in paragraph 3.1., ( Refer Chapter 15 of TAP Document) : |
| C 23.11 | Oxygen sensor: type |
| C 23.11.1 | Location of oxygen sensor: |
| C23.11.2 | Control range of oxygen sensor: |
| C 23.11.3 | Regeneration system/method - Description and drawing: |

Table 4B of AIS-007 (Revision 5)

| C23.12 | Electronic Control Unit (ECU) |
| --- | --- |
| C23.12.1 | Make |
| C23.12.2 | Identification mark |
| C23.12.3 | Calibration Identification No. |
| C23.12.4 | Adjustment possibilities ( Yes / No ) |
| C23.13 | Secondary Air Injection |
| C23.13.1 | Make |
| C23.13.2 | Identification mark |
| C23.14 | Exhaust Gas Re-circulating System |
| C23.14.1 | Brief description of the system |
| C23.14.2 | Type ( Cooled / Non-cooled/Progressive/ On-Off/ Any Other ) |
| C23.14.3 | EGR Valve |
| C23.14.3.1 | Make |
| C23.14.3.2 | Type |
| C23.14.3.3 | Identification No / Part No. / Drawing No. |
| C23.14.4 | EGR Electronic Control Unit |
| C23.14.4.1 | Make |
| C23.14.4.2 | Identification No. / Part No. / Drawing No. |
| C24.0 | Additional information for evaporative emission |
| C24.1 | Evaporative emission control system |
| C24.2 | Type |
| C24.3 | Make |
| C24.4 | Complete detailed description of devices and their state of tune |
| C24.5 | Drawing of the evaporative control system |
| C24.6 | Drawing of the fuel tank with indication of capacity and material |
| C24.7 | Canister |
| C24.7.1 | Working capacity |
| C24.7.2 | Make |
| C24.7.3 | Identification No. / Part No. / Drawing No. |
| C24.7.4 | Schematic diagram |
| C24.7.5 | Canister bed volume (1) |

Table 4B of AIS-007 (Revision 5)

| C 25.0 | On Board Diagnosis (OBD ) |
| --- | --- |
| C 25.1 | Written description and/or drawing of the Malfunction Indicator (MI). |
| C 25.2 | List and purpose of all components monitored by the OBD system. |
| C 25.3 | Written description (general working principles) for ; |
| C 25.3.1 | Positive-ignition engines. |
| C 25.3.1.1 | Catalyst monitoring |
| C 25.3.1.2 | Misfire detection |
| C 25.3.1.3 | Oxygen sensor monitoring |
| C 25.3.1.4 | Other components monitored by the OBD system |
| C 25.3.2 | Compression-ignition engines |
| C 25.3.2.1 | Catalyst monitoring |
| C 25.3.2.2 | Particulate trap monitoring |
| C 25.3.2.3 | Electronic fuelling system monitoring |
| C 25.3.2.4 | deNox system monitoring |
| C 25.3.2.5 | Other components monitored by the OBD system |
| C 25.4 | Criteria for MI activation (fixed number of driving cycles or statistical method) |
| C 25.5 | List of all OBD output codes and formats used (with explanation of each). |
| C 25.6 | The following additional information shall be provided by the vehicle manufacturer for the purposes of enabling the manufacture of OBD-compatible replacement or service parts and diagnostic tools and test equipment, unless such information is covered by intellectual property rights or constitutes specific know-how of the manufacturer or the OEM supplier(s). |
| C 25.6.1 | A description of the type and number of the pre-conditioning cycles used for the original type approval of the vehicle. |
| C 25.6.2 | A description of the type of the OBD demonstration cycle used for the original type-approval of the vehicle for the component monitored by the OBD system. |

Table 4B of AIS-007 (Revision 5)

| C 25.6.3 | A comprehensive document describing all sensed components with the strategy for fault detection and MI activation (fixed number of driving cycles or statistical method), including a list of relevant secondary sensed parameters for each component monitored by the OBD system. A list of all OBD output codes and format used (with an explanation of each) associated with individual emission related power-train components and individual non-emission related components, where monitoring of the component is used to determine MI activation. In particular, a comprehensive explanation for the data given in service $05 Test ID $21 to FF and the data given in service $06 must be provided. In the case of vehicle types that use a communication link in accordance with ISO 15765-4 “Road vehicles, diagnostics on controller area network (CAN) – part 4: requirements for emissions-related systems”, a comprehensive explanation for the data given in service $06 Test ID $00 to FF, for each OBD monitor ID supported, must be provided. This information may be defined in the form of a table, as follows: Component Fault code Monitoring strategy MI activation criteria Secondary parameters Pre-condit-ioning Demonstr- ation test Catalyst P0420 Oxygen sensor 1 and 2 signals 3rd cycle Engine speed, engine load, A/F mode, catalyst temperature Two type 1 cycles Type 1’ |
| --- | --- |
| C 25.7 | Torque limiter (yes/No) (for vehicles with GVW above 3500 kg) |
| C25.7.1 | Description of the torque limiter activation |
| C25.7.2 | Description of the full load curve limitation |
| C 26.0 | Particulate trap ( Yes / No) |
| C 26.1 | Dimensions and shape of the particulate trap (capacity): |
| C 26.2 | Type of particulate trap and design: |
| C 26.3 | Location of the particulate trap (reference distances in the exhaust system): |
| C 26.4 | Regeneration system/method - Description and Drawing: |
| C 26.4.1 | The number of Type I operating cycles, or equivalent engine test bench cycle, between two cycles where regeneration phases occur under the conditions equivalent to Type I test (Distance 'D' in figure 1 in Chapter 15 of TAP Document) : |
| C 26.4.2 | Description of method employed to determine the number of cycles between two cycles where regenerative phases occur: |
| C 26.4.3 | Parameters to determine the level of loading required before regeneration occurs (i.e. temperature, pressure, etc.): |
| C 26.4.4 | Description of method used to load system in the test procedure described in paragraph 3.1., Chapter 15 of TAP Document : |

| Table 4C of AIS-007 (Revision 5) TECHNICAL SPECIFICATION-FOUR WHEELERS AND ABOVE PART C - Technical Specification for the individual Engine of the Engine family fitted on vehicles with GVW greater than 3500 kg |
| --- |
| Clause No. | Description |
| C1.0 | Description of Engine: |
| C1.1 | Type (Compression Ignition / Positive Ignition) |
| C1.2 | Make |
| C1.3 | Name and address of the engine manufacturing plant |
| C1.4 | Working principle: (Four / two stroke), (DI / IDI ) (NA/TC/TCIC/ Any other ) |
| C1.5 | Model name and identification |
| C1.6 | Type of fuel used |
| C1.7 | No.& Layout of cylinders & firing order |
| C1.8 | Swept volume cc |
| C1.9 | Bore (mm) |
| C1.10 | Stroke (mm) |
| C1.11 | Compression ratio (specify tolerance) |
| C1.12 | Engine performance (declared by the manufacturer): |
| C1.12.1 | Max. Net power of engine on bench (kW @ rpm)(Specify standard and tolerance) |
| C1.12.2 | Maximum net torque on bench (Nm @ rpm) Note : In case of diesel engines the max. Power and max. Torque shall be specified as per conditions given in Chapter 6 of Part IV of Doc. MoRTH / CMVR / TAP-115 / 116 Issue No.3 |
| C1.13 | Location of engine (Front / Rear) |
| C2.0 | Combustion System: |
| C2.1 | Type of combustion chamber (Hemispherical/ squish/others) |
| C2.2 | Drawing(s) of combustion chamber and piston crown (Enclose the drawing & Mention the drawing no. & Part no.) |
| C2.3 | Minimum cross section area of ports |
| C2.3.1 | Inlet (cm2) |
| C2.3.2 | Outlet (cm2) |
| C3.0 | Ignition System (Spark Ignition engines only): |
| C3.1 | Make |
| C3.2 | Type |
| C3.3 | Nominal Voltage |
| C3.4 | Operating Principle |
| C3.5 | CDI |

Table 4C of AIS-007 (Revision 5)

| C3.6 | Table of Combination for EMI test |
| --- | --- |
| C3.7 | Ignition advance curve (specify tolerance) & enclose the curve |
| C3.8 | Ignition timing (specify tolerance) |
| C3.9 | Contact point gap and dwell angle (specify tolerance) |
| C3.10 | Type and make of distributor |
| C3.11 | Sparking plugs |
| C3.11.1 | Make |
| C3.11.2 | Type and designation |
| C3.11.3 | Spark-gap setting |
| C3.11.4 | Nominal resistance (kilo ohm) (if resistive type) |
| C3.12 | Ignition coil |
| C3.12.1 | Make |
| C3.12.2 | Type |
| C3.12.3 | Identification |
| C3.13 | Ignition condenser |
| C3.13.1 | Make |
| C3.13.2 | Type |
| C3.13.3 | Identification |
| C3.14 | EMI suppressor cap / Device / Electronic unit |
| C3.14.1 | Make |
| C3.14.2 | Type (Resistive/Capacitive) |
| C3.14.3 | identification |
| C3.14.4 | Nominal resistance (kilo ohm) |
| C3.14.5 | Terminology and Drawing of interference Suppression equipment |
| C3.15 | H.T.Cable |
| C3.15.1 | Make and Place / |
| C3.15.2 | Type (Resistive/Non-resistive) |
| C3.15.3 | Length mm (if resistive type) |
| C3.15.4 | Outside dia. mm (if resistive type) |
| C3.15.5 | Nominal resistance kilo ohm, (if resistive type) |
| C3.16 | Systems incorporating electronic oscillator with an operating frequency greater than 9 kHz |

Table 4C of AIS-007 (Revision 5)

| C4.0 | Cooling system : |
| --- | --- |
| C4.1 | Liquid cooling system |
| C4.1.1 | Nature of liquid and capacity |
| C4.1.2 | Circulating pump yes/no |
| C4.1.3 | Characteristics of Circulating pump or make(s) & type(s) |
| C4.1.3.1 | Drive ratio |
| C4.1.4 | Thermostat type and setting |
| C4.1.5 | Radiator drawing(s) |
| C4.1.5.1 | Make(s) and Place |
| C4.1.5.2 | Type(s) |
| C4.1.5.3 | Relief valve pressure setting |
| C4.1.6 | Fan characteristics (Fan power, kW) Enclose the fan power curve corresponding to full load (v/s engine speed) of viscous fan. |
| C4.1.6.1 | Make(s) |
| C4.1.6.1.1 | No. of blades |
| C4.1.6.1.2 | Material of blades ( metal / plastic ) |
| C4.1.6.2 | Type(s) [Fixed / Viscous / Electrical driven] |
| C4.1.6.3 | Fan drive system |
| C4.1.6.4 | Drive ratio |
| C4.1.6.5 | Fan cowl |
| C4.1.6.6 | Fan diameter (mm) |
| C4.1.6.7 | Max. Speed of fan (in rev/min) |
| C4.1.7 | Radiator core open area (cm²) |
| C4.2 | Air Cooling system |
| C4.2.1 | Blower characteristics |
| C4.2.1.1 | Make |
| C4.2.1.2 | Type(s) |
| C4.2.1.3 | Drive ratio(s) |
| C4.2.2 | Air ducting (std production) |
| C5.0 | Temperature permitted by manufacturer in 0C for liquid cooling (Location of measurement be specified) |
| C5.1 | Max. temp. at engine outlet |
| C6.0 | Temperature permitted by manufacturer in 0C for Air cooling (Location of measurement be specified ) |
| C6.1 | Reference point |

Table 4C of AIS-007 (Revision 5)

| C6.2 | Max. temperature at reference point |
| --- | --- |
| C6.3 | Max. Temperature of the intercooled-air (Location of measurement be specified) |
| C6.4 | Max. Exhaust temperature (in case of diesel engines, at the point in the exhaust pipe(s) adjacent in outlet flange(s) of exhaust manifolds), Specify the distance from the outlet flange. |
| C7.0 | Fuel temperature 0C: (for diesel engines at the injection pump inlet) |
| C7.1 | Minimum |
| C7.2 | Maximum |
| C8.0 | Lubricant Temperature 0C (Location of measurement be specified ) |
| C8.1 | Minimum |
| C8.2 | Maximum |
| C9.0 | Intake system : (Attach drawing, mention Drawing No. & Part No.) |
| C9.1 | Supercharger / Turbocharger - yes/no |
| C9.1.1 | Description of system |
| C9.1.2 | Make(s) |
| C9.1.3 | Type(s) and Part no. |
| C9.1.4 | Description of system (e.g. Charge pressure @ max. power and torque speed, waste gate, if applicable) |
| C9.2 | Intake manifold (Enclose drawing with drawing No. & Part No.) |
| C9.2.1 | Description |
| C9.2.2 | Identification No / Part No. |
| C9.2.3 | Schematic dimensional drawing |
| C9.3 | Air filter |
| C9.3.1 | Make |
| C9.3.2 | Type |
| C9.3.3 | Identification No / Part No./ Drawing No. |
| C9.3.4 | Schematic dimensional drawing |
| C9.4 | Intake silencer |
| C9.4.1 | Make |
| C9.4.2 | Type / Description |
| C9.4.3 | Identification No / Part No./ Drawing No. |
| C9.4.4 | Schematic dimensional drawing of inlet pipe and their accessories (dash pot, heating devices, additional air intake etc.) |

Table 4C of AIS-007 (Revision 5)

| C9.5 | Inter cooler |
| --- | --- |
| C9.5.1 | Make |
| C9.5.2 | Identification No / Part No./ Drawing No. |
| C9.5.3 | Air pressure drop across the inter-cooler |
| C10.0 | Fuel feed: (By carburetor) |
| C10.1 | Number |
| C10.2 | Make |
| C10.3 | Type |
| C10.4 | Adjustments (specify tolerance) |
| C10.4.1 | Jets |
| C10.4.2 | Venturies |
| C10.4.3 | Float-chamber level |
| C10.4.4 | Mass of float |
| C10.4.5 | Float needle |
| C10.5 | Dimensions of mixture duct |
| C10.6 | Choke: Type (Manual/automatic) and closure setting |
| C10.7 | Feed pump |
| C10.7.1 | Pressure (specify tolerance) or characteristic diagrams |
| C10.7.2 | Type of fuel feed pump |
| C11.0 | Fuel feed: {By fuel injection} |
| C11.1 | Injection system description |
| C11.2 | Working principle: intake manifold/ direct injection / indirect injection / swirl chamber/others |
| C11.3 | Fuel Pump |
| C11.3.1 | Make(s) |
| C11.3.2 | Type(s) and Part no. |
| C11.3.3 | Pressure / characteristic diagram |
| C11.4 | Delivery mm3/ per stroke at max net power speed in case of Diesel Engine & specify delivery in kg/h at max net power speed in case of gas engines (specify tolerance) and enclose characteristic diagram (specify tolerance). If boost control is supplied, state the characteristics fuel delivery and boost pressure versus engine speed. |
| C11.5 | Calibration Method (on engine/pump bench) |
| C11.6 | Static Injection timing |
| C11.7 | Injection advance curve (Diagram be enclosed) |
| C11.8 | Injection advance (specify the tolerance) |

Table 4C of AIS-007 (Revision 5)

| C11.9 | Injector (s) |
| --- | --- |
| C11.9.1 | Type (s) (mention holder, nozzle and assembly no(s)) |
| C11.9.2 | Make (s) |
| C11.9.3 | Opening pressure (specify tolerance) or characteristic diagram |
| C11.9.4 | Injection piping |
| C11.9.4.1 | Length mm |
| C11.9.4.2 | Internal diameter mm |
| C 12.0 | Device for recycling crank-case gases |
| C12.1 | Description & drawings |
| C13.0 | Governor |
| C13.1 | Make(s) |
| C13.2 | Type(s) |
| C13.3 | Speed at which Cut off starts under load (rev/min) |
| C13.4 | Max. speed without load (rev/min) |
| C13.5 | Idle Speed (rev/min) |
| C14.0 | Cold start device (starting aid) |
| C14.1 | Make |
| C14.2 | Type(s) |
| C14.3 | System description |
| C15.0 | Starting System : |
| C15.1 | Make |
| C15.2 | Type(s) |
| C15.3 | System description |
| C16.0 | Valve timing / Port timing or equivalent data |
| C16.1 | Max. lift of valves |
| C16.1.1 | Inlet mm |
| C16.1.2 | Exhaust mm |
| C16.2 | Angle of valves / port (w.r.t. top dead center) |
| C16.3 | Inlet |
| C16.3.1 | Opening |
| C16.3.2 | Closing |
| C16.4 | Exhaust |
| C16.4.1 | Opening |
| C16.4.2 | Closing |
| C16.5 | Transfer |
| C16.5.1 | Opening |
| C16.5.2 | Closing |
| C16.6 | Reference or setting ranges |

Table 4C of AIS-007 (Revision 5)

| C16.7 | Valve gap (Hot or Cold as applicable) |
| --- | --- |
| C16.7.1 | Inlet |
| C16.7.2 | Exhaust |
| C16.8 | Distribution by ports |
| C16.8.1 | Volume of crank-case cavity with piston at TDC |
| C16.8.2 | Reed valve fitted ( Yes / No ) |
| C16.8.3 | Description of inlet ports, scavenging and exhaust ports with corresponding timing. |
| C17.0 | Lubrication system |
| C17.1 | Description of system |
| C17.2 | Lubrication oil capacity lit |
| C17.3 | Position of lubricant reservoir |
| C17.4 | Lubricating oil grade |
| C17.5 | Feed system (pump, injection in to intake mixing with fuel etc.,) |
| C17.6 | Lubricating pump |
| C17.6.1 | Make |
| C17.6.2 | Type |
| C17.7 | Mixture with fuel: yes/no, and if yes % ( for 2 stroke engines ) |
| C17.8 | Oil cooler : yes/no, and if yes Enclose dimensional drawings, make(s) & type(s) |
| C18.0 | Electrical equipment |
| C18.1 | Generator/alternator characteristics (specify tolerance) or |
| C18.1.1 | Make |
| C18.1.2 | Type |
| C18.1.3 | Identification No / Part No./ Drawing No. |
| C19.0 | Other engine driven auxiliaries |
| C19.1 | Enumeration & brief description, if necessary |
| C20.0 | Idling System: |
| C20.1 | Idling speed (rpm) (specify the tolerance) |
| C20.2 | Description of settings and relevant requirements |
| C20.3 | Carbon monoxide and HC content by volume in the exhaust gas with the engine idling, per cent (for SI engines only) (manufacturer’s standard) |
| C20.4 | High Idle (2500 ± 200 rpm) Lambda value(For petrol driven four wheeled vehicles only) (1± 0.03 or as specified by the vehicle manufacturer) |

Table 4C of AIS-007 (Revision 5)

| C21.0 | Requirements for engine test |
| --- | --- |
| C21.1 | Maximum permitted depression of air intake at characteristic place in kPa (Specify location of measurement)) |
| C21.2 | Exhaust back pressure at maximum net power and location of measurement (kPa) |
| C21.3 | Effective volume of exhaust-system (specify the tolerance & range) in liters (from exhaust manifold / TC outlet to tail pipe end), Enclose the exhaust system dimensional drawing and indicate the volume of each parts clearly. |
| C21.4 | Moment of inertia of combined flywheel & transmission at condition when no gear is engaged |
| C21.5 | Maximum rated speed (Specify the tolerance) |
| C21.6 | Minimum rated speed (Specify the tolerance) |
| C21.7 | Max. Net Torque on bench ……. Nm at ……..rpm ( specify tolerance ) |
| C21.8 | Max. net Power on bench, ……. Nm at ……..rpm ( specify tolerance ) |
| C21.9 | Engine Performance Declared speed and powers of the engine submitted for type approval) (Speeds to be agreed with the testing agency) |
| C21.9.1 | Engine Speeds (For ESC & ELR cycles) |
| C21.9.2 | Low Speed (nlo) (rpm) |
| C21.9.3 | High Speed (nhi) (rpm) |
| C21.9.4 | Speed A (rpm) |
| C21.9.5 | Speed B (rpm) |
| C21.9.6 | Speed C (rpm) |
| C21.9.7 | Engine Power Table Measurement point* Engine speed rpm New Power kW** (1) (2) (3) (4) (5) (6) * See Chapter 3 of Part IV of Doc. MoRTH/CMVR/TAP115/116 Issue No.4 ** Net power according to Chapter 6 of Part IV of Doc. MoRTH/CMVR/TAP115/116 Issue No.4. Note: In case, if data regarding the Moment of Inertia, is required by the test agency for carrying out the Full Throttle performance test for both the CI / SI engines, the same shall be provided by the manufacturer. |

Table 4C of AIS-007 (Revision 5)

| C22.0 | Exhaust system |
| --- | --- |
| C22.1 | Silencer |
| C22.1.1 | Type |
| C22.1.2 | Make |
| C22.1.3 | Number |
| C22.1.4 | Silencer identification No. (if proprietary) / Part No. (if not proprietary) |
| C22.2 | Internal diameter of exhaust pipe (mm) |
| C22.3 | Description with general arrangement of exhaust system along with its routing indicating the lengths of exhaust pipe, tail pipe and exhaust outlet location, indicated in a Schematic dimensional drawing. |
| C22.4 | Minimum distance between exhaust pipe(s) and the fuel line |
| C23.0 | Additional emission control devices, such as catalytic converter etc. (if any & if not covered by another heading) |
| C23.1 | Catalyser make, number |
| C23.2 | Identification Mark / Part No. |
| C23.3 | Type of catalytic action (One/two/three way) |
| C23.4 | Total charge of precious metal (g/vehicle) |
| C23.5 | Relative concentration (%) |
| C23.5.1 | Platinum |
| C23.5.2 | Rhodium |
| C23.5.3 | Palladium |
| C23.6 | Substrate (Monolythic metal/ Ceramic/ honeycomb) |
| C23.6.1 | Cell density (cells per sq. inch / cm) |
| C23.7 | Type of casing for catalyser |
| C23.8 | Diagram indicating the arrangement and position of catalytic converter w.r.t. exhaust manifold) |
| C23.9 | Lamda Sensor |
| C23.9.1 | Make |
| C23.9.2 | Type / Part No. |
| C23.9.3 | Identification No. / Part No. |
| C23.9.4 | Location |

Table 4C of AIS-007 (Revision 5)

| C 23.10 | Regeneration systems/method of exhaust after-treatment systems, description: |
| --- | --- |
| C 23.10.1 | The number of Type I operating cycles, or equivalent engine test bench cycles, between two cycles where regenerative phases occur under the conditions equivalent to Type I test (Distance "D" in figure 1 in Chapter 15 of TAP Document) : |
| C 23.10.2 | Description of method employed to determine the number of cycles between two cycles where regenerative phases occur: |
| C23.10.3 | Parameters to determine the level of loading required before regeneration occurs (i.e. temperature, pressure etc.): |
| C23.10.4 | Description of method used to load system in the test procedure described in paragraph 3.1., ( Refer Chapter 15 of TAP Document) : |
| C 23.11 | Oxygen sensor: type |
| C 23.11.1 | Location of oxygen sensor: |
| C23.11.2 | Control range of oxygen sensor: |
| C 23.11.3 | Regeneration system/method - Description and drawing: |
| C23.12 | Electronic Control Unit (ECU) |
| C23.12.1 | Make |
| C23.12.2 | Identification mark |
| C23.12.3 | Calibration Identification No. |
| C23.12.4 | Adjustment possibilities ( Yes / No ) |
| C23.13 | Secondary Air Injection |
| C23.13.1 | Make |
| C23.13.2 | Identification mark |
| C23.14 | Exhaust Gas Recirculating System |
| C23.14.1 | Brief description of the system |
| C23.14.2 | Type ( Cooled / Non-cooled/Progressive/ On-Off/ Any Other ) |
| C23.14.3 | EGR Valve |
| C23.14.3.1 | Make |
| C23.14.3.2 | Type |
| C23.14.3.3 | Identification No / Part No./ Drawing No. |
| C23.14.4 | EGR Electronic Control Unit |
| C23.14.4.1 | Make |
| C23.14.4.2 | Identification No / Part No./ Drawing No. |

Table 4C of AIS-007 (Revision 5)

| C24.0 | Additional information for evaporative emission |
| --- | --- |
| C24.1 | Evaporative emission control system |
| C24.2 | Type |
| C24.3 | Make |
| C24.4 | Complete detailed description of devices and their state of tune |
| C24.5 | Drawing of the evaporative control system |
| C24.6 | Drawing of the fuel tank with indication of capacity and material |
| C24.7 | Canister |
| C24.7.1 | Working capacity |
| C24.7.2 | Make |
| C24.7.3 | Identification No / Part No./ Drawing No. |
| C24.7.4 | Schematic diagram |
| C24.7.5 | Canister bed volume (1) |
| C 25.0 | On Board Diagnosis (OBD ) |
| C 25.1 | Written description and/or drawing of the Malfunction Indicator(MI). |
| C 25.2 | List and purpose of all components monitored by the OBD system. |
| C 25.3 | Written description (general working principles) for ; |
| C 25.3.1 | Positive-ignition engines. |
| C 25.3.1.1 | Catalyst monitoring |
| C 25.3.1.2 | Misfire detection |
| C 25.3.1.3 | Oxygen sensor monitoring |
| C 25.3.1.4 | Other components monitored by the OBD system |
| C 25.3.2 | Compression-ignition engines |
| C 25.3.2.1 | (Catalyst monitoring) |
| C 25.3.2.2 | Particulate trap monitoring |
| C 25.3.2.3 | Electronic fuelling system monitoring |
| C 25.3.2.4 | deNox system monitoring |
| C 25.3.2.5 | Other components monitored by the OBD system |
| C 25.4 | Criteria for MI activation (fixed number of driving cycles or statistical method) |

Table 4C of AIS-007 (Revision 5)

| C 25.5 | List of all OBD output codes and formats used (with explanation of each). |
| --- | --- |
| C 25.6 | The following additional information shall be provided by the vehicle manufacturer for the purposes of enabling the manufacture of OBD-compatible replacement or service parts and diagnostic tools and test equipment, unless such information is covered by intellectual property rights or constitutes specific know-how of the manufacturer or the OEM supplier(s). |
| C 25.6.1 | A description of the type and number of the pre-conditioning cycles used for the original type approval of the vehicle. |
| C 25.6.2 | A description of the type of the OBD demonstration cycle used for the original type-approval of the vehicle for the component monitored by the OBD system. |
| C 25.6.3 | A comprehensive document describing all sensed components with the strategy for fault detection and MI activation (fixed number of driving cycles or statistical method), including a list of relevant secondary sensed parameters for each component monitored by the OBD system. A list of all OBD output codes and format used (with an explanation of each) associated with individual emission related power-train components and individual non-emission related components, where monitoring of the component is used to determine MI activation. In particular, a comprehensive explanation for the data given in service $05 Test ID $21 to FF and the data given in service $06 must be provided. In the case of vehicle types that use a communication link in accordance with ISO 15765-4 “Road vehicles, diagnostics on controller area network (CAN) – part 4: requirements for emissions-related systems”, a comprehensive explanation for the data given in service $06 Test ID $00 to FF, for each OBD monitor ID supported, must be provided. This information may be defined in the form of a table, as follows: Component Fault code Monitoring strategy MI activation criteria Secondary parameters Pre-condit-ioning Demonstr- ation test Catalyst P0420 Oxygen sensor 1 and 2 signals 3rd cycle Engine speed, engine load, A/F mode, catalyst temperature Two type 1 cycles Type 1’ |
| C 25.7 | Torque limiter (yes/No) |
| C25.7.1 | Description of the torque limiter activation |
| C25.7.2 | Description of the full load curve limitation |

Table 4C of AIS-007 (Revision 5)

| C 26.0 | Particulate trap ( Yes / No) |
| --- | --- |
| C 26.1 | Dimensions and shape of the particulate trap (capacity): |
| C 26.2 | Type of particulate trap and design: |
| C 26.3 | Location of the particulate trap (reference distances in the exhaust system): |
| C 26.4 | Regeneration system/method - Description and Drawing: |
| C 26.4.1 | The number of Type I operating cycles, or equivalent engine test bench cycle, between two cycles where regeneration phases occur under the conditions equivalent to Type I test (Distance 'D' in figure 1 in Chapter 15 of TAP Document) : |
| C 26.4.2 | Description of method employed to determine the number of cycles between two cycles where regenerative phases occur: |
| C 26.4.3 | Parameters to determine the level of loading required before regeneration occurs (i.e. temperature, pressure, etc.): |
| C 26.4.4 | Description of method used to load system in the test procedure described in paragraph 3.1., Chapter 15 of TAP Document : |

Table-4D of AIS-007 (Revision 5)

Technical Specifications of the Engines fitted on Agricultural Tractors

| 1.0 | Description of Vehicle |  |
| --- | --- | --- |
| 1.1 | Trade Name or mark of the Vehicle |  |
| 1.2 | Vehicle Type |  |
| 1.3 | Declared maximum PTO Power (kW) |  |
| 1.4 | Declared Rated PTO power (kW) |  |
| 1.5 | CFMTTI Test report no. |  |
| 2.0 | Manufacturer’s name and address |  |
| 2.1 | Telephone No. |  |
| 2.2 | Fax No. |  |
| 2.3 | Email |  |
| 3.0 | Brief Details of Agricultural Tractor |  |
| 3.1 | Unladen mass of vehicle (kN) |  |
| 3.2 | Reference mass of the vehicle |  |
| 3.3 | Gross vehicle Weight |  |
| 3.4 | Gear Box |  |
| 3.5 | Manual or Automatic (If it is automatic, give all the pertinent data) |  |
| 3.6 | Number of Gears |  |
| 3.7 | Transmission Ratio |  |
| 3.7.1 | First Gear |  |
| 3.7.2 | Second Gear |  |
| 3.7.3 | Third Gear |  |
| 3.7.4 | Fourth Gear |  |
| 3.7.5 | Overdrive |  |
| 3.8 | Gear Shifting Pattern |  |
| 3.9 | Final Drive Ratio |  |
| 3.10 | Tyre |  |
| 3.10.1 | Dimensions |  |
| 3.10.2 | Dynamic Rolling Circumference |  |
| 3.10.3 | Type |  |
| 3.10.4 | Ply Rating |  |
| 3.10.5 | Tyre Pressure |  |
| 3.10.5.1 | Front |  |

Table-4D of AIS-007 (Revision 5)

| 3.10.5.2 | Rear |  |
| --- | --- | --- |
| 3.11 | Wheel Drive |  |
| 3.11.1 | Front |  |
| 3.11.2 | Rear |  |
| 3.12 | Vehicle Performance (Declared by Manufacturer) |  |
| 3.13 | Vehicle Max Speed |  |
| 3.14 | Acceleration (Max.) |  |
| 4.0 | Essential Characteristics of Engine Family |  |
| 4.1 | Common Parameters |  |
| 4.2 | Combustion Cycle |  |
| 4.3 | Cooling Medium |  |
| 4.4 | Method of Air Aspiration |  |
| 4.5 | Combustion chamber type / Design |  |
| 4.6 | Valve and porting – Configuration, size and number |  |
| 4.7 | Fuel System |  |
| 4.8 | Engine Management Systems |  |
| 4.9 | Proof of Identity pursuant to drawing number(s): |  |
| 4.9.1 | Charge cooling system |  |
| 4.9.2 | Exhaust gas Recirculation |  |
| 4.9.3 | Water Injection / Emulsion |  |
| 4.9.4 | Air Injection |  |
| 4.9.5 | Exhaust gas after treatment system |  |
| 4.10 | Proof of Identical (or lowest for the parent engine) ratio |  |
| 4.11 | System capacity / fuel delivery per stroke, pursuant to diagram number(s) |  |
| 5.0 | Engine Family Listing |  |
| 5.1 | Name of Engine family |  |

Table-4D of AIS-007 (Revision 5)

| 5.2 | Specifications of Engine within this family |  |
| --- | --- | --- |
| Engine Type |  |  |  |  | Parent Engine |
| No. of Cylinders |  |  |  |  |  |
| Rated Speed (rpm) |  |  |  |  |  |
| Rated gross power (kW) |  |  |  |  |  |
| Max torque speed (rpm) |  |  |  |  |  |
| Fuel delivery per stroke at rated speed (mm3) |  |  |  |  |  |
| Fuel delivery per stroke at Max Torque Speed (mm3) |  |  |  |  |  |
| Max Torque (Nm) |  |  |  |  |  |
| Low idle speed (rpm) |  |  |  |  |  |
| Cylinder displacement ( in % of parent engine) |  |  |  |  | 100 |
| 6.0 (A) | Engine (Type within the Family) |  |
| 6.1 | Type (NA/TC/TCIC, DI/IDI) |  |
| 6.2 | Manufacturer's name & Manufacturing Plant address. |  |
| 6.3 | Working principle (four / two stroke) |  |
| 6.4 | Model name and identification |  |
| 6.5 | Type of fuel used |  |
| 6.6 | No.& Layout of cylinders & firing order |  |
| 6.7 | Swept volume cc |  |
| 6.8 | Bore(mm) |  |
| 6.9 | Stroke (mm) |  |
| 6.10 | Compression ratio (specify tolerance) |  |
| 6.11 | Engine performance (declared by the manufacturer,) |  |
| 6.11.1 | Max. Gross power of engine on bench kW (Specify standard and tolerance) |  |
| 6.11.2 | Maximum Gross torque on bench Nm @ rpm |  |
| 6.11.3 | Engine RPM at max. Power (specify tolerance) |  |
| Note: | In case of diesel engines the max. Power and max. Torque shall be specified as per conditions given in Chapter 6 of Part IV of Doc. MoSRTH / CMVR / TAP-115 / 116 Issue No 3. 4 |
| 6.12 | Location of engine (Front / Rear) |  |

Table-4D of AIS-007 (Revision 5)

| 7.0 | Combustion : |  |
| --- | --- | --- |
| 7.1 | Type of combustion chamber (Hemispherical / squish/others) |  |
| 7.2 | Drawings of combustion chamber and piston crown (mention drawing no) |  |
| 7.3 | Minimum cross section area of ports |  |
| 7.3.1 | Inlet mm2 |  |
| 7.3.2 | Outlet mm2 |  |
| 8.0 | Cooling system : |  |
| 8.1 | Liquid cooling system |  |
| 8.1.1 | Nature of liquid and capacity |  |
| 8.1.2 | Circulating pump yes/no |  |
| 8.1.3 | Characteristics of Circulating pump or make(s) & type(s) |  |
| 8.1.3.1 | Drive ratio |  |
| 8.1.4 | Thermostat type and setting |  |
| 8.2 | Air Cooling system |  |
| 8.2.1 | Blower characteristics |  |
| 8.2.1.1 | Make(s) |  |
| 8.2.1.2 | Type(s) |  |
| 8.2.1.3 | Drive ratio(s) |  |
| 8.2.2 | Air ducting(std production) |  |
| 9.0 | Temperature regulating system (yes/no) |  |
| 9.1 | Brief description |  |
| 10.0 | Temperature permitted by manufacturer °C |  |
| 10.1 | Liquid cooling:- |  |
| 10.1.1 | Max. Temp. at engine Outlet |  |
| 10.2 | Air cooling:- |  |
| 10.2.1 | Reference point |  |
| 10.2.2 | Max. temperature at reference point |  |
| 10.3 | Max. outlet temperature of the intercooled-air |  |
| 10.4 | Maximum exhaust temperature °C |  |
| 10.4.1 | Max. exhaust temperature (in case of diesel engines, at the point in the exhaust pipe(s) adjacent in outlet flange(s) of exhaust manifolds) |

Table-4D of AIS-007 (Revision 5)

| 11.0 | Fuel temperature °C : |  |
| --- | --- | --- |
| 11.1 | Minimum |  |
| 11.2 | Maximum |  |
| 12.0 | Lubricant Temperature °C : |  |
| 12.1 | Minimum |  |
| 12.2 | Maximum |  |
| 13.0 | Intake system : |  |
| 13.1 | Supercharger / Turbocharger - yes/no |  |
| 13.1.1 | Description of system |  |
| 13.1.2 | Make(s) |  |
| 13.1.3 | Type(s) & Part No. |  |
| 13.2 | Intake manifold |  |
| 13.2.1 | Description & Drawings |  |
| 13.3 | Air filter |  |
| 13.3.1 | Make |  |
| 13.3.2 | Type & Part No. |  |
| 13.4 | Intake silencer |  |
| 13.4.1 | Make |  |
| 13.4.2 | Type |  |
| 13.5 | Description & diagrams of inlet pipe & their accessories (dash pot, heating device, additional air intake etc.) |  |
| 13.6 | Inter cooler |  |
| 13.6.1 | Make |  |
| 13.6.2 | Identification mark / & Part No. |  |
| 14.0 | Fuel feed: |  |
| 14.1 | Injection system description |  |
| 14.2 | Working principle: intake manifold/ direct injection/ indirect injection/swirl chamber/others |  |
| 14.3 | Fuel Pump |  |
| 14.3.1 | Make(s) & |  |
| 14.3.2 | Type(s) & Part No. |  |

Table-4D of AIS-007 (Revision 5)

| 14.4 | Delivery mm3/per stroke at Rated speed and at Max Torque speed (specify tolerance) Or characteristic diagram (specify tolerance) |  |
| --- | --- | --- |
| 14.5 | Calibration procedure on engine/pump bench |  |
| 14.6 | Injection timing deg BTDC (specify tolerance) |  |
| 14.7 | Injection advance curve (attach the same) |  |
| 14.8 | Injection advance (specify the tolerance) |  |
| 14.9 | Injectors |  |
| 14.9.1 | Type, (mention Holder & Nozzle no(s)) |  |
| 14.9.2 | Make |  |
| 14.9.3 | Opening pressure (specify tolerance) or characteristic diagram |  |
| 14.9.4 | Injection piping |  |
| 14.9.5 | Length mm |  |
| 14.9.6 | Internal diameter mm |  |
| 15.0 | Device for recycling crank-case gases : |  |
| 15.1 | Description & diagrams |  |
| 16.0 | Governor : |  |
| 16.1 | Make(s) & |  |
| 16.2 | Type(s) |  |
| 16.3 | Cut off point under load (rpm) |  |
| 16.4 | Max. Speed without load (rpm) |  |
| 16.5 | Idle Speed (rpm) |  |
| 17.0 | Cold start device (starting aid): |  |
| 17.1 | Make(s) |  |
| 17.2 | Type(s) |  |
| 17.3 | System description |  |
| 18.0 | Starting System : |  |
| 18.1 | Make(s) |  |
| 18.2 | Type(s) |  |
| 18.3 | System description |  |
| 19.0 | Valve timing / Port timing or equivalent data : |  |
| 19.1 | Max. lift of valves |  |
| 19.1.1 | Inlet mm |  |

Table-4D of AIS-007 (Revision 5)

| 19.1.2 | Exhaust mm |  |
| --- | --- | --- |
| 19.2 | Angle of valves / port (w.r.t. top dead center) |  |
| 19.3 | Inlet |  |
| 19.3.1 | Opening |  |
| 19.3.2 | Closing |  |
| 19.4 | Exhaust |  |
| 19.4.1 | Opening |  |
| 19.4.2 | Closing |  |
| 19.5 | Transfer |  |
| 19.5.1 | Opening |  |
| 19.5.2 | Closing |  |
| 19.6 | Reference or setting ranges |  |
| 19.7 | Valve gap (Hot & Cold) |  |
| 19.7.1 | Inlet |  |
| 19.7.2 | Exhaust |  |
| 19.8 | Distribution by ports |  |
| 19.8.1 | Volume of crank-case cavity with piston at TDC |  |
| 19.8.2 | Description of reed valve if any with drawing |  |
| 19.8.3 | Description (with drawing) of inlet ports, scavenging and exhaust ports with corresponding timing. (The drawing should include one representing the inner surface of the cylinder) |  |
| 20.0 | Lubrication system : |  |
| 20.1 | Description of system |  |
| 20.2 | Lubrication oil capacity lit |  |
| 20.3 | Position of lubricant reservoir |  |
| 20.4 | Lubricating oil grade |  |
| 20.5 | Feed system(pump, injection in to intake mixing with fuel etc.,) |  |
| 20.6 | Lubricating pump |  |
| 20.6.1 | Make |  |
| 20.6.2 | Type |  |
| 20.7 | Mixture with fuel : yes/no, and if yes % |  |
| 20.8 | Oil cooler : yes/no, and if yes Drawings/ makes & types |  |

Table-4D of AIS-007 (Revision 5)

| 21.0 | Electrical equipment : |  |
| --- | --- | --- |
| 21.1 | Generator/alternator characteristics (specify tolerance) or |  |
| 21.1.1 | Make |  |
| 21.1.2 | Type |  |
| 22.0 | Other engine driven auxiliaries: |  |
| 22.1 | Enumeration & brief description, if necessary |  |
| 23.0 | Idling System : |  |
| 23.1 | Idling speed (rpm) (specify the tolerance) |  |
| 23.2 | Description of settings and relevant requirements |  |
| 24.0 | Additional requirements for diesel engines: |  |
| 24.1 | Maximum permitted depression of air intake at characteristic place (Specify location of measurement) (kPa) |  |
| 24.2 | Exhaust back pressure at maximum Gross power and location of measurement (kPa) |  |
| 24.3 | Effective volume of exhaust-System (specify the tolerance & range) in liters (from exhaust manifold / TC outlet to tail pipe end), Enclose the exhaust system drawing and indicate the volume of each parts clearly. |  |
| 24.4 | Moment of inertia of combined flywheel & transmission at condition when no gear is engaged |  |
| 24.5 | Maximum rated speed (Specify the tolerance) |  |
| 24.6 | Minimum rated speed (Specify the tolerance) |  |
| 24.7 | Power absorbed by fan kW (specify the tolerance) |  |
| 24.8 | Max. Gross torque on bench, Nm@ rpm |  |
| 24.9 | Declared speed and powers of the engine/ submitted for type approval) (Speeds to be agreed with the testing agency) |  |
| Measurement point* | Engine speed rpm | Gross Power kW** |  |
| * | See Chapter 3 of Part IV of Doc.MoSRTHST/CMVR/TAP115/116 Issue No 3. 4 |
| ** | Gross power according to Chapter 6 of Part IV of Doc.MoSRTHST/CMVR/TAP115/116 Issue No 3. 4 |

Table-4D of AIS-007 (Revision 5)

| 25.0 | Exhaust system : |  |
| --- | --- | --- |
| 25.1 | Silencer, Number, Type and make |  |
| 25.2 | Identification mark (If proprietary) / Part No. |  |
| 25.3 | Internal dia of exhaust pipe |  |
| 25.4 | Description (with a general arrangement drawing of exhaust system along with its routing indicating the lengths of exhaust pipe, tail pipe and exhaust outlet location) |  |
| 25.5 | Minimum distance between exhaust pipe(s) and the fuel line |  |
| 26.0 | Additional emission control devices, such as catalytic converter etc. (if any & if not covered by another heading) |  |
| 26.1 | Catalyser make, Number |  |
| 26.2 | Identification Mark / Part No |  |
| 26.3 | Type of catalytic action (One/two/three way) |  |
| 26.4 | Total charge of precious metal (g/vehicle) |  |
| 26.5 | Relative concentration (%) |  |
| 26.5.1 | Platinum |  |
| 26.5.2 | Rhodium |  |
| 26.5.3 | Palladium |  |
| 26.6 | Substrate (Monolythic metal/ Ceramic/ honeycomb) |  |
| 26.7 | Cell density (cells per sq.inch) |  |
| 26.8 | Type of casing for catalyser |  |
| 26.9 | Diagram indicating the arrangement and position of catalytic converter w.r.t exhaust manifold) |  |
| 26.10 | Electronic Control Unit (ECU) |  |
| 26.10.1 | Make |  |
| 26.10.2 | Identification mark |  |
| 26.10.3 | Calibration Identification No. |  |
| 26.11 | Secondary Air Injection |  |
| 26.11.1 | Make |  |
| 26.11.2 | Identification mark |  |
| 26.12 | Exhaust Gas Recirculation System |  |
| 26.12.1 | Make |  |
| 26.12.2 | Type |  |
| 26.12.3 | Identification mark |  |

| Table 5 of AIS-007 (Revision 5) TECHNICAL SPECIFICATION – FOUR WHEELERS AND ABOVE PART D – BRAKES |
| --- |
| Clause No. | Description |
| D1.0 | Service brakes : |
| D1.1 | Make |
| D1.2 | Type (Mechanical/hydraulic/air/air assisted/vacuum assisted/others) |
| D1.3 | Control system & braking wheel |
| D1.4 | Schematic layout indicating method of split of brake system, location of valves, reservoirs, ABS components etc. (Attach drawing and indicate the drawing number) |
| D1.5 | Anti-Lock braking system Provided (Yes/No/Optional) |
| D1.5.1 | If yes, details of ABS |
| D1.5.2 | Make |
| D1.5.3 | Category of ABS |
| D1.5.4 | Nos. of directly controlled wheel(s) |
| D1.5.5 | Brief description of failure warning tell–tale |
| D1.5.6 | Wheel Speed Sensors |
| D1.5.6.1 | No. of sensors |
| D1.5.6.2 | Make of sensors |
| D1.5.6.3 | Type of sensors |
| D1.5.7 | Modulator |
| D1.5.7.1 | Nos. of Modulators |
| D1.5.7.2 | Make of Modulators |
| D1.5.7.3 | Identification No. / Part No. of Modulator |
| D1.5.7.4 | Brief description and features |
| D1.5.8 | Controller |
| D1.5.8.1 | Nos. of Controller |
| D1.5.8.2 | Make of Controller |
| D1.5.8.3 | Identification No. / Part No. of Controller |
| D1.5.8.4 | Brief description and features |
| D1.5.9 | Height of Center of Gravity (mm) |
| D1.5.9.1 | Un laden condition |
| D1.5.9.2 | Laden condition |
| D 1.5.10 | Slack adjuster |
| D 1.5.10.1 | Front ( Automatic / Manual ) |
| D 1.5.10.1.1 | Type |

Table 5 of AIS-007 (Revision 5)

| D 1.5.10.2 | Rear ( Automatic / Manual ) |
| --- | --- |
| D 1.5.10.2.1 | Type |
| D2.0 | Brake lining or pad |
| D2.1 | Nominal Dimensions, (mm) (Length x Width x thickness) |
| D2.1.1 | Front wheel |
| D2.1.2 | Rear wheel |
| D2.1.3 | Others |
| D2.1.4 | Type of liner wear indicator (window/ acoustic/ optical/ any other) |
| D2.2 | Effective area per axle (cm²) |
| D2.2.1 | Front |
| D2.2.2 | Rear |
| D2.2.3 | Others |
| D2.3 | Make |
| D2.3.1 | Front wheel / axle |
| D2.3.2 | Rear wheel / axle |
| D2.3.3 | Others |
| D2.3.4 | Whether asbestos or asbestos-free |
| D3.0 | Brake drum or disc |
| D3.1 | Front axle ( Disc / Drum ) |
| D3.1.1 | Effective Diameter (mm) |
| D3.2 | Rear axle ( Disc / drum ) |
| D3.2.1 | Effective Diameter (mm) |
| D3.3 | Other axle ( Disc / Drum ) |
| D3.3.1 | Effective diameter (mm) |
| D4.0 | Master cylinder or brake valve |
| D4.1 | Make |
| D4.2 | Inner diameter of the master cylinder (mm) |
| D4.3 | Operating stroke (mm) |
| D5.0 | Wheel cylinder / Wheel Chamber |
| D5.1 | Diameter (mm) |
| D5.1.1 | Front |
| D5.1.2 | Rear |
| D5.1.3 | Others |
| D5.2 | Type (single acting/double acting) |
| D5.2.1 | Front |
| D5.2.2 | Rear |
| D5.2.3 | Others |
| D5.2.4 | Make of wheel cylinder / slave cylinder |

Table 5 of AIS-007 (Revision 5)

| D6.0 | Booster : |
| --- | --- |
| D6.1 | Make |
| D6.2 | Type |
| D6.3 | Boost ratio |
| D6.4 | Size of the booster (mm) (diameter) |
| D7.0 | Vacuum or air assistance |
| D7.1 | Pressure |
| D7.1.1 | Nominal (P2 as per IS 11852) |
| D7.1.2 | Cut in |
| D7.1.3 | Cut out |
| D7.2 | Type of vacuum pump or air compressor |
| D 7.2.1 | Air compressor cubic capacity (cc) |
| D7.3 | Type of pressure regulator |
| D7.4 | No. of tanks |
| D7.5 | Tank Capacity (l) Description Capacity |
| D7.5.1 | Tank 1 |
| D7.5.2 | Tank 2 |
| D7.5.3 | Tank 3 |
| D7.5.4 | Tank 4 |
| D7.6 | Brake Chamber Front Rear Parking Make and type Size mm Inner diameter mm Stroke mm |
| D7.6.1 |  |
| D7.6.2 |  |
| D7.6.3 |  |
| D7.6.4 |  |
| D8.0 | Brake hose (if Hydraulic) |
| D8.1 | Make, and Identification No. |
| D8.1.1 | Type of expansion (HL / HR) |
| D8.2 | Free Length of hoses |
| D8.3 | Thickness of lining (mm) |
| D8.4 | Nominal bore dia. (mm) |
| D9.0 | Failure Warning device for braking |
| D9.1 | Type (Visual display/ audible/others) |
| D9.2 | Operation pressure (kg/cm2 / bar / kPa) |
| D9.3 | Type of safety device |

Table 5 of AIS-007 (Revision 5)

| D10.0 | Parking brake |
| --- | --- |
| D10.1 | Make |
| D10.2 | Type (mechanical/spring brake) |
| D10.3 | Acting on Transmission/wheel |
| D10.4 | Control System & Braking wheel |
| D10.5 | Lining/pad |
| D10.6 | Name of producer |
| D10.7 | Dimension (mm) |
| D10.8 | Area (cm 2) |
| D10.9 | Material |
| D10.10 | Diameter of brake drum/disc (mm) |
| D11.0 | Secondary brake |
| D11.1 | Type |
| D11.2 | Description |
| D12.0 | Additional retarding devices |
| D12.1 | Type |
| D12.2 | Description |
| D12.3 | Deceleration at 30 km/h, m/s2 |
| D13.0 | Brake fluid |
| D13.1 | Make |
| D13.2 | Trade name |
| D13.3 | Specification/ grade as per Indian standard |
| D14.0 | Load distribution : Laden kg Unladen kg Unladen F/R Ratio Front axle Rear axle Other axle Total |
| D15.0 | Proportioning valve |
| D15.1 | Make |
| D15.2 | Characteristics |
| D15.3 | Identification |

Table 5 of AIS-007 (Revision 5)

| D16.0 | Apportioning valve |
| --- | --- |
| D16.1 | Make |
| D16.2 | Characteristics |
| D16.3 | Identification |
| D17.0 | Load sensing valve |
| D17.1 | Make |
| D17.2 | Characteristics |
| D17.3 | Identification |
| D18.0 | valve |
| D18.1 | Make |
| D18.2 | Characteristics |
| D18.3 | Identification |
| D19.0 | Other valves |
| D19.1 | Function |
| D19.2 | Make |
| D19.3 | Characteristics |
| D19.4 | Identification |

| Table 6 of AIS-007 (Revision 5) TECHNICAL SPECIFICATION – FOUR WHEELERS AND ABOVE PART E – ELECTRICAL |
| --- |
| Clause No. | Description |
| E1.0 | Battery |
| E1.1 | Type & number |
| E1.2 | Voltage |
| E2.0 | Wind Screen Wiper |
| E2.1 | Type (Manual/power) |
| E2.2 | No. of wipers |
| E2.3 | Wiper motor |
| E2.3.1 | Make |
| E2.3.2 | Type |
| E2.3.3 | Identification mark |
| E2.3.4 | Rated voltage |
| E2.3.5 | Number of sweep Frequencies |
| E2.3.6 | Highest sweep frequency (Cycles/min) |
| E2.3.7 | Lowest sweep frequency (Cycles/min) |
| E2.4 | Wiper arm |
| E2.4.1 | Length |
| E2.4.2 | Make |
| E2.5 | Wiper blade |
| E2.5.1 | Length |
| E2.5.2 | Make |
| E2.5.3 | Identification |
| E2.6 | H Point |
| E2.7 | Washer tank |
| E2.7.1 | Type |
| E2.7.2 | Make |
| E2.7.3 | Identification No. / Part No |
| E2.7.4 | Capacity l |
| E2.7.5 | Material |
| E2.7.6 | Washer tank motor / Washer Pump |
| E2.7.6.1 | Make |
| E2.7.6.2 | Model |
| E2.7.7 | Nozzle(s) |
| E2.7.7.1 | No. Of Nozzles |

Table 6 of AIS-007 (Revision 5)

| E2.8 | Defroster / Demist |
| --- | --- |
| E2.8.1 | Make |
| E2.8.2 | Details of Demisting and / or Defrosting system |
| E2.8.2.1 | Schematic Diagram of Engine cooling system |
| E2.8.2.2 | Schematic Diagram of Heating system |
| E2.8.2.3 | Cross sectional view of complete air handling system including position of louvers (vents) on dash board |
| E2.8.2.4 | Blower identification |
| E2.8.2.4.1 | Blower Voltage and capacity (Watts) |
| E2.8.2.5 | If defrost system is fitted, specify defrost test temprature (-8 +/- 2 deg C / -18 +/- 3 deg C) |
| E2.9 | Drawing indicating the seat back angle, seat travel, H point, Rake angle, F point, steering wheel position, Driver’s vision points, Angle obstruction of the ‘A’ pillar and the related dimensions as per related standards. |
| E3.0 | Horn |
| E3.1 | Make |
| E3.2 | Type (As per IS 1884:1993) |
| E3.3 | Operating voltage |
| E3.4 | Identification: TAC No. / BIS License No. / E- Marking |
| E3.5 | Number |
| E3.6 | Sketch showing mounting of horn |
| E3.7 | Brief Dimensional Drawing indicating the shape and material of the body work at the front of the horn, which might affect the level of the sound, emitted by the horn and have a masking effect |
| E3.8 | Maximum vehicle speed for continuous operation (km/h) (Only for AC horns) |
| E4.0 | Lighting Installation requirements |
| E4.1 | Brief Dimensional Drawing indicating installation details of all light & light signalling devices of the vehicle as per AIS-008 |
| E4.2 | Head lamp leveling system ( manual / automatic ) |
| E4.2.1 | Stop position ( if manual ) |
| E4.2.2 | Initial inclination |
| E4.2.3 | Drawing showing initial inclination angle on the head lamp |
| E4.2.4 | Drawing showing type and controls of dipped beam leveling device with table showing positions of switch for various vehicle loading condition |
| E4.3 | Tell-Tale for leveling switch |
| E4.3.1 | Description and sketch showing the detail positions of Tell-Tale and seating layout (for M category vehicles) |

Table 6 of AIS-007 (Revision 5)

| E5.0 | Head lamp |
| --- | --- |
| E5.1 | Main beam |
| E5.1.1 | Make |
| E5.1.2 | Type of lens (Glass / Plastic) |
| E5.1.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E5.1.4 | Number and Colour of Lens |
| E5.2 | Dipped beam |
| E5.2.1 | Make |
| E5.2.2 | Type of lens (Glass / Plastic) |
| E5.2.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E5.2.4 | Number and Colour of Lens |
| E5.3 | Head Lamp cleaning device provided (Yes / No) ( For Headlamps having intensity more than 2000 lumen) |
| E5.3.1 | Cleaner Type as per AIS-083 |
| E5.3.1.1 | Make |
| E5.3.2 | A list, specifying the parts which constitute the headlamp cleaner and drawings thereof, (e.g. pumps, nozzles, valves, motors and wipers); |
| E5.3.3 | A brief technical description indicating the length of the cleaning period, the consumption of cleaning fluid during the cleaning period and the minimum capacity of the container provided; |
| E5.3.4 | Capacity class of the fluid container: 25/50 |
| E5.3.5 | Drawings showing the installation to a vehicle |
| E5.3.6 | Drawings showing the relative attachment between the headlamp(s) and the wiper(s), nozzle(s), or corresponding parts, |
| E5.3.7 | Drawings showing the cleaning principle employed |
| E5.3.8 | where appropriate, the part of the illuminating surface of the headlamp relevant to the cleaner shall also be shown |
| E5.4 | Bend Lighting , provided (Yes / No) |
| E5.4.1 | Cornering Lamp (if provided) |
| E5.4.2 | Make |
| E5.4.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E5.4.4 | Type of lens (Glass / Plastic) |
| E5.4.5 | Number and Colour of Lens |
| E5.5 | Day Time Running Lamp (if provided) |
| E5.5.1 | Make |
| E5.5.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E5.5.3 | Type of lens (Glass / Plastic) |
| E5.5.4 | Number and Colour of Lens |

Table 6 of AIS-007 (Revision 5)

| E6.0 | Front Fog Lamp |
| --- | --- |
| E6.1 | Make |
| E6.2 | Type of lens (Glass / Plastic) |
| E6.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E6.4 | Number and Colour of Lens |
| E7.0 | Rear Fog Lamp |
| E7.1 | Make |
| E7.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E7.3 | Number and Colour of Lens |
| E8.0 | Side Marker lamps |
| E8.1 | Make |
| E8.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E8.3 | Number and Colour of Lens |
| E9.0 | Registration Plate lamp |
| E9.1 | Make |
| E9.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E9.3 | Number and Colour of Lens |
| E10.0 | Position lamp / Parking Lamp – Front |
| E10.1 | Front Position Lamp |
| E10.1.1 | Make |
| E10.1.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E10.1.3 | Number and Colour of Lens |
| E10.2 | Front Parking Lamp |
| E10.2.1 | Make |
| E10.2.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E10.2.3 | Number and Colour of Lens |
| E11.0 | Position lamp / Parking Lamp – Rear |
| E11.1 | Rear Position Lamp |
| E11.1.1 | Make |
| E11.1.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E11.1.3 | Number and Colour of Lens |
| E11.2 | Rear Parking Lamp |
| E11.2.1 | Make |
| E11.2.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E11.2.3 | Number and Colour of Lens |

Table 6 of AIS-007 (Revision 5)

| E12.0 | Stop lamp (S1 / S2) |
| --- | --- |
| E12.1 | Make |
| E12.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E12.3 | Number and Colour of Lens |
| E13.0 | Stop lamp ( S3) for M1 category & N category as applicable |
| E13.1 | Make |
| E13.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E13.3 | Number and Colour of Lens |
| E14.0 | Reversing lamp |
| E14.1 | Make |
| E14.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E14.3 | Number and Colour of Lens |
| E15.0 | Direction indicator Lamp |
| E15.1 | Front |
| E15.1.1 | Make |
| E15.1.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E15.1.3 | Number and Colour of Lens |
| E15.2 | Rear |
| E15.2.1 | Make |
| E15.2.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E15.2.3 | Number and Colour of Lens |
| E15.3 | Side |
| E15.3.1 | Make |
| E15.3.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E15.3.3 | Number and Colour of Lens |
| E15.4 | Flasher for Direction Indicators |
| E15.4.1 | Flashing Frequency ( No of flashes / minute ) |
| E16.0 | Hazard warning signal |
| E16.1 | Front |
| E16.1.1 | Make |
| E16.1.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E16.1.3 | Number and Colour of Lens |
| E16.2 | Rear |
| E16.2.1 | Make |
| E16.2.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E16.2.3 | Number and Colour of Lens |

Table 6 of AIS-007 (Revision 5)

| E16.3 | Side |
| --- | --- |
| E16.3.1 | Make |
| E16.3.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E16.3.3 | Number and Colour of Lens |
| E17.0 | Reflector |
| E17.1 | Front |
| E17.1.1 | Make |
| E17.1.2 | Type |
| E17.1.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E17.1.4 | Number and Colour of Lens |
| E17.1.5 | Reflective surface Area |
| E17.1.6 | Shape (Square / rectangular / circular / elliptical /other) |
| E17.2 | Rear |
| E17.2.1 | Make |
| E17.2.2 | Type |
| E17.2.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E17.2.4 | Number and Colour of Lens |
| E17.2.5 | Reflective surface Area |
| E17.2.6 | Shape (Square / rectangular / circular / elliptical /other) |
| E17.3 | Side |
| E17.3.1 | Make |
| E17.3.2 | Type |
| E17.3.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E17.3.4 | Number and Colour of Lens |
| E17.3.5 | Reflective surface Area |
| E17.3.6 | Shape (Square / rectangular / circular / elliptical /other) |
| E18.0 | End-outline marker lamp (Top light) |
| E18.1 | Front |
| E18.1.1 | Make |
| E18.1.2 | Type of lens (Glass / Plastic) |
| E18.1.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E18.1.4 | Number and colour of Lens |
| E18.2 | Rear |
| E18.2.1 | Make |

Table 6 of AIS-007 (Revision 5)

| E18.2.2 | Type of lens (Glass / Plastic) |
| --- | --- |
| E18.2.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E18.2.4 | Number and colour of Lens |
| E 5.0 to E 18.0 - Installation details. | Diagram of vehicle indicating location, reference axis, mark of apparent surface, contour of vehicle parts limiting geometric visibility of all lights and light signaling devices, location of extreme outer edges and longitudinal median plane of vehicle including following dimensions in mm. Along width of vehicle-horizontal distance between inner illuminating surfaces, distance between inner illuminating surfaces and outer most part of vehicle and distance between nearest point of illuminating surfaces of indicators and dipped-beam head lamp. Along length of vehicle (where applicable) – distance between the transverse plane corresponding to the longitudinal rearmost extremity to center of reference of rear indicators. Heights of highest and lowest point of illuminating surfaces. |
| E19.0 | Automotive bulbs |
| E19.1 | Head lamp bulb (main beam and dip) |
| E19.1.1 | Make |
| E19.1.2 | Category as per AIS-034 |
| E19.1.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.1.4 | Head lamp bulb (Dipped beam) |
| E19.1.5 | Make |
| E19.1.6 | Category as per AIS-034 |
| E19.1.7 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.2 | Parking Lamp bulb – Front |
| E19.2.1 | Make |
| E19.2.2 | Category as per AIS-034 |
| E19.2.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.3 | Parking Lamp bulb – Rear |
| E19.3.1 | Make |
| E19.3.2 | Category as per AIS-034 |
| E19.3.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.4 | Direction indicator lamp bulb - front |
| E19.4.1 | Make |
| E19.4.2 | Category as per AIS-034 |
| E19.4.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.5 | Direction indicator lamp bulb - rear |
| E19.5.1 | Make |
| E19.5.2 | Category as per AIS-034 |
| E19.5.3 | Identification: TAC No. / BIS License No. / E- Marking |

Table 6 of AIS-007 (Revision 5)

| E19.6 | Direction indicator lamp bulb - side |
| --- | --- |
| E19.6.1 | Make |
| E19.6.2 | Category as per AIS-034 |
| E19.6.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E 19.7 | Front Position Lamp bulb |
| E 19.7.1 | Make |
| E 19.7.2 | Category as per AIS-034 |
| E 19.7.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.8 | Rear Position Lamp ( tail lamp )Bulb |
| E19.8.1 | Make |
| E19.8.2 | Category as per AIS-034 |
| E19.8.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.9 | Stop lamp bulb |
| E19.9.1 | Make |
| E19.9.2 | Category as per AIS-034 |
| E19.9.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.10 | Number plate lamp bulb |
| E19.10.1 | Make |
| E19.10.2 | Category as per AIS-034 |
| E19.10.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.11 | End out Marker bulb |
| E19.11.1 | Make |
| E19.11.2 | Category as per AIS-034 |
| E19.11.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.12 | Reversing lamp bulb |
| E19.12.1 | Make |
| E19.12.2 | Category as per AIS-034 |
| E19.12.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.13 | Stop Lamp Bulb (S3) |
| E19.13.1 | Make |
| E19.13.2 | Category as per AIS-034 |
| E19.13.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.14 | Front Fog Lamp Bulb |
| E19.14.1 | Make |
| E19.14.2 | Category as per AIS-034 |
| E19.14.3 | Identification: TAC No. / BIS License No. / E- Marking |

Table 6 of AIS-007 (Revision 5)

| E19.15 | Rear Fog Lamp Bulb |
| --- | --- |
| E19.15.1 | Make |
| E19.15.2 | Category as per AIS-034 |
| E19.15.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.16 | Side Marker Lamp Bulb |
| E19.16.1 | Make |
| E19.16.2 | Category as per AIS-034 |
| E19.16.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.17 | Cornering lamp bulb (if provided) |
| E19.17.1 | Make |
| E19.17.2 | Designation Category as per AIS-034 |
| E19.17.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.18 | Day time Running lamp bulb (if provided) |
| E19.18.1 | Make |
| E19.18.2 | Designation Category as per AIS-034 |
| E19.18.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E19.19 | Bending lamp bulb (if provided) |
| E19.19.1 | Make |
| E19.19.2 | Designation Category as per AIS-034 |
| E19.19.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E20.0 | Warning Triangle |
| E20.1 | Make |
| E20.2 | Identification: TAC No. / BIS License No. / E- Marking |
| E21.0 | Reflective tape (AIS-090) |
| E 21.1 | Make |
| E 21.2 | Width of tape(s) in mm |
| E 21.3 | Identification: TAC No. / BIS License No. / E- Marking |
| E 21.4 | Dimensional Drawing indicating installation details of reflective Tapes at front, Rear & side of the vehicle / load body / container / Tanker etc., as per AIS-090 |
| E 22.0 | Electromagnetic Compatibility as per AIS-004 (Part 3) |
| E 22.1 | Description and drawings/photographs of the shapes and constituent materials of the part of the body forming the engine compartment and the part of the passenger compartment nearest to it: |
| E 22.2 | Drawings or photographs of the position of the metal components housed in the engine compartment (e.g. heating appliances, spare wheel, air filter, steering mechanism, etc.): |

Table 6 of AIS-007 (Revision 5)

| E 22.3 | List of Electrical/Electronic Systems which are not previously listed |
| --- | --- |
| E 22.4 | List of all subassemblies, which includes an electronic oscillator or switching frequency greater than 9kHz (like ECU,steering, suspension,Body Control Module, etc.). The list shall include Device name, Make and Part No./Type ID/Drawing No |
| E 22.4.1 | List of all Electrical components, which include Broadband EMI sources (like HAVC Motor, Wiper Motor, Window motor and Horn etc.)The list shall include Device name, Make and Part No./Type ID/Drawing No. |
| E 22.5 | Table of installation and use of RF transmitters in the vehicle(s), if applicable (see paragraph 3.1.8. of this standard): |
| E 22.6 | Vehicle equipped with 24 GHz short-range radar equipment: yes/no/optional |
| E 23.0 | Any other features (As declared by the vehicle manufacturer) |

Table 7 of AIS-007 (Revision 5)

BRIEF TECHNICAL SPECIFICATIONS FOR MOTOR VEHICLES

| Manufacturer’s name and address |  |
| --- | --- |
| Importer’s name and address (in case of CBU) |  |
| Vehicle data |  |
| Basic model |  |
| Type / Description |  |
| Category of the vehicle |  |
| Variant(s) |  |
| Type / Description |  |
| Category of variant(s) |  |
| Engine |  |
| Make |  |
| Model |  |
| Type |  |
| Bore x stroke (mm) |  |
| No. of cylinders |  |
| Displacement |  |
| Compression ratio |  |
| Max. Engine output (kW @ rpm) |  |
| Max. Torque (Nm @ rpm) |  |
| Air cleaner type |  |
| Clutch |  |
| Type |  |
| Gear box |  |
| Make model |  |
| Type |  |
| No. of gears |  |
| Gear ratio 1st 2nd 3rd 4th 5th 6th Reverse |  |
| Drive Axle (Front / Rear / All) |  |
| Front axle ratio |  |

Table 7 of AIS-007 (Revision 5)

| Rear axle ratio |  |
| --- | --- |
| Steering |  |
| Type / Description |  |
| Steering wheel diameter mm |  |
| Ratio |  |
| Frame |  |
| Long member size (mm) |  |
| Number of cross members |  |
| Suspension |  |
| Type / Description |  |
| Spring |  |
| Anti-roll bar |  |
| Shock absorbers |  |
| Brake |  |
| Service brake (Brief description) |  |
| Auto Slack Adjuster Fitted ( Yes / No / Optional ) |  |
| ABS Fitted (Yes / No / Optional ) |  |
| Front (Disc / Drum) |  |
| Rear (Disc / Drum) |  |
| Total braking area (cm²) |  |
| Parking brake |  |
| Secondary brake |  |
| Wheels and tyres |  |
| Wheel rim size |  |
| Tyre size designation including ply rating |  |
| Speed index |  |
| Load index / Load rating |  |
| Tyre Type (Radial / Cross / Tube / Tubeless) |  |
| Laden Tyre pressure (front & rear) (kg/cm2) |  |
| Electrical system |  |
| System voltage (V) |  |
| Battery rating (Ah) |  |
| Wiper motor |  |
| Wiping system (Brief description) |  |
| Fuel tank |  |
| Material |  |
| Capacity (l) |  |

Table 7 of AIS-007 (Revision 5)

| Dimensions |  |
| --- | --- |
| Wheel base (mm) |  |
| Overall width (mm) |  |
| Overall length (mm) |  |
| Overall height (mm) |  |
| Front track (mm) |  |
| Rear track (mm) |  |
| Min. ground clearance (mm) |  |
| Cargo box dimensions (mm) |  |
| Load body platform area |  |
| Weights |  |
| Maximum GVW kg (for rigid vehicles) |  |
| Maximum GCW kg (for articulated / combination vehicles) |  |
| Maximum FAW (kg) |  |
| Maximum RAW (kg) |  |
| Kerb weight with 90% fuel (with spare wheel , tools, etc.) (kg) |  |
| Maximum gradeability in 1st gear |  |
| Seating |  |
| Seating capacity |  |
| Sketch showing seating layout with dimensions |  |

Table 8 of AIS-007 (Revision 5)

| Rule No. | Subject | Name of the Manufacturer ( Please give information for every supplier / vendor under the same para, separate lines ) | TAC No. / BIS License No / Test Report No. as applicable. (indicate validity date ) (Application Ref No. allotted by concerned Test Agency, If approval is in the process ) | Possible date of submission of required approval, if the same is in process | CoP Cert No. with validity date (where ever applicable) |
| --- | --- | --- | --- | --- | --- |
| 95 | Tyres (Compliance to IS 15633 / IS 15627/IS 15636) |  |  |  |  |
|  | Front |  |  |  |  |
|  | Rear |  |  |  |  |
|  | Spare wheel (as applicable) |  |  |  |  |
| 100 | Safety Glass Windscreen Side Rear (For 3 & 4 Wheeler) |  |  |  |  |
| 101 | Windscreen Wiping System Wiping System Washing System Wiper Blade (For 3 & 4 Wheelers) |  |  |  |  |
| 104 | Reflex Reflector Front, White Rear, Red Side, Amber |  |  |  |  |
|  | CNG / LPG Kit Components |  |  |  |  |
|  | Cylinder (as per Gas Cylinder Rule, 2004) |  |  |  |  |
|  | Cylinder Valve / Multi Function Valve (as per Gas Cylinder Rule, 2004) |  |  |  |  |
|  | CNG / LPG Pressure Regulator |  |  |  |  |
|  | CNG / LPG Gas Solenoid Valve |  |  |  |  |
|  | CNG / LPG Gas Air Mixer |  |  |  |  |

Table 8 of AIS-007 (Revision 5)

|  | Petrol Solenoid valve |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | CNG/LPG Rigid Pipe |  |  |  |  |
|  | CNG/ LPG High Pressure Flexible Hose |  |  |  |  |
|  | CNG/ LPG Low Pressure Flexible Hose |  |  |  |  |
|  | Electrical Fuses |  |  |  |  |
|  | Ventilation Hose/ Conduit |  |  |  |  |
|  | Electrical Wiring Harness |  |  |  |  |
|  | Seat Upholstery, Roof, Side linings |  |  |  |  |
|  | Non-moisture retaining Hard rubber for cylinder mounting (as applicable) |  |  |  |  |
| 118 | Speed Limiter Installation Test Report as per AIS-018 (SLD / SLF) |  |  |  |  |
| 119 | Horns(s) Horn Installation (For all vehicles) |  |  |  |  |
| 123 | Pillion Hand Holds (For all vehicles) |  |  |  |  |
| 124/1 | Automotive Bulbs ( Mention category of bulb/s as per AIS-034 ) |  |  |  |  |
|  | Main Beam head Lamp |  |  |  |  |
|  | Dipped Beam Head Lamp |  |  |  |  |
|  | Daytime Running Lamp |  |  |  |  |
|  | Cornering Lamp |  |  |  |  |
|  | Front Position / parking lamp |  |  |  |  |
|  | Front Fog Lamp |  |  |  |  |
|  | Front Direction Indicator Lamp |  |  |  |  |
|  | Front End-out Marker Lamp |  |  |  |  |
|  | Side Direction Indicator lamp |  |  |  |  |
|  | Side Marker lamp |  |  |  |  |
|  | Stop Lamp |  |  |  |  |
|  | Rear Direction indicator Lamp |  |  |  |  |
|  | Rear Position / Parking Lamp |  |  |  |  |

Table 8 of AIS-007 (Revision 5)

|  | Reversing Lamp |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Rear Fog Lamp |  |  |  |  |
|  | Rear Registration Plate Lamp |  |  |  |  |
|  | Rear End-out Marker Lamp |  |  |  |  |
|  | High Mounted Stop Lamp |  |  |  |  |
| 124/2 | Hydraulic Brake Hose (For all vehicles – as applicable) |  |  |  |  |
| 124/3 | Hydraulic Brake Fluid (For all vehicles – as applicable) |  |  |  |  |
| 124/5 | Steering Impact Head Form Test Body Block Test Crash Test (For M1 category having GVW not more than 1500 kg) |  |  |  |  |
| 124/6 | Side Door Impact Test (For passenger cars) |  |  |  |  |
| 124/7 | Fuel Tank (Provide details in case of multiple capacities / suppliers) |  |  |  |  |
|  | Fuel Tank (metallic) or Fuel Tank (plastic) (For Four Wheelers) |  |  |  |  |
| 124/8 | Wheel Rims (For Four wheelers) |  |  |  |  |
| 124/9 | Control Cables (For two wheelers below 50 CC) |  |  |  |  |
| 124/10 | Pneumatic Coupling (For N category of vehicles) |  |  |  |  |
| 124/12 | Bus Window Retention (Only for Buses) |  |  |  |  |
| 124/14 | Wheel Nuts /Bolts, Wheel Caps / Hub Caps (Only for Four Wheelers) |  |  |  |  |
| 124/15 | Accelerator Control Systems (Only for Four Wheelers) |  |  |  |  |

Table 8 of AIS-007 (Revision 5)

| 124/16 | Door Locks & Hinges (Only for Four Wheelers) |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Door Hinges |  |  |  |  |
|  | Front Door Hinges |  |  |  |  |
|  | Rear Door Hinges |  |  |  |  |
|  | Door Locks |  |  |  |  |
|  | Front Door Lock |  |  |  |  |
|  | Rear Door Lock |  |  |  |  |
| 124/17 | Hood Latch (For passenger cars) |  |  |  |  |
| 124/20 | i) Lighting Signalling & Indicating Systems (For 4 Wheelers) |  |  |  |  |
|  | Head Lamp (Main Beam) |  |  |  |  |
|  | Head Lamp (Dipped Beam) |  |  |  |  |
|  | Front Position / Parking Lamp |  |  |  |  |
|  | Cornering Lamp (if provided) |  |  |  |  |
|  | Front Direction Indicator |  |  |  |  |
|  | Front Fog lamp |  |  |  |  |
|  | Day-Time Running Lamp (if provided) |  |  |  |  |
|  | Front end-out marker Lamp / Top Lights |  |  |  |  |
|  | Rear end-out marker Lamp / Top Lights |  |  |  |  |
|  | Stop Lamp |  |  |  |  |
|  | Rear Position / Parking Lamp |  |  |  |  |
|  | Rear Direction Indicator |  |  |  |  |
|  | Reversing lamp |  |  |  |  |
|  | Rear Fog lamp |  |  |  |  |
|  | High mounted stop Lamp |  |  |  |  |
|  | Rear Registration Plate Lamp |  |  |  |  |
|  | Side Direction Indicator Lamp |  |  |  |  |
|  | Side Marker lamp |  |  |  |  |
|  | Head Lam Cleaning Device |  |  |  |  |

Table 8 of AIS-007 (Revision 5)

|  | ii) Lighting and Signalling Installation Requirements (for 4 wheelers) |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Report No(s). for Base Model / Variants (if already issued) |  |  |  |  |
| 124/21 | Electromagnetic Radiation (EMI) (for all combinations of spark plug, ignition coil, HT cable, Ignition System, ECU and suppress cap) (For all vehicles) |  |  |  |  |
| 124/22 | Towing Devices (For 4 wheelers) as applicable |  |  |  |  |
| 124/24 | Lighting and Signaling installation requirements for 2 & 3wheelers, including Trailers, semi-Trailers |  |  |  |  |
|  | Report No(s). for Base Model / Variants (if already issued) |  |  |  |  |
| 124/25 | Fuel Tank for 2 & 3wheelers (metallic or Non-Metallic) (Indicate Nominal capacity) |  |  |  |  |
| 124/32 | Lighting and light signaling devices for 2 wheelers, 3 wheelers and their trailers and semi trailers. |  |  |  |  |
|  | Head Lamp |  |  |  |  |
|  | Front Position / Parking Lamp |  |  |  |  |
|  | Front Direction Indicator |  |  |  |  |
|  | Stop Lamp |  |  |  |  |
|  | Rear Position / Parking Lamp |  |  |  |  |
|  | Rear Direction Indicator |  |  |  |  |
|  | Reversing lamp for 3 Wheeler |  |  |  |  |
|  | Rear Registration Plate Lamp |  |  |  |  |
|  | Side Direction Indicator Lamp |  |  |  |  |

Table 8 of AIS-007 (Revision 5)

| 124/33 | Spray Suppression System Installation test report as per AIS-013 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 124/34 | Drivers field of vision for M1 category of vehicles. |  |  |  |  |
| 124/35 | Survival space for protection of occupants in a cab. |  |  |  |  |
| 124/36 | Strength of superstructure of passenger vehicles. |  |  |  |  |
| 124/37 | Flammability requirements for M3 category vehicles with more than 22 passengers. |  |  |  |  |
| 124/38 | Interior fittings for M1 category |  |  |  |  |
| 124/39 | Windscreen wiping system requirements for 3 wheelers |  |  |  |  |
| 124/42 | Handholds for L5, M & N category vehicles |  |  |  |  |
| 124/43 | Wheel Rims for L category vehicles |  |  |  |  |
| 124/44 | Protective Devices for L category vehicles |  |  |  |  |
| 124/46 | Defrost & Demist Systems for M1 category vehicles |  |  |  |  |
| 124/48 | Spray Suppression test for 2-Wheelers |  |  |  |  |
| 124/49 | Traction Battery used in Battery Operated Vehicles |  |  |  |  |
| 124/1A | Vehicle Rear Under run Protection And Lateral Protection (For four wheelers) |  |  |  |  |
| 125/1A | Safety Belt and Safety Belt Anchorages (For four wheelers) |  |  |  |  |

Table 8 of AIS-007 (Revision 5)

| 125/(2) | Rear View Mirror and Rear View Mirror Installation Requirements as per AIS-002 ( For all vehicles as referred in AIS-001 ) |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Interior Mirror (Class-I ) |  |  |  |  |
|  | Main Mirror large ( Class-II ) |  |  |  |  |
|  | Main Mirror small ( Class-III ) |  |  |  |  |
|  | Wide Angle Mirror ( Class-IV ) |  |  |  |  |
|  | Close proximity Mirror ( Class-V ) |  |  |  |  |
|  | Front Mirror ( Class-VI ) |  |  |  |  |
|  | Mirrors for L category vehicle with bodywork (Class-VII ) |  |  |  |  |
| 125/1C | Seat Size, Anchorages and Head Restraints ( For four wheelers ) |  |  |  |  |
| 138 | Warning Triangles |  |  |  |  |
| Note : Please enclose copies for TAC / CoP / BIS License / ECE Certificate / Test Reports wherever required by the testing agency. Fill all the columns. If any clause is not applicable, mention “NA” in corresponding column. Do not keep it blank. In case samples are submitted to testing agency, please provide Reference No. if the approval is in process.) |

Table 9 of AIS-007 (Revision 5)

INFORMATION ON TEST REPORTS FOR VEHICLE LEVEL AND

SYSTEM LEVEL COMPLIANCE

|  | Rule No. | Subject | Model | No. of test report / certificate * | Issued by | Justification for applicability as per CEA for the model under consideration |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

* Xerox copies of the certificates to be submitted in case if it is from another testing agency or   whenever necessary.

Table 10 of AIS-007 (Revision 5)

INFORMATION NEEDED FOR APPLYING CRITERIA FOR

EXTENSION OF APPROVAL

| Rule No: | Subject: | Notified Standard | CEA as per doc. no. |
| --- | --- | --- | --- |

Value for each variant

| Variants | (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CEA Parameters |  |  |  |  |  |  |  |  |  |
| (1) |  |  |  |  |  |  |  |  |  |
| (2) |  |  |  |  |  |  |  |  |  |
| (3) |  |  |  |  |  |  |  |  |  |
| (4) |  |  |  |  |  |  |  |  |  |
| (5) |  |  |  |  |  |  |  |  |  |
| (6) |  |  |  |  |  |  |  |  |  |
| (7) |  |  |  |  |  |  |  |  |  |
| (8) |  |  |  |  |  |  |  |  |  |
| (9) |  |  |  |  |  |  |  |  |  |
| (10) |  |  |  |  |  |  |  |  |  |
| (11) |  |  |  |  |  |  |  |  |  |
| (12) |  |  |  |  |  |  |  |  |  |
| (13) |  |  |  |  |  |  |  |  |  |
| (14) |  |  |  |  |  |  |  |  |  |

Additional information required in the case of application for extension based on an already tested model:

1. 	Test report No:

2. 	Specification No.

3. 	Detailed justification and logic for applicability of CEA.

4.	Copies of Test report and specification should be enclosed in case they are not already available with the Test Agency.

5.	Column (1) should indicate the parameters for the tested model.

Note: Where practically not possible to provide the information in the above form, it may be given  in separate sheets / tables with designated sheet nos.

Table 11 of AIS-007 (Revision 5)

DETAILS OF LOCATION OF CHASSIS NUMBER AND CODE FOR MONTH AND

YEAR OF MANUFACTURE AS PER RULE 122 OF CMVR

| Name of the Vehicle Manufacturer & Address : |  |
| --- | --- |
| Name of the basic model : |  |
| Name of Variants, if any : |  |
| Place of Embossing or etching the Chassis Number (Vehicle Identification Number). Supporting details by drawing or pictures may be provided if necessary. |  |
| Code for month and year of production: |
| Code for month of production: | Code for year of production: |
| Month | Code | Year | Code |
| January |  |  |  |
| February |  |  |  |
| March |  |  |  |
| April |  |  |  |
| May |  |  |  |
| June |  |  |  |
| July |  |  |  |
| August |  |  |  |
| September |  |  |  |
| October |  |  |  |
| November |  |  |  |
| December |  |  |  |

| Position of the code for month of production in the Chassis number : |  |
| --- | --- |
| Position of the code for year of production in the Chassis number : |  |
| Height of the Chassis number (Vehicle Identification Number) : |  |

Example of Engine/Motor No. :-

Example of Chassis No. (Vehicle Identification Number) with Month & Year of Manufacture:-

Table 12 of AIS-007 (Revision 5)

DETAILS OF CHANGE IN TECHNICAL SPECIFICATION

| Manufacturers name and address : |
| --- |
| Name of the model and variants: |
| CMVR Certificate No. | Date | Specification No. |
| 3.1 |  |  |  |
| 3.2 |  |  |  |
| Valid Extension |  |
| 4.1 | Dated |  |
| 4.2 | Specifications Revision |  |
| Nature of Change: |  |
| Changes in the Specifications |
| Sr. No. | Specifications No. and Clause No. | Description | Parameter (Earlier) | Parameter (New Extension) |
| 6.1 |  |  |  |  |
| 6.2 |  |  |  |  |
| 6.3 |  |  |  |  |
| 6.4 |  |  |  |  |

Table 13 of AIS-007 (Revision 5)

# Technical Specifications - Battery Operated Vehicles

| 1.0 | General description of vehicle |
| --- | --- |
| 1.1 | Vehicle Model |
| 1.2 | Vehicle Type |
| 1.3 | Drawing and /or photographs of the vehicle |
| 2.0 | Description of The Traction Battery |
| 2.1 | Trade Name and Mark of the Battery |
| 2.2 | Kind of Electro – Chemical Couple |
| 2.3 | Nominal Voltage (V) |
| 2.4 | Battery Maximum Thirty Minutes Power (Constant Power Discharge) (kW) |
| 2.5 | Battery Performance in 2 h Discharge (Constant Power or Constant Current ) |
| 2.5.1 | Battery Energy (kWh) |
| 2.5.2 | Battery Capacity , Ah in 2 h |
| 2.6 | End of Discharge Voltage Value (V) |
| 2.7 | Provision of ventilation for battery Yes / No |
| 2.7.1 | Brief description of the ventilation system adopted in the vehicle. (Refer AIS-038/2003 Clause 3.1.1). Provide drawing if necessary. |
| 2.7.2 | Brief description of the ventilation system adopted in the battery compartment. (Refer AIS-038/2003, Clause 3.1.2). Provide drawing if necessary. |
| 2.8 | On-board Indication of battery state of charge |
| 2.8.1 | Details of indication when state of charge of the battery reaches a level when the manufacturer recommends re-charging. |
| 2.8.1.1 | Indication format. |
| 2.8.1.2 | Relationship of state of charge indicator and the indication. |
| 2.8.1.3 | Make |
| 2.8.1.4 | Model |
| 2.8.2 | Indication of state of charge of battery reaches a level at which driving vehicle further may cause damage to batteries |
| 2.8.2.1 | Indication format. |
| 2.8.2.2 | Relationship of state of charge indicator and the indication. |
| 2.9 | Battery Mass (kg) |
| 2.10 | Brief description of maintenance procedure, if any |
| 3.0 | Description of The Drive Train |
| 3.1 | General |
| 3.1.1 | Make |
| 3.1.2 | Type |
| 3.1.3 | Use : Mono motor / multi motors (number) |

Table 13 of AIS-007 (Revision 5)

| 3.1.4 | Transmission Arrangement parallel / transaxial / others to precise |
| --- | --- |
| 3.1.5 | Test Voltage (V) |
| 3.1.6 | Motor Nominal Speed (Min -1) |
| 3.1.7 | Motor Maximum Speed, Min –1 or by default reducer outlet shaft / gear box speed (specify gear engaged) |
| 3.1.8 | Maximum Power Speed (Min –1) and (km/h) |
| 3.1.9 | Maximum Power (kW) |
| 3.1.10 | Maximum Thirty Minutes Power (kW) |
| 3.1.11 | Maximum Thirty Minutes speed km/h (Reference in AIS-039/2003 and AIS-040/2003) |
| 3.1.12 | Flexible Range (where P>90% of Max. Power ) |
| 3.1.13 | Speed at the beginning of the range (Min –1) |
| 3.1.14 | Speed at the end of the range (Min –1 ) |
| 3.2 | Traction Motor |
| 3.2.1 | Make |
| 3.2.2 | Working Principle |
| 3.2.2.1 | Direct current / alternating current / number of phases |
| 3.2.2.2 | Separate excitation / series / compound |
| 3.2.2.3 | Synchron / asynchron |
| 3.2.2.4 | Coiled rotor / with permanent magnets / with housing |
| 3.2.2.5 | Number of Poles of the Motor |
| 3.2.3 | Motor power curve (kW) with motor RPM (min-1) / vehicle speed in (km/h) |
| 3.3 | Power Controller |
| 3.3.1 | Make |
| 3.3.2 | Type |
| 3.3.3 | Control Principle : vectorial / open loop / closed / other (to be specified ) |
| 3.3.4 | Maximum effective current supplied to the Motor (A) |
| 3.3.5 | Voltage range use (V to V) |
| 3.4 | Cooling System motor : liquid / air controller : liquid / air |
| 3.4.1 | Liquid cooling equipment characteristics |
| 3.4.1.1 | Nature of the liquid , circulating pumps, yes / no |
| 3.4.1.2 | Characteristics or make(s) and type(s) of the pump |
| 3.4.1.3 | Thermostat : setting |
| 3.4.1.4 | Radiator : drawing(s) or make(s) and type(s) |

Table 13 of AIS-007 (Revision 5)

| 3.4.1.5 | Relief valve : pressure setting |
| --- | --- |
| 3.4.1.6 | Fan : Characteristics or make(s) and type(s) |
| 3.4.1.7 | Fan : duct |
| 3.4.2 | Air-cooling equipment characteristics |
| 3.4.2.1 | Blower : Characteristics or make(s) and type(s) |
| 3.4.2.2 | Standard air ducting |
| 3.4.2.3 | Temperature regulating system yes / no |
| 3.4.2.4 | Brief description |
| 3.4.2.5 | Air filter : make(s) type(s) |
| 3.4.3 | Maximum temperatures recommended by the manufacturer: |
| 3.4.3.1 | Motor Outlet : oC |
| 3.4.3.2 | Controller inlet : oC |
| 3.4.3.3 | At motor reference point(s) oC |
| 3.4.3.4 | At controller reference point(s) oC |
| 3.5 | Insulating Category : |
| 3.5.1 | International Protection (IP)-Code : |
| 3.6 | Lubrication System Principle Bearings : friction / ball Lubricant : grease / oil Seal : yes / no Circulation : with / without |
| 4.0 | Charger : |
| 4.1 | Charger : on board / external |
| 4.1.1 | Trademark , model, rating |
| 4.2 | Description of the normal profile of charging system : |
| 4.3 | Specifications of mains |
| 4.3.1 | mains : single phase/ three phase : |
| 4.3.2 | Nominal Voltage (V) & frequency (Hz) with tolerances: |
| 4.4 | Reset period recommended between the end of the discharge and the start of the charge |
| 4.5 | Recommended duration of a complete charge |
| 4.6 | In case of on-board charger |
| 4.6.1 | Continuous rating of charger socket (A) : |
| 4.6.2 | Time rating (h) of charger socket, if any : |
| 4.6.3 | Whether soft-start facility Yes / No : |
| 4.6.4 | Maximum initial in-rush current (A) |

Table 13 of AIS-007 (Revision 5)

| 5.0 | Electrical details of vehicle for functional safety |
| --- | --- |
| 5.1 | Schematic diagram showing the electrical layout giving all major electrical items along with their physical location in the vehicle. It shall include batteries, power-train components, protection fuses, circuit breakers etc. (Reference in AIS-038/2003 Clause 3.1.3) |
| 5.2 | Specifications of circuit breakers/ fuses used for protection of batteries / power-train (Reference in AIS-038/ 2003 Clause 3.1.3) |
| 5.2.1 | IS / IEC specifications |
| 5.2.2 | Rating (A) |
| 5.2.3 | Opening time (ms) |
| 5.3 | Working voltage V (Reference in AIS-038/ 2003 Clause 3.2) |
| 5.4 | Schematic highlighting physical location of live parts having working voltage greater than 60 V DC or 25 V AC (Reference in AIS-038/ 2003 Clause 3.2.1.2) |
| 5.5 | Electric cables / connectors / wiring harness (Reference in AIS-038/ 2003 Clause 3.2.2.2) |
| 5.5.1 | IEC protection class |
| 5.5.2 | Insulation material used |
| 5.5.3 | Conduits provided Yes / No |
| 5.6 | List of exposed conductive parts of on-board equipment. (Reference in AIS-038/ 2003 Clause 3.2.2.3) |
| 5.6.1 | Any potential equalization resistance used to electrically connect these parts Yes/ No |
| 5.6.2 | If yes, give details |
| 5.7 | List of failures due to which the vehicle will come to standstill (Reference in AIS-038/ 2003 Clause 3.3.6) |
| 5.8 | List of conditions under which the performance of vehicle is limited and how. (Reference in AIS-038/ 2003 Clause 3.3.13 ) |
| 5.9 | Declaration regarding Design guidelines followed with respect to various requirements. |
| 6.0 | Electrical energy consumption of Vehicle in W-h/km, as per Clause 5.5.1 of AIS-039 |

Table 14 of AIS-007 (Revision 5)

BRIEF TECHNICAL SPECIFICATIONS FOR CONSTRUCTION EQUIPMENT VEHICLE

| Details of the manufacturer |  |
| --- | --- |
| Name and address |  |
| Telephone No. |  |
| Fax No. / E-mail ID |  |
| Vehicle data |  |
| Basic model |  |
| Type (Brief description) |  |
| Variant(s) |  |
| Type (Brief description) |  |
| Implements / Attachments (Brief description) |  |
| Engine No. |  |
| Chassis No. |  |
| Engine |  |
| Make |  |
| Model and identification |  |
| Type |  |
| Bore x stroke (mm) |  |
| No. of cylinders |  |
| Displacement |  |
| Compression ratio |  |
| Max. Engine output (kW@rpm) |  |
| Max. Torque (Nm@rpm) |  |
| Air cleaner |  |
| Oil filter |  |
| Fuel filter |  |
| Capacity of cooling system |  |
| Oil sump capacity (l) |  |
| Weight of engine (kg) (complete) |  |
| Radiator frontal area (core area) |  |
| Catalytic converter details, if fitted |  |
| Clutch |  |
| Type |  |
| Outside diameter |  |
| Gear box |  |
| Make |  |
| Model & identification |  |
| Type |  |
| No. of gears |  |

Table 14 of AIS-007 (Revision 5)

| Gear ratio 1st 2nd 3rd 4th 5th 6th Reverse |  |
| --- | --- |
| Front axle ratio |  |
| Rear axle ratio |  |
| Steering |  |
| Type |  |
| Steering wheel diameter (mm) |  |
| Ratio |  |
| No. of rotation of the wheel (Lock to lock) |  |
| Steered axle |  |
| Frame |  |
| Long member size (mm) |  |
| Number of cross members |  |
| Suspension |  |
| Type (Brief description) |  |
| Spring |  |
| Anti-roll bar |  |
| Shock absorbers |  |
| Brake |  |
| Service brake (Brief description) |  |
| Front |  |
| Rear |  |
| Total braking area (cm2) |  |
| Secondary brake (Brief description) |  |
| Parking brake (Brief description) |  |
| Wheels and tyres |  |
| Wheel rim size |  |
| Tyre size and ply rating |  |
| Dynamic rolling radius of tyre |  |
| Tyre pressure (front & rear) (kg/cm2) |  |
| Electrical system |  |
| System voltage (V) |  |
| Battery rating |  |
| Alternator type |  |
| Max. output |  |
| Wiping system (Brief description) |  |
| Wiper motor |  |

Table 14 of AIS-007 (Revision 5)

| Fuel tank |  |
| --- | --- |
| Material |  |
| Capacity (l) |  |
| Dimensions in travel mode |  |
| Wheel base (mm) |  |
| Overall width (mm) |  |
| Overall length (mm) |  |
| Overall height (mm) |  |
| Front track (mm) |  |
| Rear track (mm) |  |
| Min. ground clearance (mm) |  |
| Min. turning circle diameter (m) |  |
| Max. clearance circle diameter (m) |  |
| Weights |  |
| Unladen FAW, kg (FAW1, FAW2 etc.) |  |
| Unladen RAW, kg (RAW1, RAW2 etc.) |  |
| Unladen weight, kg (weight in travel mode with 90% fuel, accessories and tools) |  |
| Maximum gradeability (laden) |  |
| Maximum speed (kmph) |  |
| Seating capacity and layout |  |

Table 15 of AIS-007 (Revision 5)

DETAILED TECHNICAL SPECIFICATIONS FOR

CONSTRUCTION EQUIPMENT VEHICLES

| 1.0 | Details of Manufacturer |  |
| --- | --- | --- |
| 1.1 | Manufacturer's name and address |  |
| 1.2 | Telephone No. |  |
| 1.3 | Fax No. |  |
| 1.4 | E-mail ID |  |
| 1.5 | Contact person |  |
| 2.0 | Vehicle Data |  |
| 2.1 | Basic model |  |
| 2.2 | Variant(s) |  |
| 2.3 | Type |  |
| 2.4 | Engine No. |  |
| 2.5 | Chassis No. |  |
| 2.6 | Publications available (Owner's manual, service manual, spare parts list) |  |
| 3.0 | Performance |  |
| 3.1 | Max. speed (kmph) |  |
| 3.2 | Stopping distance (m) (From initial speed kmph) |  |
| 3.3 | Parking brake performance |  |
| 3.4 | Climbing performance (start & stop) |  |
| 3.5 | Min. turning circle diameter (m) |  |
| 4.0 | Weights |  |
| 4.1 | Vehicle kerb weight (kg) |  |
| 4.1.1 | Front axle (FAW1, FAW2 etc.) |  |
| 4.1.2 | Rear axle (RAW1, RAW2 etc.) |  |
| 4.1.3 | Total |  |
| 5.0 | Dimensions |  |
| 5.1 | Overall length (m) |  |
| 5.2 | Overall width (m) |  |
| 5.3 | Overall height (m) |  |
| 5.4 | Wheel base (m) |  |
| 5.5 | Tread (m) |  |
| 5.5.1 | Front wheel |  |
| 5.5.2 | Rear wheel |  |
| 5.6 | Min. road clearance (m) |  |
| 5.7 | Road clearance from floor (m) |  |

Table 15 of AIS-007 (Revision 5)

| 5.8 | Body overhang (m) |  |
| --- | --- | --- |
| 5.8.1 | Front end |  |
| 5.8.2 | Rear end |  |
| 5.9 | Gravity height (m) |  |
| 5.10 | Max. stable inclination angle |  |
| 5.10.1 | Left |  |
| 5.10.2 | Right |  |
| 5.11 | Riding capacity |  |
|  | Note : The essential characteristics of the Parent engine and the Engines falling in the same family are as given in the enclosed Annexure - 1. Clause 6.0 to Clause 27.0 are related to the characteristics of the parent engine. Clause A 6.0 to A 27.0 are related to the characteristics of every engine that falls within the same family. This may be filled separately for each engine. |
| 6.0 | Engine (Parent) |  |
| 6.1 | Type (NA/TC/TCIC, DI/IDI) |  |
| 6.2 | Manufacturer's name & Address of the Manufacturing Plant. |  |
| 6.3 | Working principle (four / two stroke) |  |
| 6.4 | Model name and identification |  |
| 6.5 | Type of fuel used |  |
| 6.6 | No.& Layout of cylinders & firing order |  |
| 6.7 | Swept volume (cc) |  |
| 6.8 | Bore (mm) |  |
| 6.9 | Stroke (mm) |  |
| 6.10 | Compression ratio (specify tolerance) |  |
| 6.11 | Engine performance (declared by the manufacturer) |  |
| 6.11.1 | Max. Gross power of engine on bench kW (Specify standard and tolerance) |  |
| 6.11.2 | Maximum Gross torque on bench Nm @ rpm |  |
| 6.11.3 | Engine RPM at max. Power (specify tolerance) |  |
|  | Note: In case of diesel engines the max. power and max. torque shall be specified as per conditions given in Chapter 6 of Part IV of Doc. MoSRTH / CMVR / TAP-115 / 116 Issue No 3. |
| 6.12 | Location of engine (Front / Rear) |  |

Table 15 of AIS-007 (Revision 5)

| 7.0 | Combustion |  |
| --- | --- | --- |
| 7.1 | Type of combustion chamber (Hemispherical / squish/others) |  |
| 7.2 | Drawings of combustion chamber and piston crown (mention drawing no) |  |
| 7.3 | Minimum cross section area of ports |  |
| 7.3.1 | Inlet (mm2) |  |
| 7.3.2 | Outlet (mm2) |  |
| 8.0 | Liquid cooling system |  |
| 8.1 | Nature of liquid and capacity |  |
| 8.2 | Circulating pump yes/no |  |
| 8.3 | Characteristics of Circulating pump or make(s) & type(s) |  |
| 8.3.1 | Drive ratio |  |
| 8.4 | Thermostat type and setting |  |
| 8.5 | Air ducting (std production) |  |
| 9.0 | Air Cooling system |  |
| 9.1 | Blower characteristics |  |
| 9.1.1 | Make(s) |  |
| 9.1.2 | Type(s) |  |
| 9.1.3 | Drive ratio(s) |  |
| 10.0 | Temperature regulating system (yes/no) |  |
| 10.1 | Brief description |  |
| 11.0 | Temperature permitted by manufacturer (0C) |  |
| 11.1 | Liquid cooling :- |  |
| 11.1.1 | Max. temp. at engine Outlet |  |
| 11.2 | Air cooling:- |  |
| 11.2.1 | Reference point |  |
| 11.2.2 | Max. temperature at reference point |  |
| 11.3 | Max. outlet temperature of the intercooled-air ( Location of measurement be specified ) |  |
| 11.4 | Max. exhaust temperature (in case of diesel engines, at the point in the exhaust pipe(s) adjacent in outlet flange(s) of exhaust manifolds) |

Table 15 of AIS-007 (Revision 5)

| 12.0 | Fuel temperature (0C) : |  |
| --- | --- | --- |
| 12.1 | Minimum |  |
| 12.2 | Maximum |  |
| 13.0 | Lubricant Temperature (0C) ( Location of measurement be specified ) |  |
| 13.1 | Minimum |  |
| 13.2 | Maximum |  |
| 14.0 | Intake system |  |
| 14.1 | Supercharger / Turbocharger – yes/no |  |
| 14.1.1 | Description of system |  |
| 14.1.2 | Make(s) |  |
| 14.1.3 | Type(s) & Part No. |  |
| 14.2 | Intake manifold |  |
| 14.2.1 | Description & Drawings |  |
| 14.3 | Air filter |  |
| 14.3.1 | Make |  |
| 14.3.2 | Type & Part No. |  |
| 14.3.3 | Dimensional drawing, with drawing number and part number |  |
| 14.4 | Intake silencer |  |
| 14.4.1 | Make |  |
| 14.4.2 | Type |  |
| 14.5 | Description & dimensional drawing of inlet pipe & their accessories (dash pot, heating device, additional air intake etc.) |  |
| 14.6 | Inter cooler |  |
| 14.6.1 | Make |  |
| 14.6.2 | Identification mark / & Part No. |  |
| 15.0 | Fuel feed |  |
| 15.1 | Injection system description |  |
| 15.2 | Working principle: intake manifold/ direct injection/ indirect injection/swirl chamber/others |  |
| 15.3 | Fuel Pump |  |
| 15.3.1 | Make(s) & Place / |  |

Table 15 of AIS-007 (Revision 5)

| 15.3.2 | Type(s) & Part No. |  |
| --- | --- | --- |
| 15.4 | Delivery mm3/per stroke at Rated speed and at Max Torque speed (specify tolerance) or characteristic diagram (specify tolerance) |  |
| 15.5 | Calibration procedure on engine/pump bench |  |
| 15.6 | Injection timing deg BTDC (specify tolerance) |  |
| 15.7 | Injection advance curve (attach the same) |  |
| 15.8 | Injection advance (specify the tolerance) |  |
| 15.9 | Injectors |  |
| 15.9.1 | Type, (mention holder, nozzle and assembly no(s)) |  |
| 15.9.2 | Make |  |
| 15.9.3 | Opening pressure (specify tolerance) or characteristic diagram |  |
| 15.9.4 | Injection piping |  |
| 15.9.5 | Length (mm) |  |
| 15.9.6 | Internal diameter (mm) |  |
| 16.0 | Device for recycling crank-case gases |  |
| 16.1 | Description & diagrams |  |
| 17.0 | Governor |  |
| 17.1 | Make(s) & |  |
| 17.2 | Type(s) |  |
| 17.3 | Cut off point under load (rpm) |  |
| 17.4 | Max. Speed without load (rpm) |  |
| 17.5 | Idle Speed (rpm) |  |
| 18.0 | Cold start device (starting aid) |  |
| 18.1 | Make(s) |  |
| 18.2 | Type(s) |  |
| 18.3 | System description |  |
| 19.0 | Starting System |  |
| 19.1 | Make(s) |  |
| 19.2 | Type(s) |  |
| 19.3 | System description |  |

Table 15 of AIS-007 (Revision 5)

| 20.0 | Valve timing / Port timing or equivalent data |  |
| --- | --- | --- |
| 20.1 | Max. lift of valves |  |
| 20.1.1 | Inlet (mm) |  |
| 20.1.2 | Exhaust (mm) |  |
| 20.2 | Angle of valves / port (w.r.t. top dead center) |  |
| 20.3 | Inlet |  |
| 20.3.1 | Opening |  |
| 20.3.2 | Closing |  |
| 20.4 | Exhaust |  |
| 20.4.1 | Opening |  |
| 20.4.2 | Closing |  |
| 20.5 | Transfer |  |
| 20.5.1 | Opening |  |
| 20.5.2 | Closing |  |
| 20.6 | Reference or setting ranges |  |
| 20.7 | Valve gap (Hot & Cold) |  |
| 20.7.1 | Inlet |  |
| 20.7.2 | Exhaust |  |
| 20.8 | Distribution by ports |  |
| 20.8.1 | Volume of crank-case cavity with piston at TDC |  |
| 20.8.2 | Description of reed valve if any with drawing |  |
| 20.8.3 | Description (with drawing) of inlet ports, scavenging and exhaust ports with corresponding timing. (The drawing should include one representing the inner surface of the cylinder) |  |
| 21.0 | Lubrication system |  |
| 21.1 | Description of system |  |
| 21.2 | Lubrication oil capacity lit |  |
| 21.3 | Position of lubricant reservoir |  |
| 21.4 | Lubricating oil grade |  |
| 21.5 | Feed system (pump, injection in to intake mixing with fuel etc.) |  |
| 21.6 | Lubricating pump |  |
| 21.6.1 | Make |  |
| 21.6.2 | Type |  |

Table 15 of AIS-007 (Revision 5)

| 21.7 | Mixture with fuel : yes/no, and if yes % |  |
| --- | --- | --- |
| 21.8 | Oil cooler : yes/no, and if yes Drawings/ makes & types |  |
| 22.0 | Electrical equipment |  |
| 22.1 | Generator/alternator characteristics (specify tolerance) or |  |
| 22.1.1 | Make |  |
| 22.1.2 | Type |  |
| 23.0 | Other engine driven auxiliaries: |  |
| 23.1 | Enumeration & brief description, if necessary |  |
| 24.0 | Idling System |  |
| 24.1 | Idling speed (rpm) (specify the tolerance) |  |
| 24.2 | Description of settings and relevant requirements |  |
| 25.0 | Additional requirements |  |
| 25.1 | Maximum permitted depression of air intake at characteristic place (Specify location of measurement) (kPa) |  |
| 25.2 | Exhaust back pressure at maximum Gross power and location of measurement (kPa) |  |
| 25.3 | Effective volume of exhaust -System (specify the tolerance & range) in liters (from exhaust manifold / TC outlet to tail pipe end), Enclose the exhaust system drawing and indicate the volume of each parts clearly. |  |
| 25.4 | Moment of inertia of combined flywheel & transmission at condition when no gear is engaged |  |
| 25.5 | Maximum rated speed (Specify the tolerance) |  |
| 25.6 | Minimum rated speed (Specify the tolerance) |  |
| 25.7 | Power absorbed by fan kW (specify the tolerance) |  |
| 25.8 | Max. Gross torque on bench, Nm@ rpm |  |
| 25.9 | Declared speed and powers of the engine submitted for type approval (Speeds to be agreed with the testing agency) |  |

Table 15 of AIS-007 (Revision 5)

| Measurement point* | Engine speed rpm | Gross Power kW** |  |
| --- | --- | --- | --- |
| * | See Chapter 3 of Part IV of Doc.MoSRTHST/CMVR/TAP115/116 Issue No 3. |
| ** | Gross power according to Chapter 6 of Part IV of Doc.MoSRTHST/CMVR/TAP115/116 Issue No 3. |
| 26.0 | Exhaust system : |  |
| 26.1 | Silencer, Number, Type and make |  |
| 26.2 | Identification mark (If proprietary) / Part No. |  |
| 26.3 | Internal dia. of exhaust pipe |  |
| 26.4 | Description (with a general arrangement , dimensional drawing of exhaust system along with its routing indicating the lengths of exhaust pipe, tail pipe and exhaust outlet location) |  |
| 26.5 | Minimum distance between exhaust pipe(s) and the fuel line |  |
| 27.0 | Additional emission control devices, such as catalytic converter etc. (if any & if not covered by another heading) |  |
| 27.1 | Catalyser make, Number |  |
| 27.2 | Identification Mark / Part No |  |
| 27.3 | Type of catalytic action (One/two/three way) |  |
| 27.4 | Total charge of precious metal (g/vehicle) |  |
| 27.5 | Relative concentration (%) |  |
| 27.5.1 | Platinum |  |
| 27.5.2 | Rhodium |  |
| 27.5.3 | Palladium |  |
| 27.6 | Substrate (Monolythic metal/ Ceramic/ honeycomb) |  |
| 27.7 | Cell density (cells per sq. inch) |  |
| 27.8 | Type of casing for catalyser |  |
| 27.9 | Diagram indicating the arrangement and position of catalytic converter w.r.t. exhaust manifold) |  |

Table 15 of AIS-007 (Revision 5)

| 27.10 | Electronic Control Unit (ECU) |  |
| --- | --- | --- |
| 27.10.1 | Make |  |
| 27.10.2 | Identification mark |  |
| 27.10.3 | Calibration Identification No. |  |
| 27.11 | Secondary Air Injection |  |
| 27.11.1 | Make |  |
| 27.11.2 | Identification mark |  |
| 27.12 | Exhaust Gas Recirculating System |  |
| 27.12.1 | Make |  |
| 27.12.2 | Type |  |
| 27.12.3 | Identification mark |  |
|  | Note : The following Clause A 6.0 to A 27.0 are to be filled separately for each of the engines that fall within the same family : |
| A6.0 | Engine (Type within the Family) |  |
| A6.1 | Type (NA/TC/TCIC, DI/IDI) |  |
| A6.2 | Manufacturer's name & Manufacturing Plant address. |  |
| A6.3 | Working principle (four / two stroke) |  |
| A6.4 | Model name and identification |  |
| A6.5 | Type of fuel used |  |
| A6.6 | No.& Layout of cylinders & firing order |  |
| A6.7 | Swept volume (cc) |  |
| A6.8 | Bore(mm) |  |
| A6.9 | Stroke (mm) |  |
| A6.10 | Compression ratio (specify tolerance) |  |
| A6.11 | Engine performance (declared by the manufacturer,) |  |
| A6.11.1 | Max. Gross power of engine on bench (kW) (Specify standard and tolerance) |  |
| A6.11.2 | Maximum Gross torque on bench (Nm @ rpm) |  |
| A6.11.3 | Engine RPM at max. Power (specify tolerance) |  |
|  | Note: In case of diesel engines the max. power and max. torque shall be specified as per conditions given in Chapter 6 of Part IV of Doc. MoSRTH / CMVR / TAP-115 / 116 Issue No 3. |
| A6.12 | Location of engine (Front / Rear) |  |

Table 15 of AIS-007 (Revision 5)

| A7.0 | Combustion : |  |
| --- | --- | --- |
| A7.1 | Type of combustion chamber (Hemispherical / squish/others) |  |
| A7.2 | Drawings of combustion chamber and piston crown (mention drawing no) |  |
| A7.3 | Minimum cross section area of ports |  |
| A7.3.1 | Inlet mm2 |  |
| A7.3.2 | Outlet mm2 |  |
| A8.0 | Liquid cooling system |  |
| A8.1 | Nature of liquid and capacity |  |
| A8.2 | Circulating pump yes/no |  |
| A8.3 | Characteristics of Circulating pump or make(s) & type(s) |  |
| A8.3.1 | Drive ratio |  |
| A8.4 | Thermostat type and setting |  |
| A9.0 | Air Cooling system |  |
| A9.1 | Blower characteristics |  |
| A9.1.1 | Make(s) |  |
| A9.1.2 | Type(s) |  |
| A9.1.3 | Drive ratio(s) |  |
| A9.2 | Air ducting(std production) |  |
| A10.0 | Temperature regulating system (yes/no) |  |
| A11.0 | Temperature permitted by manufacturer (0C) |  |
| A11.1 | Liquid cooling:- |  |
| A11.1.1 | Max. temp. at engine Outlet |  |
| A11.2 | Air cooling:- |  |
| A11.2.1 | Reference point |  |
| A11.2.2 | Max. temperature at reference point |  |
| A11.3 | Max. outlet temperature of the intercooled - air (Location of measurement to be specified) |  |
| A11.4 | Maximum exhaust temperature (0C) |  |
| A11.4.1 | Max. exhaust temperature (in case of diesel engines, at the point in the exhaust pipe(s) adjacent in outlet flange(s) of exhaust manifolds) |
| A12.0 | Fuel temperature (0C) |  |
| A12.1 | Minimum |  |
| A12.2 | Maximum |  |

Table 15 of AIS-007 (Revision 5)

| A13.0 | Lubricant Temperature (0C) (Location of measurement to be specified) |  |
| --- | --- | --- |
| A13.1 | Minimum |  |
| A13.2 | Maximum |  |
| A14.0 | Intake system |  |
| A14.1 | Supercharger / Turbocharger - yes/no |  |
| A14.1.1 | Description of system |  |
| A14.1.2 | Make(s) |  |
| A14.1.3 | Type(s) & Part No. |  |
| A14.2 | Intake manifold |  |
| A14.2.1 | Description & Drawings |  |
| A14.3 | Air filter |  |
| A14.3.1 | Make |  |
| A14.3.2 | Type & Part No. |  |
| A14.3.3 | Dimensional drawing, with drawing number and part number |  |
| A14.4 | Intake silencer |  |
| A14.4.1 | Make |  |
| A14.4.2 | Type |  |
| A14.5 | Description & diagrams of inlet pipe & their accessories (dash pot, heating device, additional air intake etc.) |  |
| A14.6 | Inter cooler |  |
| A14.6.1 | Make |  |
| A14.6.2 | Identification mark / & Part No. |  |
| A15.0 | Fuel feed |  |
| A15.1 | Injection system description |  |
| A15.2 | Working principle: intake manifold/ direct injection / indirect injection / swirl chamber/others |  |
| A15.3 | Fuel Pump |  |
| A15.3.1 | Make(s) & ( if imported) |  |
| A15.3.2 | Type(s) & Part No. |  |
| A15.4 | Delivery mm3/per stroke at Rated speed and at Max Torque speed (specify tolerance) or characteristic diagram (specify tolerance) |  |
| A15.5 | Calibration procedure on engine/pump bench |  |
| A15.6 | Injection timing deg BTDC (specify tolerance) |  |
| A15.7 | Injection advance curve (attach the same) |  |
| A15.8 | Injection advance (specify the tolerance) |  |

Table 15 of AIS-007 (Revision 5)

| A15.9 | Injectors |  |
| --- | --- | --- |
| A15.9.1 | Type, (mention Holder, Nozzle & assembly no(s)) |  |
| A15.9.2 | Make |  |
| A15.9.3 | Opening pressure (specify tolerance) or characteristic diagram |  |
| A15.9.4 | Injection piping |  |
| A15.9.5 | Length mm |  |
| A15.9.6 | Internal diameter (mm) |  |
| A16.0 | Device for recycling crank-case gases |  |
| A16.1 | Description & diagrams |  |
| A17.0 | Governor |  |
| A17.1 | Make(s) & |  |
| A17.2 | Type(s) |  |
| A17.3 | Cut off point under load (rpm) |  |
| A17.4 | Max. Speed without load (rpm) |  |
| A17.5 | Idle Speed (rpm) |  |
| A18.0 | Cold start device (starting aid) |  |
| A18.1 | Make(s) |  |
| A18.2 | Type(s) |  |
| A18.3 | System description |  |
| A19.0 | Starting System |  |
| A19.1 | Make(s) |  |
| A19.2 | Type(s) |  |
| A19.3 | System description |  |
| A20.0 | Valve timing / Port timing or equivalent data |  |
| A20.1 | Max. lift of valves |  |
| A20.1.1 | Inlet (mm) |  |
| A20.1.2 | Exhaust (mm) |  |
| A20.2 | Angle of valves / port (w.r.t. top dead center) |  |
| A20.3 | Inlet |  |
| A20.3.1 | Opening |  |
| A20.3.2 | Closing |  |
| A20.4 | Exhaust |  |
| A20.4.1 | Opening |  |
| A20.4.2 | Closing |  |
| A20.5 | Transfer |  |
| A20.5.1 | Opening |  |
| A20.5.2 | Closing |  |
| A20.6 | Reference or setting ranges |  |

Table 15 of AIS-007 (Revision 5)

| A20.7 | Valve gap (Hot & Cold) |  |
| --- | --- | --- |
| A20.7.1 | Inlet |  |
| A20.7.2 | Exhaust |  |
| A20.8 | Distribution by ports |  |
| A20.8.1 | Volume of crank-case cavity with piston at TDC |  |
| A20.8.2 | Description of reed valve if any with drawing |  |
| A20.8.3 | Description (with drawing) of inlet ports, scavenging and exhaust ports with corresponding timing. (The drawing should include one representing the inner surface of the cylinder) |  |
| A21.0 | Lubrication system |  |
| A21.1 | Description of system |  |
| A21.2 | Lubrication oil capacity lit |  |
| A21.3 | Position of lubricant reservoir |  |
| A21.4 | Lubricating oil grade |  |
| A21.5 | Feed system(pump, injection in to intake mixing with fuel etc.,) |  |
| A21.6 | Lubricating pump |  |
| A21.6.1 | Make |  |
| A21.6.2 | Type |  |
| A21.7 | Mixture with fuel : yes/no, and if yes % |  |
| A21.8 | Oil cooler : yes/no, and if yes Drawings/ makes & types |  |
| A22.0 | Electrical equipment |  |
| A22.1 | Generator/alternator characteristics (specify tolerance) or |  |
| A22.1.1 | Make |  |
| A22.1.2 | Type |  |
| A23.0 | Other engine driven auxiliaries |  |
| A23.1 | Enumeration & brief description, if necessary |  |
| A24.0 | Idling System |  |
| A24.1 | Idling speed (rpm) (specify the tolerance) |  |
| A24.2 | Description of settings and relevant requirements |  |
| A25.0 | Additional requirements |  |
| A25.1 | Maximum permitted depression of air intake at characteristic place, in kPa (Specify the location of measurement) |  |

Table 15 of AIS-007 (Revision 5)

| A25.2 | Exhaust back pressure at maximum Gross power and location of measurement (kPa) |  |
| --- | --- | --- |
| A25.3 | Effective volume of exhaust-System (specify the tolerance & range) in liters (from exhaust manifold / TC outlet to tail pipe end), Enclose the exhaust system drawing and indicate the volume of each parts clearly. |  |
| A25.4 | Moment of inertia of combined flywheel & transmission at condition when no gear is engaged |  |
| A25.5 | Maximum rated speed (Specify the tolerance) |  |
| A25.6 | Minimum rated speed (Specify the tolerance) |  |
| A25.7 | Power absorbed by fan (kW) (specify the tolerance) |  |
| A25.8 | Max. Gross torque on bench (Nm@ rpm) |  |
| A25.9 | Declared speed and powers of the engine submitted for type approval (Speeds to be agreed with the testing agency) |  |
| Measurement point* | Engine speed rpm | Gross Power kW** |  |
| * | See Chapter 3 of Part IV of Doc.MoSRTHST/CMVR/TAP115/116 Issue No 3. |
| ** | Gross power according to Chapter 6 of Part IV of Doc.MoSRTHST/CMVR/TAP115/116 Issue No 3. |
| A26.0 | Exhaust system |  |
| A26.1 | Silencer, Number, Type and make |  |
| A26.2 | Identification mark (If proprietary) / Part No. |  |
| A26.3 | Internal dia. of exhaust pipe |  |
| A26.4 | Description (with a general arrangement dimensional drawing of exhaust system along with its routing indicating the lengths of exhaust pipe, tail pipe and exhaust outlet location) |  |
| A26.5 | Minimum distance between exhaust pipe(s) and the fuel line |  |

Table 15 of AIS-007 (Revision 5)

| A27.0 | Additional emission control devices, such as catalytic converter etc. (if any & if not covered by another heading) |  |
| --- | --- | --- |
| A27.1 | Catalyser make, Number |  |
| A27.2 | Identification Mark / Part No. |  |
| A27.3 | Type of catalytic action (One/two/three way) |  |
| A27.4 | Total charge of precious metal (g/vehicle) |  |
| A27.5 | Relative concentration (%) |  |
| A27.5.1 | Platinum |  |
| A27.5.2 | Rhodium |  |
| A27.5.3 | Palladium |  |
| A27.6 | Substrate (Monolythic metal/ Ceramic/ honeycomb) |  |
| A27.7 | Cell density (cells per sq. inch) |  |
| A27.8 | Type of casing for catalyser |  |
| A27.9 | Diagram indicating the arrangement and position of catalytic converter w.r.t. exhaust manifold) |  |
| A27.10 | Electronic Control Unit (ECU) |  |
| A27.10.1 | Make |  |
| A27.10.2 | Identification mark |  |
| A27.10.3 | Calibration Identification No. |  |
| A27.11 | Secondary Air Injection |  |
| A27.11.1 | Make |  |
| A27.11.2 | Identification mark |  |
| A27.12 | Exhaust Gas Recirculating System |  |
| A27.12.1 | Make |  |
| A27.12.2 | Type |  |
| A27.12.3 | Identification mark |  |
| 28.0 | Fuel tank |  |
| 28.1 | Name of producer |  |
| 28.2 | Material |  |
| 28.3 | Capacity |  |
| 28.4 | Position |  |
| 29.0 | Transmission system |  |
| 29.1 | Mechanism from engine to transmission |  |

Table 15 of AIS-007 (Revision 5)

| 29.2 | Reduction ratio from engine to transmission |  |
| --- | --- | --- |
| 29.3 | Clutch |  |
| 29.3.1 | Name of producer |  |
| 29.3.2 | Type |  |
| 29.3.3 | Control system |  |
| 29.4 | Facing |  |
| 29.4.1 | Name of producer |  |
| 29.4.2 | Dimension (mm) |  |
| 29.4.3 | Area (cm2) |  |
| 29.4.4 | Number of operating faces |  |
| 29.4.5 | Material |  |
| 29.5 | Transmission clutch fluid capacity |  |
| 29.6 | Booster type |  |
| 29.6.1 | Name of producer |  |
| 29.6.2 | Type |  |
| 30.0 | Control system |  |
| 30.1 | Gear ratio |  |
| 30.1.1 | 1st |  |
| 30.1.2 | 2nd |  |
| 30.1.3 | 3rd |  |
| 30.1.4 | 4th |  |
| 30.1.5 | 5th |  |
| 30.1.6 | 6th |  |
| 30.1.7 | Reverse 1st |  |
| 30.2 | Sub transmission |  |
| 30.2.1 | Type |  |
| 30.3 | Gear ratio |  |
| 30.3.1 | High |  |
| 30.3.2 | Low |  |
| 30.4 | Propeller shaft |  |
| 30.5 | Length inside & outside diameter, mm |  |
| 30.5.1 | 1st |  |
| 30.5.2 | 2nd |  |
| 30.5.3 | 3rd |  |
| 30.5.4 | 4th |  |
| 30.6 | Universal joint |  |

Table 15 of AIS-007 (Revision 5)

| 30.6.1 | Type |  |
| --- | --- | --- |
| 30.6.2 | Number |  |
| 30.7 | Crown wheel |  |
| 30.7.1 | Type |  |
| 30.7.2 | Reduction ratio |  |
| 30.8 | Differential |  |
| 30.8.1 | Type |  |
| 30.9 | Running system |  |
| 30.9.1 | Front axle |  |
| 30.9.1.1 | Type |  |
| 30.9.1.2 | Toe-in (mm) |  |
| 30.9.1.3 | Camber angle |  |
| 30.9.1.4 | Caster angle |  |
| 30.9.1.5 | King pin angle |  |
| 30.9.1.6 | Trial (mm) |  |
| 30.9.2 | Rear axle |  |
| 30.9.2.1 | Type |  |
| 30.9.2.2 | Toe-in (mm) |  |
| 30.9.2.3 | Camber angle |  |
| 30.9.2.4 | Caster angle |  |
| 30.9.2.5 | King pin angle |  |
| 30.9.2.6 | Trial (mm) |  |
| 31.0 | Steering system |  |
| 31.1 | Type |  |
| 31.2 | Steering wheel Position |  |
| 31.3 | Outside diameter mm |  |
| 31.4 | Maximum number of rotations of steering wheel from lock to lock |  |
| 31.5 | Type of axis & joint |  |
| 31.6 | Steering gear type |  |
| 31.7 | Steering gear ratio |  |
| 31.8 | Steering angle |  |
| 31.8.1 | Inside |  |
| 31.8.2 | Outside |  |
| 31.9 | Booster |  |
| 31.9.1 | Name of producer |  |
| 31.9.2 | Type |  |

Table 15 of AIS-007 (Revision 5)

| 31.9.3 | Kind of oil |  |
| --- | --- | --- |
| 31.9.4 | Oil capacity (l) |  |
| 31.10 | Locking device |  |
| 31.10.1 | Name of producer |  |
| 31.10.2 | Type |  |
| 31.10.3 | Mounting position |  |
| 32.0 | Tyres |  |
| 32.1 | No. and arrangement of wheels |  |
| 32.1.1 | Front |  |
| 32.1.2 | Rear |  |
| 32.1.3 | Others |  |
| 32.2 | Tyre type (Radial/cross ply), size & ply rating |  |
| 32.2.1 | Front wheel |  |
| 32.2.2 | Rear wheel |  |
| 32.2.3 | Other |  |
| 32.3 | Rolling radius (mm) |  |
| 32.3.1 | Static |  |
| 32.3.2 | Dynamic (if data is available) |  |
| 32.4 | Inflation pressure – Unladen (kg/cm2 / kPa) |  |
| 32.4.1 | Front |  |
| 32.4.2 | Rear |  |
| 32.4.3 | Other |  |
| 32.5 | Inflation pressure – Laden (kg/cm2 / kPa ) |  |
| 32.5.1 | Front |  |
| 32.5.2 | Rear |  |
| 32.5.3 | Other |  |
| 32.6 | Makes: |  |
| 32.7 | Tread Wear Indicator, Provided (Yes/No) |  |
| 32.8 | Month & Year code of manufacture, Provided (Yes/No) |  |
| 32.9 | Maximum loading capacity, Provided (Yes/No) |  |
| 33.0 | Wheel rim |  |
| 33.1 | Size |  |
| 33.1.1 | Front |  |

Table 15 of AIS-007 (Revision 5)

| 33.1.2 | Rear |  |
| --- | --- | --- |
| 33.1.3 | Others |  |
| 33.2 | Name of manufacturer |  |
| 33.3 | Identification mark |  |
| 33.4 | Pitch circle dia. of mounting bolts (mm) |  |
| 33.5 | Number of mounting bolts |  |
| 33.6 | Material (Steel/ Aluminum alloy etc.) |  |
| 34.0 | Braking system |  |
| 34.1 | Service brake (Description) |  |
| 34.1.1 | Name of producer |  |
| 34.1.2 | Type |  |
| 34.2 | Secondary brake (Description) |  |
| 34.2.1 | Name of producer |  |
| 34.2.2 | Type |  |
| 34.3 | Control system & braking wheel |  |
| 34.4 | Dimensions of lining or pad, ( L x W x t ) |  |
| 34.4.1 | Front wheels (mm) |  |
| 34.4.2 | Rear wheels (mm) |  |
| 34.5 | Area of lining or pad (cm2 ) |  |
| 34.5.1 | Front wheels (cm2) |  |
| 34.5.2 | Rear wheels (cm2) |  |
| 34.6 | Brake drum or disc effective diameter (mm) |  |
| 34.6.1 | Front wheel |  |
| 34.6.2 | Rear wheel |  |
| 34.7 | Lining or pad |  |
| 34.7.1 | Name of producer |  |
| 34.7.2 | Material (Asbestos / Asbestos free) |  |
| 34.8 | Master cylinder or brake valve |  |
| 34.8.1 | Name of producer |  |
| 34.8.2 | Type |  |
| 34.9 | Inner diameter of master cylinder (mm) |  |
| 34.10 | Type of supply tank |  |
| 34.11 | Inner diameter of wheel cylinder or brake piston cap |  |
| 34.11.1 | Front wheel |  |
| 34.11.2 | Rear wheel |  |
| 34.12 | Booster |  |
| 34.12.1 | Name of producer |  |

Table 15 of AIS-007 (Revision 5)

| 34.12.2 | Type |  |
| --- | --- | --- |
| 34.12.3 | Magnification |  |
| 34.13 | Air compressor & others |  |
| 34.14 | Vacuum or air |  |
| 34.15 | Air pressure (kg/cm2) |  |
| 34.16 | Type of vacuum pump or air compressor |  |
| 34.17 | Type of pressure regulator |  |
| 34.18 | Tank |  |
| 34.18.1 | Position |  |
| 34.18.2 | Capacity (l) |  |
| 34.19 | Brake pipe |  |
| 34.19.1 | Name of producer |  |
| 34.19.2 | Material |  |
| 34.19.3 | Rust proof treatment |  |
| 34.20 | Brake hose (Hydraulic) |  |
| 34.20.1 | Make |  |
| 34.20.2 | Identification mark / Part Number |  |
| 34.30.3 | Length of hose (mm) |  |
| 34.20.4 | Nominal bore diameter (mm) |  |
| 34.20.5 | End fitting type |  |
| 34.20.6 | Material |  |
| 34.21 | Brake fluid |  |
| 34.21.1 | Name of manufacturer |  |
| 34.21.2 | Trade name |  |
| 34.21.3 | Specification / grade as per Indian standard |  |
| 34.22 | Braking force (stepping force kg) |  |
| 34.23 | Type of braking force control system |  |
| 34.24 | Warning device for braking |  |
| 34.24.1 | Type |  |
| 34.25 | Operation pressure (kg./cm2 ) |  |
| 34.26 | Type of safety device |  |
| 34.27 | Parking brake |  |
| 34.27.1 | Name of producer |  |
| 34.27.2 | Type |  |
| 34.27.3 | Braking wheel |  |
| 34.28 | Lining |  |
| 34.28.1 | Name of producer |  |
| 34.28.2 | Dimension of lining or pad (L x W x t) |  |
| 34.28.2.1 | Front wheel (mm) |  |

Table 15 of AIS-007 (Revision 5)

| 34.28.2.2 | Rear wheel (mm) |  |
| --- | --- | --- |
| 34.28.3 | Area of lining pad |  |
| 34.28.3.1 | Front |  |
| 34.28.3.2 | Rear |  |
| 34.28.4 | Material |  |
| 34.29 | Diameter of brake drum, mm |  |
| 34.30 | Braking force (Operation force kg.) |  |
| 34.31 | Auxiliary brake |  |
| 34.31.1 | Type |  |
| 34.31.2 | Performance |  |
| 34.32 | Emergency brake |  |
| 34.32.1 | Type |  |
| 34.32.2 | Performance |  |
| 34.33 | Separate brake |  |
| 34.33.1 | Type |  |
| 34.33.2 | Performance |  |
| 35.0 | Suspension system |  |
| 35.1 | Front axle |  |
| 35.1.1 | Type of suspension |  |
| 35.1.2 | Type of spring |  |
| 35.1.3 | Dimension of main spring (mm) |  |
| 35.1.3.1 | Stack |  |
| 35.1.3.2 | Flat length |  |
| 35.1.3.3 | Free camber |  |
| 35.1.3.4 | Dimension of auxiliary spring |  |
| 35.2 | Rear axle |  |
| 35.2.1 | Type of suspension |  |
| 35.2.2 | Type of spring |  |
| 35.2.3 | Dimension of main spring |  |
| 35.2.3.1 | Stack |  |
| 35.2.3.2 | Flat length |  |
| 35.2.3.3 | Free camber |  |
| 35.2.3.4 | Dimension of auxiliary spring |  |
| 35.3 | Type of shock absorber |  |
| 35.3.1 | Front wheel |  |
| 35.3.2 | Rear wheel |  |
| 35.4 | Type of stabilizer |  |
| 35.4.1 | Front wheel |  |
| 35.4.2 | Rear wheel |  |

Table 15 of AIS-007 (Revision 5)

| 36.0 | Chassis frame |  |
| --- | --- | --- |
| 36.1 | Type |  |
| 36.2 | Cross sectional view |  |
| 36.3 | Dimension, mm |  |
| 36.4 | Type of side protection device |  |
| 37.0 | Windscreen wiping system |  |
| 37.1 | Wind screen wiper |  |
| 37.1.1 | Type (manual/power) |  |
| 37.1.2 | No. of wipers |  |
| 37.2 | Wiper motor |  |
| 37.2.1 | Name of manufacturer |  |
| 37.2.2 | Type and identification |  |
| 37.2.3 | Rated voltage |  |
| 37.2.4 | Number of sweep Frequencies |  |
| 37.2.5 | Highest sweep frequency (cycles/min) |  |
| 37.2.6 | Lowest sweep frequency (cycles/min) |  |
| 37.3 | Wiper arm |  |
| 37.3.1 | Length |  |
| 37.3.2 | Manufacturer and Identification |  |
| 37.4 | Wiper blade |  |
| 37.4.1 | Length |  |
| 37.4.2 | Manufacturer and Identification |  |
| 37.4.3 | Rubber material |  |
| 37.5 | Type of fixing (as per IS 7827) |  |
| 37.6 | H point |  |
| 37.7 | Windscreen washing system |  |
| 37.8 | Type |  |
| 37.9 | Make |  |
| 37.10 | Defroster |  |
| 37.11 | Type |  |
| 37.12 | Make |  |
| 37.13 | Drawing indicating the seat back angle, seat travel, H point, Rake angle ,F point, steering wheel position and the related dimensions (Ref : Figure 1 and Figure 2 of AIS-011) |  |

Table 15 of AIS-007 (Revision 5)

| 38.0 | Equipment for safety |  |
| --- | --- | --- |
| 38.1 | Seat belt anchorages |  |
| 38.1.1 | Name of producer |  |
| 38.1.2 | Type |  |
| 38.1.3 | Number |  |
| 38.2 | Seat belt |  |
| 38.2.1 | Name of producer |  |
| 38.2.2 | Type |  |
| 38.2.3 | Number |  |
| 38.3 | Head restraint |  |
| 38.3.1 | Name of producer |  |
| 38.3.2 | Type |  |
| 38.3.3 | Number |  |
| 38.4 | Type of room safety device |  |
| 38.5 | Type of air conditioner |  |
| 38.6 | Position of emergency exit |  |
| 38.7 | Type of device preventing vehicle starting with door opened |  |
| 39.0 | Safety Glass |  |
| 39.1 | Front wind shield |  |
| 39.1.1 | Name of producer |  |
| 39.1.2 | Type |  |
| 39.1.3 | Thickness, mm |  |
| 39.1.4 | Radius of curvature if curved |  |
| 39.2 | Glasses other than front wind shield |  |
| 39.2.1 | Name of producer |  |
| 39.2.2 | Type |  |
| 39.2.3 | Thickness |  |
| 39.2.4 | Radius of curvature if curved |  |
| 40.0 | Rear view mirror |  |
| 40.1 | Left |  |
| 40.1.1 | Name of producer |  |
| 40.1.2 | Type |  |
| 40.1.3 | Dimension & radius of curvature (mm) |  |
| 40.2 | Right |  |
| 40.2.1 | Name of producer |  |
| 40.2.2 | Type |  |
| 40.2.3 | Dimension & radius of curvature (mm) |  |
| 40.3 | Inside |  |
| 40.3.1 | Name of producer |  |

Table 15 of AIS-007 (Revision 5)

| 40.3.2 | Type |  |
| --- | --- | --- |
| 40.3.3 | Dimension & radius of curvature (mm) |  |
| 41.0 | Horn |  |
| 41.1 | Name of producer |  |
| 41.2 | Type |  |
| 41.3 | Operating voltage |  |
| 41.4 | Identification No. / Part No. |  |
| 43.5 | Number |  |
| 42.0 | Controls (Specify method of operation) |  |
| 42.1 | Ignition |  |
| 42.2 | Horn |  |
| 42.3 | Lamps (Head lamp, Tail lamp, Parking lamp and Number plate lamp) |  |
| 42.4 | Turn signal |  |
| 42.5 | Transmission shift lever |  |
| 42.6 | Wind shield wiper |  |
| 42.7 | High beam/low beam |  |
| 42.8 | Parking brake |  |
| 42.9 | Master switch for electrical |  |
| 42.10 | Hazard warning signal |  |
| 42.11 | Service Brake |  |
| 42.12 | Accelerator Pedal (Floor hinged/hanging type) |  |
| 42.13 | Others |  |
| 43.0 | Displays and tell tales |  |
|  | (Indicate the type of tell tales provided and whether they are symbols or letters) |
| 43.1 | Head lamp – upper / lower control |  |
| 43.2 | Ignition cut-off |  |
| 43.3 | Turn signal |  |
| 43.4 | Fuel Gauge |  |
| 43.5 | Engine coolant temperature |  |
| 43.6 | Low oil pressure |  |
| 43.7 | High beam indicator |  |
| 43.8 | Electrical charge indicator |  |
| 43.9 | Brake failure |  |
| 43.10 | Battery Charging |  |
| 43.11 | Engine oil |  |
| 43.12 | Horn |  |
| 43.13 | Speedometer |  |
| 43.14 | Odometer |  |

Table 15 of AIS-007 (Revision 5)

| 44.0 | Auto lamps (bulbs) |  |
| --- | --- | --- |
| 44.1 | Head lamp bulb (main and dip) |  |
| 44.1.1 | Make |  |
| 44.1 | Designation as per AIS-034 |  |
| 44.2 | Parking Lamp bulb – Front |  |
| 44.2.1 | Make |  |
| 44.3 | Designation as per AIS-034 |  |
| 44.4 | Parking Lamp bulb – Rear |  |
| 44.4.1 | Make |  |
| 44.4.2 | Designation as per AIS-034 |  |
| 44.5 | Direction indicator lamp bulb - front |  |
| 44.5.1 | Make |  |
| 44.5.2 | Designation as per AIS-034 |  |
| 44.6 | Direction indicator lamp bulb - rear |  |
| 44.6.1 | Make |  |
| 44.6.2 | Designation as per AIS-034 |  |
| 44.7 | Direction indicator lamp bulb - side |  |
| 44.7.1 | Make |  |
| 44.7.2 | Designation as per AIS-034 |  |
| 44.8 | Front Position Lamp bulb |  |
| 44.8.1 | Make |  |
| 44.8.2 | Designation as per AIS-034 |  |
| 44.9 | Rear Position Lamp ( tail lamp )Bulb |  |
| 44.9.1 | Make |  |
| 44.9.2 | Designation as per AIS-034 |  |
| 44.10 | Stop lamp bulb |  |
| 44.10.1 | Make |  |
| 44.10.2 | Designation as per AIS-034 |  |
| 44.11 | Number plate lamp bulb |  |
| 44.11.1 | Make |  |
| 44.11.2 | Designation as per AIS-034 |  |
| 44.12 | End out Marker bulb |  |
| 44.12.1 | Make |  |

Table 15 of AIS-007 (Revision 5)

| 44.12.2 | Designation as per AIS-034 |  |
| --- | --- | --- |
| 44.13 | Reversing lamp bulb |  |
| 44.13.1 | Make |  |
| 44.13.2 | Designation as per AIS-034 |  |
| 44.14 | Stop Lamp Bulb (S3) |  |
| 44.14.1 | Make |  |
| 44.14.2 | Designation as per AIS-034 |  |
| 44.15 | Front Fog Lamp Bulb |  |
| 44.15.1 | Make |  |
| 44.15.2 | Designation as per AIS-034 |  |
| 44.16 | Rear Fog Lamp Bulb |  |
| 44.16.1 | Make |  |
| 44.16.2 | Designation as per AIS-034 |  |
| 44.17 | Side Marker Lamp Bulb |  |
| 44.17.1 | Make |  |
| 44.17.2 | Designation as per AIS-034 |  |
| 45.0 | Lighting equipment |  |
| 45.1 | Head lamp |  |
| 45.1.1 | Main beam |  |
| 45.1.1.1 | Make |  |
| 45.1.1.2 | Type of lens (Glass / Plastic) |  |
| 45.1.1.3 | Identification No. / Part No. |  |
| 45.1.1.4 | Number and Colour of Lens |  |
| 45.1.2 | Dipped beam |  |
| 45.1.2.1 | Make |  |
| 45.1.2.2 | Type of lens (Glass / Plastic) |  |
| 45.1.2.3 | Identification No. / Part No. |  |
| 45.1.2.4 | Number and Colour of Lens |  |
| 45.2 | Front Fog Lamp |  |
| 45.2.1 | Make |  |
| 45.2.2 | Type of lens (Glass / Plastic) |  |
| 45.2.3 | Identification No. / Part No. |  |
| 45.2.4 | Number and Colour of Lens |  |

Table 15 of AIS-007 (Revision 5)

| 45.3 | Rear Fog Lamp |  |
| --- | --- | --- |
| 45.3.1 | Make |  |
| 45.3.2 | Type of lens (Glass / Plastic) |  |
| 45.3.3 | Identification No. / Part No. |  |
| 45.3.4 | Number and Colour of Lens |  |
| 45.4 | Side Marker lamps |  |
| 45.4.1 | Make |  |
| 45.4.2 | Type of lens (Glass / Plastic) |  |
| 45.4.3 | Identification No. / Part No. |  |
| 45.4.4 | Number and colour of Lens |  |
| 45.5 | Registration Plate lamp |  |
| 45.5.1 | Make |  |
| 45.5.2 | Type of lens (Glass / Plastic) |  |
| 45.5.3 | Identification No. / Part No. |  |
| 45.5.4 | Number and colour of Lens |  |
| 45.6 | Position lamp / Parking Lamp - Front |  |
| 45.6.1 | Front Position Lamp |  |
| 45.6.1.1 | Make |  |
| 45.6.1.2 | Type of lens (Glass / Plastic) |  |
| 45.6.1.3 | Identification No. / Part No. |  |
| 45.6.1.4 | Number and colour of Lens |  |
| 45.6.2 | Front Parking Lamp |  |
| 45.6.2.1 | Make |  |
| 45.6.2.2 | Type of lens (Glass / Plastic) |  |
| 45.6.2.3 | Identification No. / Part No. |  |
| 45.6.2.4 | Number and colour of Lens |  |
| 45.7 | Position lamp / Parking Lamp - Rear |  |
| 45.7.1 | Rear Position Lamp |  |
| 45.7.1.1 | Make |  |
| 45.7.1.2 | Type of lens (Glass / Plastic) |  |
| 45.7.1.3 | Identification No. / Part No. |  |
| 45.7.1.4 | Number and colour of Lens |  |
| 45.7.2 | Rear Parking Lamp |  |
| 45.7.2.1 | Make |  |
| 45.7.2.2 | Type of lens (Glass / Plastic) |  |
| 45.7.2.3 | Identification No. / Part No. |  |
| 45.7.2.4 | Number and colour of Lens |  |

Table 15 of AIS-007 (Revision 5)

| 45.8 | Stop lamp (S1 / S2) |  |
| --- | --- | --- |
| 45.8.1 | Make |  |
| 45.8.2 | Type of lens (Glass / Plastic) |  |
| 45.8.3 | Identification No. / Part No. |  |
| 45.8.4 | Number and colour of Lens |  |
| 45.9 | Stop lamp (S3) for M1 category |  |
| 45.9.1 | Make |  |
| 45.9.2 | Type of lens ( Glass / Plastic ) |  |
| 45.9.3 | Identification No. / Part No. |  |
| 45.9.4 | Number and colour of lens |  |
| 45.10 | Reversing lamp |  |
| 45.10.1 | Make |  |
| 45.10.2 | Type of lens (Glass / Plastic) |  |
| 45.10.3 | Identification No. / Part No. |  |
| 45.10.4 | Number and colour of Lens |  |
| 45.11 | Direction indicator Lamp |  |
| 45.11.1 | Front |  |
| 45.11.1.1 | Make |  |
| 45.11.1.2 | Type of lens (Glass / Plastic) |  |
| 45.11.1.3 | Identification No. / Part No. |  |
| 45.11.1.4 | Number and colour of Lens |  |
| 45.11.2 | Rear |  |
| 45.11.2.1 | Make |  |
| 45.11.2.2 | Type of lens (Glass / Plastic) |  |
| 45.11.2.3 | Identification No. / Part No. |  |
| 45.11.2.4 | Number and colour of Lens |  |
| 45.11.3 | Side |  |
| 45.11.3.1 | Make |  |
| 45.11.3.2 | Type of lens (Glass / Plastic) |  |
| 45.11.3.3 | Identification No. / Part No. |  |
| 45.11.3.4 | Number and colour of Lens |  |
| 45.11.4 | Type of flasher |  |
| 45.12 | Hazard warning signal |  |
| 45.12.1 | Front |  |
| 45.12.1.2 | Make |  |
| 45.12.1.3 | Type of lens ( Glass / Plastic ) |  |
| 45.12.1.4 | Identification No. / Part No. |  |
| 45.12.1.5 | Number and Colour of lens |  |
| 45.12.2 | Rear |  |

Table 15 of AIS-007 (Revision 5)

| 45.12.2.1 | Make |  |
| --- | --- | --- |
| 45.12.2.2 | Type of lens ( Glass / Plastic ) |  |
| 45.12.2.3 | Identification No. / Part No. |  |
| 45.12.2.4 | Number and Colour of lens |  |
| 45.12.3 | Side |  |
| 45.12.3.1 | Make |  |
| 45.12.3.2 | Type of lens ( Glass / Plastic ) |  |
| 45.12.3.3 | Identification No. / Part No. |  |
| 45.12.3.4 | Number and Colour of lens |  |
| 46.0 | Reflector |  |
| 46.1 | Front |  |
| 46.1.1 | Name of producer |  |
| 46.1.2 | Type & identification |  |
| 46.1.3 | Number and colour |  |
| 46.1.4 | Performance |  |
| 46.2 | Rear |  |
| 46.2.1 | Name of producer |  |
| 46.2.2 | Type & identification |  |
| 46.2.3 | Number and colour |  |
| 46.2.4 | Performance |  |
| 46.3 | Side |  |
| 46.3.1 | Name of producer |  |
| 46.3.2 | Type & identification |  |
| 46.3.3 | Number and colour |  |
| 46.3.4 | Performance |  |
| 46.4 | Yellow flasher |  |
| 46.4.1 | Name of producer |  |
| 46.4.2 | Type & identification |  |
| 46.4.3 | Number and colour |  |
| 46.4.4 | Performance |  |
| 46.5 | Warning device horn |  |
| 46.5.1 | Name of producer |  |
| 46.5.2 | Type & identification |  |
| 46.5.3 | Number |  |
| 46.5.4 | Performance |  |
| 46.6 | Visibility ensuring device |  |
| 47.0 | Meters |  |
| 47.1 | Speedometer |  |
| 47.1.1 | Name of producer |  |

Table 15 of AIS-007 (Revision 5)

| 47.1.2 | Model |  |
| --- | --- | --- |
| 47.1.3 | Type |  |
| 47.1.4 | Performance & error |  |
| 47.2 | Odometer |  |
| 47.2.1 | Name of producer |  |
| 47.2.2 | Model |  |
| 47.2.3 | Type |  |
| 47.2.4 | Performance & error |  |
| 47.3 | Tachograph |  |
| 47.3.1 | Name of producer |  |
| 47.3.2 | Model |  |
| 47.3.3 | Type |  |
| 47.3.4 | Performance & error |  |
| 47.4 | Pressure gauge |  |
| 47.4.1 | Name of producer |  |
| 47.4.2 | Model |  |
| 47.4.3 | Type |  |
| 47.4.4 | Performance |  |
| 47.5 | Engine speed indicator |  |
| 47.5.1 | Name of producer |  |
| 47.5.2 | Model |  |
| 47.5.3 | Type |  |
| 47.5.4 | Performance |  |
| 47.6 | Fire extinguisher |  |
| 47.6.1 | Name of producer |  |
| 47.6.2 | Model |  |
| 47.6.3 | Type |  |
| 47.6.4 | Performance |  |
| 47.7 | Pressure container |  |
| 47.7.1 | Name of producer |  |
| 47.7.2 | Capacity of producer |  |
| 47.7.3 | Max. Pressure for use (kg/cm2) |  |
| 47.7.4 | Material |  |
| 47.8 | List of spare tools normally given with the vehicle |  |
| 48.0 | Additional information, if any |  |

### Annexure I

### ESSENTIAL CHARACTERISTICS OF THE ENGINE FAMILY

1.0  Common Parameters (1)

1.1. Combustion cycle: .

1.2. Cooling medium: .

1.3. Method of air aspiration: .

1.4. Combustion chamber type/design: .

1.5. Valve and porting - configuration, size and number:

1.6. Fuel system: .

1.7. Engine management systems:

Proof of identity pursuant to drawing number(s):

- charge cooling system: .

- exhaust gas recirculation (2): .

- water injection/emulsion (2): .

- air injection (2): .

1.8. Exhaust after-treatment system (2): .

Proof of identical (or lowest for the parent engine) ratio: system capacity/fuel delivery per stroke, pursuant to diagram number(s):

2.0  Engine Family Listing

2.1. Name of engine family: .

2.2. Specification of engines within this family:

|  |  |  |  |  | Parent engine |
| --- | --- | --- | --- | --- | --- |
| Engine Type |  |  |  |  |  |
| No of cylinders |  |  |  |  |  |
| Rated speed (rpm) |  |  |  |  |  |
| Rated Gross power (kW) |  |  |  |  |  |
| Maximum torque speed (rpm) |  |  |  |  |  |
| Fuel delivery per stroke at Rated Speed (mm3) |  |  |  |  |  |
| Fuel delivery per stroke at Max Torque Speed (mm3) |  |  |  |  |  |
| Maximum torque (Nm) |  |  |  |  |  |
| Low idle speed (rpm) |  |  |  |  |  |
| Cylinder displacement (in % of parent engine) |  |  |  |  | 100 |

(1) To be completed in conjunction with the specifications given in Annexure II

(2) If not applicable mark n.a.

Table 16 of AIS-007 (Revision 5)

BRIEF TECHNICAL SPECIFICATIONS FOR AGRICULTURAL / OTHER TRACTORS

(To be submitted by the Applicant/ Manufacturer to testing Agency in quadruplicate)

| 1.0 General description about manufacturer |  |
| --- | --- |
| 1.1 | Details of tractor Manufacturer |  |
| 1.1.1 | Name & Address of Manufacturer / Applicant |  |
| 1.1.2 | Telephone Number (s) |  |
| 1.1.3 | Fax Number (s) |  |
| 1.1.4 | E mail Address |  |
| 1.1.5 | Website |  |
| 1.2 | Details of Applicant, if other than manufacturer |  |
| 1.2.1 | Address of applicants |  |
| 1.2.2 | Telephone number(s) |  |
| 1.2.3 | Fax number(s) |  |
| 1.2.4 | E mail address |  |
| 1.2.5 | Website |  |
| 2.0 | Brief technical specification of tractor |  |
| 2.1 | Agricultural Tractor |  |
| 2.1.1 | Make |  |
| 2.1.2 | Model |  |
| 2.1.3 | Type |  |
| 2.1.4 | Chassis No. |  |
| 2.1.5 | Variant(s) if any – give Annexure |  |
| 2.1.6 | Max. PTO power, kW @ rpm (declared value) |  |
| 2.1.7 | Rated PTO power, kW @ rpm (declared value) |  |
| 3.0 | Prime Mover for the Tractor (ENGINE) |  |
| 3.1 | Make |  |
| 3. 2 | Model |  |
| 3. 3 | Type |  |
| 3. 4 | Engine No. |  |
| 3. 5 | Bore / stroke, mm |  |
| 3. 6 | Capacity (cc) |  |
| 3. 7 | No. of cylinders |  |
| 3. 8 | Rated engine speed (rpm) |  |
| 3. 9 | Max engine out put (kW @ rpm) (declared value) |  |
| 3.10 | Rated engine out put (kW @ rpm) (declared value) |  |

Table 16 of AIS-007 (Revision 5)

| 3.11 | Fuel Injection Pump: |  |
| --- | --- | --- |
| 3.11.1 | Make |  |
| 3.11.2 | Model |  |
| 3.12 | Governor: |  |
| 3.12.1 | Make |  |
| 3.12.2 | Model |  |
| 3.13 | Turbocharger (if fitted): |  |
| 3.13.1 | Make |  |
| 3.13.2 | Model |  |
| 3.14 | Air Cleaner Type |  |
| 3.15 | Cooling System : Liquid / Air Cooled |  |
| 3.15.1 | Type |  |
| 4.0 | Clutch : |  |
| 4.1 | Type : Main / PTO |  |
| 5.0 | Gear box : |  |
| 5.1 | Make |  |
| 5.2 | Model |  |
| 5.3 | Type |  |
| 6.0 | No. of speeds |  |
| 6.1 | - Forward |  |
| 6.2 | - Reverse |  |
| 7.0 | Maximum design speed ( as per AIS-116) kmph |  |
| 7.1 | Range of speeds (kmph) (at Rated Engine RPM) |  |
| 7.1.1 | - Forward |  |
| 7.1.2 | - Reverse |  |
| 8.0 | Steering |  |
| 8.1 | Type & Description |  |
| 8.2 | TCD |  |
| 8.3 | Steering wheel dia. (mm) |  |
| 9.0 | Wheel equipment & tyres |  |
| 9.1 | Front : |  |
| 9.1.1 | Tyre size & ply rating |  |
| 9.1.2 | Recommended tyre pressure, kPa (kgf/cm2) |  |
| 9.2 | Rear : |  |
| 9.2.1 | Tyre size & ply rating |  |
| 9.2.2 | Recommended tyre pressure, kPa (kgf/cm2) |  |
| 10 .0 | Brakes : |  |
| 10.1 | Service brake |  |

Table 16 of AIS-007 (Revision 5)

| 10.2 | Type, Mechanical/Hydraulic /Any other(describe briefly) |  |
| --- | --- | --- |
| 10.3 | Hand / Parking brake |  |
| 10.4 | Type and brief description |  |
| 11.0 | Electrical system of tractor |  |
| 11.1 | System voltage,( V) |  |
| 11.2 | Battery |  |
| 11.2.1 | - Capacity and rating | :--------Ah at 20hours discharge rate |
| 12.0 | Mass (kg) | Front | Rear | Total |
| 12.1 | Unballasted |  |  |  |
| 12.2 | Max permissible Ballasted |  |  |  |
| 13.0 | Seat (s) Seat (s) |  |
| 13.1 | Operator’s seat |  |
| 13.2 | - Location |  |
| 14.0 | Overall Dimension, (mm) |  |
| 14.1 | Overall length |  |
| 14.2 | Overall width |  |
| 14.3 | Overall height |  |
| 14.4 | Wheel Base |  |
| 14.5 | Min. ground clearance |  |
| 14.6 | Front Track width |  |
| 14.7 | Rear Track width |  |
| 15.0 | Fuel system |  |
| 15.1 | Type |  |
| 16.0 | Maximum Gradeability in degrees |  |

I, ---------------------------------------------------------- of M/s  ----------------------------------------- hereby declare that information given above in page no. 1 to 3 is as per design / drawings of the prototype / commercial model of tractor ------------------------------------------------  submitted for inspection / test and is complete and correct to the best of my knowledge and belief. I also understand that in case of any information furnished above is found to be not correct or incomplete, then among other actions, the certificate is liable to be cancelled. It is further declared that this machine has never been tested by any of the test agency as referred in Rule 126 of CMVR 1989. It is further declared that no application has been submitted to any other agencies as referred in Rule 126 of CMVR 1989.

Applicant / Manufacturer	          :

Signature of Authorised Signatory   :

Name	                                              :

Designation	                                 :

Place:

Date:

Countersigned:

Table 17 of AIS-007 (Revision 5)

DETAILED TECHNICAL SPECIFICATIONS FOR AGRICULTURAL TRACTORS

| 1.1 | General |  |
| --- | --- | --- |
| 1.1.1 | Name of Manufacturer / Importer |  |
| 1.1.2 | Address |  |
| 1.1.3 | Name of the contact Person |  |
| 1.1.4 | Telephone Numbers |  |
| 1.1.5 | Fax No. |  |
| 1.1.6 | Email |  |
| 1.2 | List of Imported components (% By value) (Attach list separately indicating Name and Part Number) |  |
| 1.3 | Method of selection (by Testing Authority or by the manufacturer / applicant) |  |
| 1.4 | Recommended duration and Schedule of Running-In by manufacturer |  |
| 1.4.1 | Engine |  |
| 1.4.2 | Transmission |  |
| 2.0 | Tractor |  |
| 2.1 | Type |  |
| 2.1.1 | Make |  |
| 2.1.2 | Model No. |  |
| 2.1.3 | Brand name, if any |  |
| 2.1.4. | Indian Trade name |  |
| 2.1.5 | Chassis Number and its place of location on the tractor |  |
| 2.1.6 | Serial No. |  |
| 2.1.7 |  |  |
| 2.1.8 | Year of Manufacture |  |
| 2.1.9 | Variant(s), if any (Variant name and variant features, also Include a model wise separate sheet for necessary details) |  |
| 2.1.10 | Maximum PTO Power, kW (Declared value) |  |
| 2.1.11 | Rated PTO Power, kW (Declared value) |  |
| 2.1.12 | CFMTTI Test Report Number |  |
| 2.1.13 | Assembly identification | Identification mark | Location |
| 2.1.13.1 | Engine identification / Sl. Number |  |  |
| 2.1.13.2 | Chassis identification / Sl. Number |  |  |

Table 17 of AIS-007 (Revision 5)

| 2.1.13.3 | Gearbox/Transmission housing identification Mark / No. |  |  |
| --- | --- | --- | --- |
| 2.1.13.4 | Hydraulic System identification Mark/No. |  |  |
| 2.1.13.5 | Other major assemblies, if any |  |  |
| 3.0 | Description of engine |  |
| 3.1 | Name and address of engine manufacturer: |  |
| 3.1.1 | Telephone Number(s) |  |
| 3.1.2 | Fax Number(s) |  |
| 3.1.3 | E-mail Address |  |
| 3.1.4 | Website |  |
| 3.1.5 | Make |  |
| 3.1.6 | Model |  |
| 3.1.6.1 | Place of embossing / punching of the engine model on the engine |  |
| 3.1.7 | Type |  |
| 3.1.8 | Serial No./ Identification Number and its place of location on engine |  |
| 3.1.9 | Year of manufacture |  |
| 3.1.10 |  |  |
| 3.1.11 | Engine speed (Manufacturer’s recommended production settings), (rpm) |  |
| 3.1.11.1 | Max speed at no load i.e. high idling speed and tolerance |  |
| 3.1.11.2 | Low idling speed and tolerance |  |
| 3.1.11.3 | Speed at maximum torque and tolerance |  |
| 3.1.12 | Rated speed, (rpm): |  |
| 3.1.12.1 | - For PTO work |  |
| 3.1.12.2 | - For drawbar work |  |
| 3.1.13 | Type of suction, [Naturally aspirated / super charged / turbo charged (Please specify)] |  |
| 3.1.14 | Working principle (Four / Two stroke) |  |
| 3.1.15 | Bore, mm |  |
| 3.1.16 | Stroke, mm |  |
| 3.1.17 | Number and layout of cylinders and firing order |  |
| 3.1.18 | Type of cylinder liners [Dry/wet, replaceable/ Non replaceable (please specify)] |  |
| 3.1.19 | Cylinder capacity, cc |  |
| 3.1.20 | Compression ratio (Specify the tolerance) |  |

Table 17 of AIS-007 (Revision 5)

| 3.1.21 | Drawing of combustion chamber and piston crown |  |
| --- | --- | --- |
| 3.1.22 | Number of valves per cylinder, ( inlet and exhaust) |  |
| 3.1.23 | Arrangement of valves |  |
| 3.1.24 | Minimum cross-sectional area of ports |  |
| 3.1.25 | Inlet, mm2 |  |
| 3.1.26 | Outlet, mm2 |  |
| 3.1.27 | Valve clearance in cold/Hot condition (mm) Inlet Valve Exhaust Valve |  |
| 3.1.28 | No. of valve springs /valve |  |
| 3.1.29 | Valve lift, (Inlet and Exhaust) |  |
| 3.1.30 | Free length of valve springs when new Inner / Outer (mm) |  |
| 3.1.31 | Compressed (assembled) length of valve springs (mm) |  |
| 3.2 | Cooling System |  |
| 3.2.1 | liquid / air cooling |  |
| 3.2.2 | Characteristics of liquid-cooling system |  |
| 3.2.3 | Nature of liquid circulating pump: Yes / No |  |
| 3.2.4 | Drive ratio |  |
| 3.2.5 | Means of Temp control : |  |
| 3.2.5.1 | - Type |  |
| 3.2.5.2 | - Location |  |
| 3.2.5.3 | - Opening temp. of thermostat valve ( °C ) |  |
| 3.2.5.4 | - Temp. of fully open thermostat valve ( °C) |  |
| 3.2.6 | Radiator : make(s) and Model / type(s) |  |
| 3.2.6.1 | - Outer dimensions (mm) |  |
| 3.2.6.2 | - Size of frontal area, (cm2) |  |
| 3.2.7 | - Recommended Pressure of cap, kPa/ (kgf/cm2) |  |
| 3.2.8 | - Name & or brand name of coolant |  |
| 3.2.9 | - Coolant water ratio (as applicable) |  |
| 3.2.10 | - Bare radiator capacity (l) |  |
| 3.2.11 | - Capacity of expansion tank (l) |  |

Table 17 of AIS-007 (Revision 5)

| 3.2.12 | - Total capacity of cooling system (l) |  |
| --- | --- | --- |
| 3.2.13 | Fan : characteristics or make(s) and type(s) |  |
| 3.2.13.1 | - Number of fan blades |  |
| 3.2.13.2 | - Outer diameter of fan, (mm) |  |
| 3.2.13.3 | - Inner diameter of cowl, (mm) |  |
| 3.2.13.4 | Fan cowl |  |
| 3.2.13.5 | Fan drive system |  |
| 3.2.14 | Coolant pump: |  |
| 3.2.14.1 | - Make and Type |  |
| 3.2.14.2 | - Type of impeller, |  |
| 3.2.14.3 | - Diameter of impeller (mm) |  |
| 3.2.14.4 | - Number of vanes |  |
| 3.2.14.5 | - Number and Type of bearings |  |
| 3.2.14.6 | - Arrangement for Lubrication |  |
| 3.2.14.7 | - Period/Frequency of lubrication |  |
| 3.2.14.8 | - Method of drive |  |
| 3.2.14.9 | - Size of drive belt and No.(s) |  |
| 3.2.15 | Characteristics of air-cooling system |  |
| 3.2.16 | Blower : characteristics or make(s) and type(s) |  |
| 3.2.17 | Drive ratio(s) |  |
| 3.2.18 | Air ducting (standard production) |  |
| 3.2.19 | Temperature regulating system : yes/no (Brief description) |  |
| 3.2.20 | Temperature permitted by the manufacturer |  |
| 3.2.21 | Liquid cooling: Reference point |  |
| 3.2.22 | Air cooling: Reference point |  |
| 3.2.23 | Max. temperature at reference point |  |
| 3.2.24 | Max. Temperature of the inlet intercooler |  |
| 3.2.25 | Max. exhaust temperature at the point in the exhaust pipe(s) adjacent in outlet flange(s) of the exhaust manifolds |  |
| 3.2.26 | Fuel temperature |  |
| 3.2.27 | Lubricant temperature |  |

Table 17 of AIS-007 (Revision 5)

| 3.3 | Supercharger : yes/no (Description of the system) |  |
| --- | --- | --- |
| 3.4 | Turbocharger/Supercharger/EGR (If fitted): |  |
| 3.4.1 | -Make |  |
| 3.4.2 | -Model |  |
| 3.4.3 | -Type |  |
| 3.4.4 | -Boost (Pressure ratio) |  |
| 3.4.5 | -Speed at rated engine speed (rpm) |  |
| 3.4.6 | -Method of lubrication |  |
| 3.4.7 | -Location |  |
| 3.5 | Pre-cleaner: |  |
| 3.5.1 | Make |  |
| 3.5.2 | Type |  |
| 3.5.3 | Location |  |
| 3.6 | Air Cleaner: |  |
| 3.6.1 | - Make |  |
| 3.6.2 | - Type |  |
| 3.6.3 | - Location |  |
| 3.6.4 | - Suction pressure at Maximum power, (kPa)/ (mm of Hg) |  |
| 3.7 | If dry type: |  |
| 3.7.1 | Air filter (Make / Type/ No.) |  |
| 3.7.2 | - Vacuum indicator and its range (mm of water/mm of Hg) |  |
| 3.7.3 | - Whether dust unloading valve has been provided |  |
| 3.7.4 | - Servicing/maintenance schedule |  |
| 3.8 | Air intake and fuel feed |  |
| 3.8.1 | Description and diagrams of inlet pipes and their accessories (dash pot, heating device, additional air intake, etc.) |  |
| 3.8.2 | Maximum permitted depression of air intake at characteristic place (Specify location of measurement) kPa (Specify the tolerance) (Specify range if applicable) |  |
| 3.9 | Fuel supply system type |  |
| 3.9.1 | Fuel tank: |  |
| 3.9.1.1 | - Make |  |
| 3.9.1.2 | - Material |  |
| 3.9.1.3 | - Capacity, ( l ) |  |

Table 17 of AIS-007 (Revision 5)

| 3.9.1.4 | - Location |  |
| --- | --- | --- |
| 3.9.1.5 | - Type of mounting |  |
| 3.9.1.6 | - Provision for draining of sediments/water |  |
| 3.9.1.7 | - Type of strainer at filling mouth |  |
| 3.9.2 | Water Separator (if provided): |  |
| 3.9.2.1 | Make |  |
| 3.9.2.2 | Type |  |
| 3.9.2.3 | Location |  |
| 3.9.3 | Primary Pump (Fuel transfer pump/ Feed pump): |  |
| 3.9.3.1 | - Make |  |
| 3.9.3.2 | - Model/Group combination No. |  |
| 3.9.3.3 | - Type |  |
| 3.9.3.4 | - Location |  |
| 3.9.3.5 | Method of drive |  |
| 3.9.3.6 | - Whether sediment bowl has been provided |  |
| 3.9.4 | Fuel Filters: |  |
| 3.9.4.1 | - Make |  |
| 3.9.4.2 | - Type |  |
| 3.9.4.3 | - Number |  |
| 3.9.4.4 | - Model / Group Combination No |  |
| 3.9.5 | Type of filter element(s): |  |
| 3.9.5.1 | - Primary |  |
| 3.9.5.2 | - Secondary |  |
| 3.9.5.3 | - Capacity of Secondary filter bowl with filter elements,( l ) |  |
| 3.9.6 | Additional filter(s), if any: |  |
| 3.9.6.1 | - Make |  |
| 3.9.6.2 | - Type |  |
| 3.10 | Injection System |  |
| 3.11 | Working principle : intake manifold/direct injection/ Injection pre-chamber / swirl chamber |  |
| 3.12 | Fuel Injection Pump |  |
| 3.12.1 | Make(s), |  |
| 3.12.2 | Type(s) |  |
| 3.12.3 | Model and Identification No. |  |
| 3.12.4 | Fuel Delivery : | mm3/stroke at a pump speed of_____ rpm |

Table 17 of AIS-007 (Revision 5)

| 3.12.5 | Injection or characteristics diagram |  |
| --- | --- | --- |
| 3.12.6 | (Specify the tolerance) |  |
| 3.12.7 | Calibration procedure: On engine / on pump bench. If boost pump is supplied, state the characteristics fuel delivery and boost pressure versus engine speed. |  |
| 3.12.8 | Injection timing |  |
| 3.12.9 | Injection advance curve |  |
| 3.12.10 | Injection advance (specify the tolerance) |  |
| 3.13 | Injectors |  |
| 3.13.1 | Make |  |
| 3.13.2 | Type |  |
| 3.13.3 | Model and Identification (Holder Number and Nozzle Number) |  |
| 3.13.4 | No. of holes in each injector |  |
| 3.13.5 | Diameter of holes (mm) |  |
| 3.13.6 | Opening pressure or characteristics diagram (specify the tolerance) |  |
| 3.13.7 | Injection Piping Length |  |
| 3.13.8 | Internal diameter of injection piping |  |
| 3.14 | Governor |  |
| 3.14.1 | Make(s) |  |
| 3.14.2 | Type(s) |  |
| 3.14.3 | Cut off point under load (rpm) |  |
| 3.14.4 | Max. speed without load |  |
| 3.14.5 | Range of Speed (rpm) |  |
| 3.14.6 | Rated speed |  |
| 3.14.7 | Idle speed |  |
| 3.15 | Cold start device |  |
| 3.15.1 | Make(s) |  |
| 3.15.2 | Type(s) |  |
| 3.15.3 | System description |  |
| 3.16 | Exhaust System |  |
| 3.16.1 | Make ,Type of silencer, Position of silencer |  |
| 3.16.2 | - Provision of spark arresting device, (Yes / No) |  |
| 3.16.3 | -Make and Type of spark arresting device, if provided |  |
| 3.16.4 | Specify the back pressure at maximum Gross power and the location of measurement (kPa) (Specify the tolerance and range) |  |

Table 17 of AIS-007 (Revision 5)

| 3.16.5 | Device for recycling crank-case gases Description and diagrams |  |
| --- | --- | --- |
| 3.17 | Lubrication system |  |
| 3.17.1 | - Type |  |
| 3.17.2 | - Minimum permissible lubricating oil pressure, kPa (kgf /cm2) |  |
| 3.18 | Lubricating pump |  |
| 3.18.1 | Make |  |
| 3.18.2 | Model |  |
| 3.18.3 | Method of drive |  |
| 3.18.4 | Type |  |
| 3.18.5 | Discharge of pump at rated (Engine/pump) rpm (l/min) |  |
| 3.18.6 | Pressure release seating Kpa (kgf/cm2) |  |
| 3.18.7 | Oil sump capacity (l) |  |
| 3.18.8 | Total Lub. Oil capacity (l) |  |
| 3.18.9 | Lub. Oil Grade |  |
| 3.18.10 | Oil changing period (hr) |  |
| 3.19 | Oil cooler (Yes / No) |  |
| 3.19.1 | make(s) and type(s) |  |
| 3.20 | Lub. oil filter (s): |  |
| 3.20.1 | - Make /model identification |  |
| 3.20.2 | - Number(s) |  |
| 3.20.3 | - Type |  |
| 3.21 | Starting System: |  |
| 3.21.1 | - Type |  |
| 3.21.2 | - Aid for cold starting |  |
| 3.21.3 | - Any other device for easy starting |  |
| 3.22 | Electrical System: |  |
| 3.22.1 | Batteries: |  |
| 3.22.1.1 | - Make |  |
| 3.22.1.2 | - Model, if any |  |
| 3.22.1.3 | - Type |  |
| 3.22.1.4 | - Capacity and rating |  |
| 3.22.1.5 | - Location |  |
| 3.22.1.6 | - Ground polarity |  |

Table 17 of AIS-007 (Revision 5)

| 3.22.2 | Self Starter: |  |
| --- | --- | --- |
| 3.22.2.1 | - Make |  |
| 3.22.2.2 | - Model |  |
| 3.22.2.3 | - Capacity & Power rating |  |
| 3.22.2.4 | - Serial Number |  |
| 3.22.3 | Generator (Alternator/Dynamo): |  |
| 3.22.3.1 | - Make |  |
| 3.22.3.2 | - Model |  |
| 3.22.3.3 | - Type |  |
| 3.22.3.4 | - Out put rating |  |
| 3.22.3.5 | - Power rating |  |
| 3.22.3.6 | - Serial Number |  |
| 3.22.4 | Details of Instruments panel: |  |
| 3.22.4.1 | Engine speed –cum-cumulative run hour meter. |  |
| 3.22.4.2 | Lubricant oil pressure gauge/ indicator lamp |  |
| 3.22.4.3 | Coolant (water) temperature gauge (with colour zones). |  |
| 3.22.4.4 | Fuel level gauge (with colour zones). |  |
| 3.22.4.5 | Main switch (key-turn type). |  |
| 3.22.4.6 | Light switch (rotary type). |  |
| 3.22.4.7 | Turn indicator light switch |  |
| 3.22.4.8 | Hazard light switch |  |
| 3.22.4.9 | Head light (long beam) indicator lamp. |  |
| 3.22.4.10 | Battery charging indicator lamp. |  |
| 3.22.4.11 | Turn indicator-cum-hazard indicator tell-tale |  |
| 3.22.4.12 | Fuel shut-off knob |  |
| 3.22.4.13 | Horn push button. |  |
| 3.22.4.14 | Specify other if any |  |
| 3.22.5 | Lighting Installation requirements |  |

Table 17 of AIS-007 (Revision 5)

| Description | Producer | Type | No. and colour | Arra-ngement | Orientation | Position in width (from outer edge), height, Length (mm) | Tell tale | Geom-etric visibility | Identi-fication Mark (if available) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| Head lamps: |
| - Main beam (optional) |  |  |  |  |  |  |  |  |  |
| - Dipped beam |  |  |  |  |  |  |  |  |  |
| Front fog lamp (optional) |  |
| Front Position lamp (Parking lamp) |  |  |  |  |  |  |  |  |  |
| Side Marker lamps (optional) |  |
| Tail lamp |  |  |  |  |  |  |  |  |  |
| Rear Position lamp (Parking lamp) |  |  |  |  |  |  |  |  |  |
| Stop lamp (Brake lights) |  |  |  |  |  |  |  |  |  |
| Registration plate lamp |  |  |  |  |  |  |  |  |  |
| Reversing lamp (Optional) |  |
| Direction indicator lamps |
| - Front |  |  |  |  |  |  |  |  |  |
| - Rear |  |  |  |  |  |  |  |  |  |
| - Side (optional) |  |
| Hazard warning signal lamps |
| - Front |  |  |  |  |  |  |  |  |  |
| - Rear |  |  |  |  |  |  |  |  |  |
| - Side (optional) |  |
| Reflectors, Non-Triangular: |
| - Front |  |  |  |  |  |  |  |  |  |
| - Rear |  |  |  |  |  |  |  |  |  |
| - Side (optional) |  |
| Additional lamps if any ( Plough lamp) |  |  |  |  |  |  |  |  |  |
| - Purpose : To illuminate implement working area |  |  |  |  |  |  |  |  |  |

Table 17 of AIS-007 (Revision 5)

| 4.0 | Transmission |  |
| --- | --- | --- |
| 4.1 | - Make |  |
| 4.2 | - Model |  |
| 4.3 | - Type |  |
| 4.4 | Transmission ratio | Please enclose line diagram of complete transmission system as Annexure-III |
| 4.5 | Arrangement of power transmission | 2WD / 4WD |
| 4.6 | Clutch |  |
| 4.6.1 | Make |  |
| 4.6.2 | Type |  |
| 4.6.2.1 | - No. of friction plate(s) |  |
| 4.6.3 | Transmission/PTO |  |
| 4.6.3.1 | - Outer diameter (mm) |  |
| 4.6.3.2 | - Inner diameter (mm) |  |
| 4.6.3.3 | - Material of lining |  |
| 4.6.4 | - Method of operation |  |
| 4.7 | Gear Box |  |
| 4.7.1 | Make |  |
| 4.7.2 | Model/identification mark |  |
| 4.7.3 | Type |  |
| 4.7.4 | Number of speeds |  |
| 4.7.5 | - Forward |  |
| 4.7.6 | - Reverse |  |
| 4.7.7 | Location of main gear shifting levers |  |
| 4.7.8 | Location of speed range selector (L/M/H) lever |  |
| 4.7.9 | - Gear shifting pattern |  |

### Nominal Speeds

| Movement | Gear | Number of Engine Revs. for one Rev. of driving wheel | Nominal speed at rated engine speed when fitted with------------ size tyres of ____ mm radius index, (kmph) |
| --- | --- | --- | --- |
|  |  | LOW | HIGH | LOW | HIGH |
| Forward | 1 |  |  |  |  |
| Forward | 2 |  |  |  |  |
| Forward | 3 |  |  |  |  |
| Forward | 4 |  |  |  |  |
| Reverse | 1 |  |  |  |  |

Table 17 of AIS-007 (Revision 5)

| 5.0 | Wheel rim |  |
| --- | --- | --- |
| 5.1 | Size |  |
| 5.2 | Front |  |
| 5.3 | Rear |  |
| 5.4 | Others |  |
| 5.5 | Name of manufacturer |  |
| 5.6 | Identification mark for front and rear rims |  |
| 5.7 | Pitch circle dia of mounting bolts mm |  |
| 5.8 | Number of mounting bolts |  |
| 5.9 | Material (Steel/ Aluminum alloy etc.) |  |
| 6.0 | Wheel nut and Wheel disc |  |
| 6.1 | Wheel Nut |  |
| 6.1.1 | Name of manufacturer |  |
| 6.1.2 | Size |  |
| 6.1.3 | No. per wheel |  |
| 6.1.4 | Tightening torques for front and rear |  |
| 6.2 | Wheel disc |  |
| 6.2.1 | Name of manufacturer |  |
| 6.2.2 | Size |  |
| 6.2.3 | Material |  |
| 6.2.4 | Method of fitment (Press/bolted/others) |  |
| 7.0 | List of tools normally provided with tractor |  |
| 8.0 | Power take-off shaft |  |
| 8.1 | Location |  |
| 8.2 | Height above Ground Level (mm) |  |
| 8.3 | No. of Splines |  |
| 8.4 | Direction of Rotation (Viewed from Driving End) |  |
| 8.5 | Size (mm) |  |
| 8.6 | Name of Standard to which it conforms |  |
| 8.7 | Rated Speed (rpm) |  |
| 8.8 | Proportional Erpm at Std. 540 PTO rpm |  |
| 8.9 | PTO Speed at Rated Engine Speed (rpm) |  |
| 8.10 | Details of Other PTO Shaft, if any |  |
| 9.0 | Belt pulley |  |

Table 17 of AIS-007 (Revision 5)

| 10.0 | Power lift |  |
| --- | --- | --- |
| 10.1 | Make |  |
| 10.2 | Type of Pump |  |
| 10.3 | Oil Capacity |  |
| 10.4 | Pump Capacity at Rated Erpm and |  |
| 10.5 | Minimum Pressure, (Ipm) |  |
| 10.6 | Rated Speed of Pump corresponding To Rated Erpm (rpm) |  |
| 10.7 | Relief Valve Opening Pressure, kPa (kgf/cm2) |  |
| 10.8 | Pressure Sustained by Open Relief Valve. |  |
| 10.9 | Hydraulic Power at 90% of Min. Relief Valve |  |
| 10.10 | Setting (Crack-Off setting), kW |  |
| 10.11 | Lifting Capacity, kN (kgf) (Max. Force exerted through full range & Corrected to those values corresponding to Hydraulic Power) |  |
| 10.12 | At Hitch Points |  |
| 10.13 | On Standard Frame |  |
| 10.14 | Means of Position and Response Control |  |
| 10.15 | Means of Draft Control |  |
| 11.0 | Drawbar (s) |  |
| 11.1 | Swinging drawbar : |  |
| 11.2 | Linkage drawbar : |  |
| 12.0 | Hitch |  |
| 12.1 | Front : |  |
| 12.2 | Type & Location |  |
| 12.3 | Height above Ground level (mm) |  |
| 12.4 | Type of adjustment |  |
| 12.5 | Width (mm) |  |
| 12.6 | Diameter of pinhole (mm) |  |
| 12.7 | Rear |  |
| 12.8 | Type |  |
| 12.9 | Location |  |
| 12.10 | Height above Ground level (mm) |  |
| 12.11 | Type of adjustment |  |
| 13.0 | Steering |  |
| 13.1 | Make |  |
| 13.2 | Type |  |

Table 17 of AIS-007 (Revision 5)

| 13.3 | Location |  |
| --- | --- | --- |
| 13.4 | Method of Operation |  |
| 13.5 | Diameter of Steering Wheel (mm) |  |
| 13.6 | Steering Housing Oil Capacity (I) |  |
| 14.0 | Brakes |  |
| 14.1 | Service Brake |  |
| 14.1.1 | Make Type |  |
| 14.1.2 | Location |  |
| 14.1.3 | Thickness of Brake Lining (mm) |  |
| 14.1.4 | Area of Liner (sq. cm) |  |
| 14.1.5 | Material of Lining (Asbestos/Non-asbestos) |  |
| 14.1.6 | Method of Operation |  |
| 14.2 | Parking brake |  |
| 14.2.1 | Make |  |
| 14.2.2 | Type |  |
| 14.2.3 | Size |  |
| 14.2.4 | Method of Operation |  |
| 15.0 | Wheel Equipment |  |
| 15.1 | Steering Wheels |  |
| 15.1.1 | Make |  |
| 15.1.2 | No., Size and Ply Rating |  |
| 15.1.3 | Arrangement |  |
| 15.1.4 | Type of Tyres |  |
| 15.1.5 | Max. Permissible Load of each Tyre (kgf) |  |
| 15.1.6 | Recommended inflation pressure, kPa (kgf/cm2) |  |
| 15.1.7 | For Field (Including Wet land) kpa(kgf/cm2) |  |
| 15.1.8 | For Road |  |
| 15.1.9 | Track Width (mm) |  |
| 15.1.10 | Method of Changing Track Width |  |
| 15.2 | Driving Wheels |  |
| 15.2.1 | Make |  |
| 15.2.2 | No., Size and Ply Rating |  |
| 15.2.3 | Type of Tyres |  |
| 15.2.4 | Max. Permissible Load of each tyre, kg |  |
| 15.2.5 | Pressure |  |
| 15.2.6 | Recommended inflation pressure, kPa (kgf/cm2) |  |

Table 17 of AIS-007 (Revision 5)

| 15.2.7 | different conditions |  |
| --- | --- | --- |
| 15.2.8 | For Field |  |
| 15.2.9 | Track Widths (mm) |  |
| 15.2.10 | Method of changing Track Width |  |
| 16.0 | Wheel base (mm) |  |
| 16.1 | Method of changing Wheelbase, if any Range of adjustment (mm) |  |
| 17.0 | Minimum ground clearance (mm) |  |
| 17.1 | Method of changing Ground Clearance, if any |  |
| 17.2 | Clearance Limiting part |  |
| 18.0 | Seat |  |
| 18.1 | Make |  |
| 18.2 | Type |  |
| 18.3 | Type of Suspension /Type of Damping |  |
| 18.4 | Range of Adjustment |  |
| 19.0 | Lubricants/Coolant Capacity, liters |  |
| 19.1 | Lubricants: |
| S. No. | Particulars | Recommended grade | Capacity (l) | Change period (h) | Filter change period (h) |
| 19.1.1 | Air cleaner oil |  |  |  |  |
| 19.1.2 | Bare engine sump |  |  |  |  |
| 19.1.3 | Total lub. oil of engine |  |  |  |  |
| 19.1.4 | Steering housing |  |  |  |  |
| 19.1.5 | Gearbox housing oil |  |  |  |  |
| 19.1.6 | Differential housing oil |  |  |  |  |
| 19.1.7 | Front axle |  |  |  |  |
| 19.1.8 | Rear axle |  |  |  |  |
| 19.1.9 | Final drive (front) |  |  |  |  |
| 19.1.10 | Final drive (rear) |  |  |  |  |
| 19.1.11 | Hydraulic system (*) |  |  |  |  |
| 19.1.12 | Other (Brake etc ) |  |  |  |  |
| 19.1.13 | Grease |  |  |  |  |
| 19.2 | Number of lubricating points: |  |
| 19.2.1 | Oiling |  |
| 19.2.2 | Grease nipples |  |
| 19.2.3 | Grease cups |  |

Table 17 of AIS-007 (Revision 5)

| 20.0 | Tightening torque (kgm / Nm): |  |
| --- | --- | --- |
| 20.1 | Cylinder head nut & bolts |  |
| 20.2 | Main bearings nut & bolts |  |
| 20.3 | Big end bearings nut & bolts |  |
| 20.4 | Flywheel bolts |  |
| 21.0 | Mass and Ballast: | Front | Rear | Total |
| 21.1 | Unballasted Tractor: Mass of the tractor in working order with full tanks & radiators. [Optional front & rear weights (ballast), tyre ballast, the tractor operator, mounted implements, mounted equipments or any specialized components are not included]. |  |  |  |
| 21.2 | Tractor with standard ballast: Mass of the tractor in working order with standard ballast of -------- kgf at front and ------- kgf at rear, full tanks & radiators. [Tyre ballast, the tractor operator, mounted implements, mounted equipments or any specialized components are not included]. |  |  |  |
| 22.0 | Recommended ballast for different test: |
| 22.1 | Ballast mass | For drawbar test | For field test | For road test |
| 22.1.1 22.1.2 22.1.3 22.1.4 22.1.5 22.1.6 | Front - C.I. Ballast (kg) |  |  |  |
|  | - Water ballast (kg ) |  |  |  |
|  | Rear - C.I. Ballast (kg) |  |  |  |
|  | - Water ballast (kg) |  |  |  |
|  | Front - Location of C.I. ballast weights |  |  |  |
|  | Rear - Location of C.I. ballast weights |  |  |  |
| 23.0 | Mass of tractor in Ballasted condition (kg): |
| S. No | Test | Front | Rear | Total |
| 23.1 | For drawbar |  |  |  |
| 23.2 | For Field tests |  |  |  |
| 23.3 | For Puddling |  |  |  |
| 23.4 | For Haulage |  |  |  |

Table 17 of AIS-007 (Revision 5)

| 24.0 | Overall Dimension of Tractor (mm): |
| --- | --- |
| 24.1 | - Length |  |
| 24.2 | - Width |  |
| 24.3 | - Height |  |
| 24.4 | - Ground clearance(mm) | ------- (Specify the limiting part) |
| 25.0 | Colour of tractor: |  |
| 25.1 25.2 25.3 25.4 25.5 | - Chassis & Engine |  |
|  | - Sheet metal |  |
|  | - Bonnet |  |
|  | - Mudguards |  |
|  | - Wheel rims |  |
| 26.0 | Performance Characteristics: (Please refer IS 12207:2008 for the declarations and tolerances) |
|  | Characteristics | Requirements or Tolerance as per IS 12207:2008 | Values declared by the applicant |
|  | 2 | 3 | 4 |
| 26.1 | PTO Performance : |
| 26.1.1 | - Max. power under 2 h test, (kW) (Natural ambient condition) | Declared value to be achieved with a tolerance of: -5 / +10% for PTO power >35hp. –7.5/+10% for PTO power ( 35 hp |  |
| 26.1.2 | Power at rated engine speed, (kW) | --do-- |  |
| 26.1.3 | Specific fuel consumption corresponding to maximum power, (g/kWh) | ( 5% |  |
| 26.1.4 | Maximum equivalent crankshaft torque, (Nm) | ( 8% |  |
| 26.1.5 | Equivalent crankshaft torque at maximum power, Nm (kgf-m) | -- |  |
| 26.1.6 | Back-up torque, percent | 7 percent, min. |  |
| 26.1.7 | Maximum operating temperature ( °C) |
| 26.1.7.1 26.1.7.2 | - Engine oil | To be declared by the manufacturer under high ambient conditions. |  |
|  | - Coolant (water) | -- do-- |  |
| 26.1.8 | Engine oil consumption, (g/kWh) | Not exceeding 1% of SFC at max. power under High ambient conditions |  |

Table 17 of AIS-007 (Revision 5)

| 26.1.9 | Smoke level | Maximum light absorption coefficient of 3.25 / m or equivalent BOSCH No. 5.2 or 75 Hatridge value (As per CMVR) |  |
| --- | --- | --- | --- |
| 26.2 | Belt pulley performance (if desired by the manufacturer) |
| 26.2.1 | Power at rated engine speed | Declared value to be achieved with a tolerance of: -5 / +10% for PTO power >35hp. –7.5/+10% for PTO power ( 35 hp |  |
| 26.2.2 | Power at standard linear belt speed [(15.75±0.25) m/s] | --do-- |  |
| 26.2.3 | Maximum operating temperature of oil in the belt pulley, °C | Nil |  |
| 26.3 | Drawbar Performance : |
| 26.3.1 | Max. drawbar pull with ballast corresponding to 15 percent wheel slip or 7 percent track slip, (kN) | Minimum 65% of static mass with ballast |  |
| 26.3.2 | Max. drawbar pull without ballast or with standard ballast corresponding to 15 percent wheel slip or 7 percent track slip, (kN) | Minimum 65% of static mass of tractor without ballast or with standard ballast |  |
| 26.3.3 | Maximum drawbar power without ballast or with standard ballast, (kW). | Minimum 80% of PTO power as referred in 13.1(a) above of PTO performance |  |
| 26.3.4 | Max. transmission oil temperature ( °C) | To be declared by the manufacturer |  |
| 26.4 | Power lift and hydraulic pump performance: |
| 26.4.1 | Maximum lifting capacity throughout the range of lift, (kN): |  |
| 26.4.1.1 26.4.1.2 | - At hitch points | To be declared by the manufacturer |  |
|  | - With the standard frame | The lift capacity should at least be 18 kg/PTO hp and it should be 16 kg/engine hp where the tractor is not provided with a PTO shaft. |  |
| 26.4.2 | Maximum drop in the height of the point of application of the force after each 5 minutes interval for a total duration of 30 minute, (mm) | To be declared by the manufacturer |  |

Table 17 of AIS-007 (Revision 5)

| 26.5 | Brake performance at 25 kmph: |
| --- | --- |
| 26.5.1 | Maximum stopping distance at a force equal to or less than 600 N on brake pedal with ballast, (m): |  |
| 26.5.1.1 26.5.1.2 | -Cold brake | 10 m |  |
|  | -Hot brake | 10 m |  |
| 26.5.2 | Maximum force exerted on the brake pedal to achieve a deceleration of 2.5 m/s2 | 600 N |  |
| 26.5.3 | Whether parking brake is effective at a force of 600 N at foot pedal(s) or 400 N at hand lever | Yes / No |  |
| 26.6 | Noise measurement : |  |  |
| 26.6.1 | Maximum ambient noise emitted by the tractor dB(A) | As per CMVR |  |
| 26.6.2 | Maximum noise at operator’s ear level dB(A) | As per CMVR |  |
| 26.7 | Amplitude of mechanical vibrations at: |  |  |
| 26.7.1 26.7.2 26.7.3 | -Foot rest (left / right) | 100 microns, max |  |
|  | -Seat (with driver seated) | 100 microns, max |  |
|  | -Steering wheel | 100 microns, max |  |
| 26.8 | Air Cleaner Oil Pull Over: |  |  |
|  | Max. percentage of oil pull over | 0.25 % Maximum |  |
| 26.9 | Haulage requirements : |  |  |
| 26.9.1 26.9.2 26.9.3 26.9.3.1 26.9.4 26.9.5 26.9.5.1 | - Gross mass of the trailers, (tones): |  |  |
|  | (1) Two wheel | To be specified by the manufacturer |  |
|  | (2) Four wheel | --do-- |  |
|  | - Distance travelled / litre of fuel consumption, (km/l) |  |  |
|  | (1) Two wheel | To be specified by the manufacturer |  |
|  | (2) Four wheel | --do-- |  |
|  | - Fuel consumption (ml/km/gross mass tonne) |  |  |
| 26.9.6 | (1) Two wheel | To be specified by the manufacturer |  |
| 26.9.7 | (2) Four wheel | --do-- |  |

Table 17 of AIS-007 (Revision 5)

| 26.10 | Wetland cultivation : |  |  |
| --- | --- | --- | --- |
| 26.10.1 26.10.2 26.10.3 | Sealing for the following assemblies: Clutch assembly Brake assembly Front axle hubs | The identified assemblies should essentially meet the requirement of IS 11082. No water ingress in the identified assemblies given in column 2. Note – Water droplets due to condensation not to be considered as water ingress. |  |
| 26.11 | Safety features: |  |  |
| 26.11.1 | Guards against moving and hot parts | As per CMVR |  |
| 26.11.2 | Lighting arrangement | As per CMVR |  |
| 26.12 | Labelling of Tractors: |  |  |
| 26.12.1 | Provision of labelling plate | Should conform to the requirements of CMVR along with declared value of PTO HP |  |
| 26.13 | Discard limits for: |
| 26.13.1 | Cylinder bore diameter, (mm) |  |  |
| 26.13.2 | Cylinder ovality and taperness, (mm) |  |  |
| 26.13.3 | Piston diameter, (mm) |  |  |
| 26.13.4 | Clearance between piston and cylinder liner at the skirt, (mm) |  |  |
| 26.14 26.14.1 26.14.2 | Piston ring end gap (mm): |  |  |
|  | - Compression rings |  |  |
|  | - Oil rings |  |  |
| 26.15 26.15.1 26.15.2 | Piston ring groove clearance (mm): |  |  |
|  | - Compression rings |  |  |
|  | - Oil rings |  |  |
| 26.16 26.16.1 26.16.2 | Clearance of main bearings (mm): |  |  |
|  | Diametrical clearance |  |  |
|  | Crankshaft end float |  |  |
| 26.17 26.17.1 26.17.2 | Clearance of big or small end bearings, (mm): |  |  |
|  | Diametrical |  |  |
|  | Axial |  |  |
| 26.18 | Clearance between king pin and bush, (mm) |  |  |
| 26.19 | Clearance between center pin and bush, (mm) |  |  |

Table 17 of AIS-007 (Revision 5)

| 26.20 | Clearance between valve guide and stem (mm) |  |  |
| --- | --- | --- | --- |
| 26.21 26.21.1 26.21.2 | Spring index of valve springs N/mm/(kgf/mm) |  |  |
|  | Inner spring |  |  |
|  | Outer spring |  |  |
| 26.22 | Backlash of timing gears (mm) |  |  |
| 26.22.1 26.22.1.1 26.22.1.2 | Overall thickness of clutch plate (mm) |  |  |
|  | - Transmission clutch |  |  |
|  | - PTO shaft |  |  |
| 26.23 26.23.1 26.23.2 | Height of lining over rivet head of clutch lining (mm) |  |  |
|  | - Transmission clutch |  |  |
|  | - PTO shaft |  |  |
| 26.24 26.24.1 26.24.2 | -Thickness of brake lining (mm) |  |  |
|  | Height of lining over rivet head of brake lining (mm) |  |  |
|  | Depth of oil groove of brake disc in case of oil immerse brake |  |  |
| 26.25 | Backlash of transmission gears (mm): |  |  |
| 26.25.1 | - Transmission gears |  |  |
| 26.25.2 | - Crown wheel and pinion |  |  |
| 26.25.3 | - Final drive gear |  |  |
| 26.25.4 | - Safety features, if any |  |  |
| 26.26 | Optional requirements : | Requirements | Declaration |
| 26.26.1 | Seating requirements | Should meet the requirements of IS 12343:1998 |  |
| 26.26.2 | Fitment of ROPS | With a provision for fitment of ROPS. If ROPS fitted it should meet the requirement of IS 11821:1992 |  |
| 26.26.3 | Technical requirements for PTO shaft | Should meet the requirements of IS 4931:1995 |  |
| 26.26.4 | Dimensions of three point linkage | Should meet the requirements of IS 4468 (Part-I):1997 |  |

Table 17 of AIS-007 (Revision 5)

| 26.26.5 | Specifications of linkage and swinging drawbars | Should meet the requirements of IS 12953:1990 and IS 12362 Part 3:1994. |  |
| --- | --- | --- | --- |
| 26.26.6 | Accessories | Trailer hitch, front tow hook, linkage drawbar may be provided. |  |

I,…………………………………………………….of M/s ……………………………………………… hereby declare that information given above in page no. 1 to 21 is as per design / drawings of the prototype/commercial model of tractor submitted for Confidential/Commercial test and is correct to the best of my knowledge and belief.

Applicant / Manufacturer	                   :

Signature of Authorised Signatory            :

Name	                                                       :

Designation	                                           :

Place:

Date:

PRE-TEST CONDITION CERTIFICATE

FOR COMMERCIAL TEST (I.C.T./VARIANT/SUPPLIMENTARY)

| Make of tractor | : |  |
| --- | --- | --- |
| Model of tractor | : |  |
| Nature of test | : |  |
| (a) | The selection procedure followed for submitting the tractor meets the requirement of clause 4.3 of Indian Standard 5994-1998. |
| (b) | It is certify that the specification of machine submitted for test conforms to the production model, which we propose to introduce. |
| (c) | It is also understood that the test will be carried out on the machine as it stands together with accessories and attachments essential to the satisfactory performance of the machine. We will not be allowed to introduce alternations or modifications on the machine which should affect its normal performance during the progress of tests. If any major modifications or alterations are considered necessary, we shall withdraw the machine from tests and submit another machine of same make and model with fresh application for testing. |
| I / We do hereby abide by the above preconditions referred to at (a), (b) & (c) above in respect of the test sample submitted for confidential / commercial Test at this Institute and in case of any violation we shall withdraw the tractor from test. |
| Signature of Applicant/Authorized signatory | : |  |
| Name & Designation | : |  |
| Address: | : |  |
| Telephone No. |  |  |
| Fax No. | : |  |
| Date | : |  |

Table 18 of AIS-007 (Revision 5)

LIST OF COMPONENT TEST REPORTS / CERTIFICATES FOR

AGRICULTURAL TRACTORS / CONSTRUCTION EQUIPMENT VEHICLES

| Rule No. | Subject | Test Report Nos. | If certificate is not available likely date of submission of test report |
| --- | --- | --- | --- |
| 100 | Safety Glass Windscreen Side Rear (For Construction Equipment Vehicles) |  |  |
| 104 A | Reflex Reflector White, Front Amber, side Red, Rear Retro Reflective Tape or Paint |  |  |
| 104B(2) | Reflex Reflector Rear, Red |  |  |
| 119 | Horns Horn Installation |  |  |
| 124(A)1 | Automotive Lamps Bulbs used for: Head light main & dip. Parking light Direction indicator lamp Tail lamp Reversing lamp Stop lamp Rear registration mark indicating lamp Top light |  |  |
| 124A(2) | Lighting Signalling & Indicating Systems: Head Light: Fog Light: Rear Licence Plate Light: Rear Position Light: Tail Light: Stop Light: Directional Indicator Light: Front : Rear : Side : |  |  |

Table 18 of AIS-007 (Revision 5)

| Rule No. | Subject | Test Report Nos. | If certificate is not available likely date of submission of test report |
| --- | --- | --- | --- |
|  | Parking Light: Reversing Light: High Mounted Stop Light: Rear Warning Triangle ( Slow moving emblem) |  |  |
| 124A(3) | Hydraulic Brake Hose |  |  |
| 124A(4) | Hydraulic Brake Fluid |  |  |
| 124A(5) | Tow Hook |  |  |
| 124A(6) | Fuel Tank |  |  |
| 124A(7) | Wheel Nuts & Hub Caps |  |  |
| Note : Please enclose test report copies wherever required. In case samples are submitted to the testing agency for testing, please provide reference docket no. |

Table 19 of AIS-007 (Revision 5)

List of Test Report / Certificates of other models

for Agricultural Tractors / Construction Equipment Vehicles

|  | Rule No. | Subject | Model | No. of test report/ certificate * | Issued by | Justification for applicability for the model under consideration |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

* Xerox copies of the certificates to be submitted in case if it is from another testing agency or whenever necessary.

Table 20 of AIS-007 (Revision 5)

## TECHNICAL SPECIFICATION OF CNG RELATED PARTS

## TO BE SUBMITTED BY VEHICLE MANUFACTURER

(To be used for approval of OE CNG vehicles in lieu of Annex I of AIS-024)

| 1.0 | Name of Vehicle Manufacturer |  |
| --- | --- | --- |
| 2.0 | CNG Cylinder (DOE approved/endorsed) |  |
| 2.1 | Name of manufacturer |  |
| 2.2 | Identification No. |  |
| 2.3 | Working pressure (kg/cm2 ) |  |
| 2.4 | Max. test pressure (kg/cm2 ) |  |
| 2.5 | Cylinder capacity (water equivalent) |  |
| 2.6 | Approval reference from DOE |  |
| 3.0 | Cylinder Valve(s) (DOE approved/endorsed) |  |
| 3.1 | Name of manufacturer |  |
| 3.2 | Model name/Identification No. |  |
| 3.3 | Type |  |
| 3.4 | Working pressure (kg/cm2 ) |  |
| 3.5 | Max. test pressure (kg/cm2 ) |  |
| 3.6 | Approval reference from DOE |  |
| 4.0 | CNG Solenoid Valve |  |
| 4.1 | Name of manufacturer |  |
| 4.2 | Model Name/Identification No |  |
| 4.3 | Type |  |
| 4.4 | Working pressure (kg/cm2 ) |  |
| 4.5 | Max test pressure (kg/cm2 ) |  |
| 5.0 | Petrol Solenoid Valve |  |
| 5.1 | Name of manufacturer |  |
| 5.2 | Model Name/Identification No. |  |
| 5.3 | Type |  |
| 5.4 | Working pressure (kg/cm2 ) |  |
| 5.5 | Max test pressure (kg/cm2 ) |  |
| 6.0 | Refilling valve |  |
| 6.1 | Name of manufacturer |  |
| 6.2 | Model Name/Identification No. |  |
| 6.3 | Type |  |

Table 20 of AIS-007 (Revision 5)

| 6.4 | Working pressure (kg/cm2 ) |  |
| --- | --- | --- |
| 6.5 | Max test pressure (kg/cm2 ) |  |
| 7.0 | Pressure Regulator |  |
| 7.1 | Name of manufacturer |  |
| 7.2 | Model name/Identification No. |  |
| 7.3 | Type |  |
| 7.4 | Inlet pressure (kg/cm2 ) |  |
| 7.5 | Outlet pressure (kg/cm2 ) |  |
| 7.6 | No. of stages |  |
| 8.0 | CNG Filter |  |
| 8.1 | Name of manufacturer |  |
| 8.2 | Model name/Identification No. |  |
| 8.3 | Type |  |
| 8.4 | Inlet pressure (kg/cm2 ) |  |
| 8.5 | Outlet pressure (kg/cm2 ) |  |
| 9.0 | High Pressure Tubing |  |
| 9.1 | Name of manufacturer |  |
| 9.2 | Model name/Identification No. |  |
| 9.3 | Type |  |
| 9.4 | Working pressure (kg/cm2 ) |  |
| 9.5 | Max. test pressure (kg/cm2 ) |  |
| 9.6 | Outer diameter/Inner Diameter |  |
| 9.7 | Protection quality (material used) |  |
| 10.0 | Low Pressure Tubing |  |
| 10.1 | Name of manufacturer |  |
| 10.2 | Model name/Identification No. |  |
| 10.3 | Type |  |
| 10.4 | Working pressure (kg/cm2 ) |  |
| 10.5 | Max test pressure (kg/cm2 ) |  |
| 10.6 | Outer diameter/Inner Diameter |  |
| 10.7 | Protection quality (material used) |  |
| 11.0 | Gas-Air Mixer |  |
| 11.1 | Name of manufacturer |  |
| 11.2 | Model name/Identification No |  |
| 11.3 | Type & drawing |  |
| 11.4 | Venturi Size |  |
| 12.0 | Selector Switch |  |
| 12.1 | Name of manufacturer |  |
| 12.2 | Model name/Identification No |  |
| 12.3 | Type |  |

Table 20 of AIS-007 (Revision 5)

| 13.0 | Wiring Harness (for CNG system) (Ref. Clause A11 of Table 2 of AIS-007) |  |
| --- | --- | --- |
| 13.1 | Name of manufacturer |  |
| 14.0 | Interfacing Unit (for closed loop engines) |  |
| 14.1 | Name of manufacturer |  |
| 14.2 | Model name/Identification No. |  |
| 14.3 | Type |  |
| 15.0 | Ignition Timing Advancer |  |
| 15.1 | Name of manufacturer |  |
| 15.2 | Type |  |
| 15.3 | Timing on CNG mode |  |
| 15.4 | Timing on baseline fuel. |  |
| 16.0 | Brief Description of System Including Dimensional Layout for Cylinder and other CNG components installation, ventilation details etc. |  |
| 17.0 | Refilling valve interlocking switch |  |
| 17.1 | Name of manufacturer |  |
| 17.2 | Identification No. |  |
| 17.3 | Type |  |
| 18.0 | Current limiting Device (Fuse) |  |
| 18.1 | Name of manufacturer |  |
| 18.2 | Identification No. |  |
| 18.3 | Voltage/current rating |  |
| 18.4 | Type |  |
| 19.0 | Pressure Indicator |  |
| 19.1 | Name of manufacturer |  |
| 19.2 | Identification No. |  |
| 19.3 | Type |  |
| 20.0 | Service shut off valve |  |
| 20.1 | Name of manufacturer |  |
| 20.2 | Identification No. |  |
| 20.3 | Type |  |
| 21.0 | Compartment/Sub-compartment/Gas tight housing |  |
| 21.1 | Name of manufacturer |  |
| 21.2 | Identification No. |  |
| 21.3 | Type |  |
| 22.0 | Conduit |  |
| 22.1 | Name of manufacturer |  |
| 22.2 | Identification No. |  |
| 22.3 | Inner & outer diameter |  |
| 22.4 | Type |  |

Table 20 of AIS-007 (Revision 5)

| 23.0 | Details of Seat/Upholstery/roof and side lining |  |
| --- | --- | --- |
| 23.1 | Name of manufacturer |  |
| 23.2 | Model name/Identification No. |  |
| 23.3 | Type |  |
| 24.0 | Details of non-moisture retaining hard rubber/equivalent material padding/lining provided for inner side of the cylinder mounting band(s) |  |
| 24.1 | Name of manufacturer |  |
| 24.2 | Identification No. |  |
| 24.3 | Type |  |
| 25.0 | Any other information |  |

Table 21 of AIS-007 (Revision 5)

## TECHNICAL SPECIFICATION OF LPG RELATED PARTS

## TO BE SUBMITTED BY VEHICLE MANUFACTURERS

(To be used for approval of LPG OE vehicles in lieu of Annex I of AIS-025)

| 1.0 | Name of Vehicle Manufacturer |  |
| --- | --- | --- |
| 2.0 | LPG Cylinder (DOE approved/endorsed) |  |
| 2.1 | Name of manufacturer |  |
| 2.2 | Identification No. |  |
| 2.3 | Type |  |
| 2.4 | Max. test pressure (kg/cm2 ) |  |
| 2.5 | Working pressure (kg/cm2 ) |  |
| 2.6 | Cylinder capacity (water equivalent) |  |
| 2.7 | Approval reference from DOE |  |
| 3.0 | Cylinder Valve/Multi-Function Valve assembly (DOE approved/endorsed) |  |
| 3.1 | Multi-Function Valve shall have following |  |
|  | Automatic fill limiter |  |
|  | Service valve |  |
|  | Excess flow check valve |  |
|  | Pressure relief device |  |
|  | Fusible plug |  |
|  | Content gauge |  |
|  | Inlet connected to the fill connector having non-return valve |  |
| 3.2 | Name of manufacturer |  |
| 3.3 | Model name/Identification No. |  |
| 3.4 | Vapor/Liquid withdrawal |  |
| 3.4.1 | Type |  |
| 3.4.2 | Max. test pressure (kg/cm2 ) |  |
| 3.4.3 | Working pressure (kg/cm2 ) |  |
| 3.4.4 | Approval reference from DOE |  |
| 4.0 | LPG Solenoid Valve |  |
| 4.1 | Name of manufacturer |  |
| 4.2 | Model Name/Identification No. |  |
| 4.3 | Type |  |
| 4.4 | Working pressure (kg/cm2 ) |  |
| 4.5 | Max test pressure (kg/cm2 ) |  |

Table 21 of AIS-007 (Revision 5)

| 5.0 | Petrol Solenoid Valve (if fitted) |  |
| --- | --- | --- |
| 5.1 | Name of manufacturer |  |
| 5.2 | Model Name/Identification No. |  |
| 5.3 | Type |  |
| 5.4 | Working pressure (kg/cm2 ) |  |
| 5.5 | Max test pressure (kg/cm2 ) |  |
| 6.0 | Refilling valve |  |
| 6.1 | Name of the manufacturer |  |
| 6.2 | Model name/Identification No. |  |
| 6.3 | Type |  |
| 6.4 | Working pressure (kg/cm2 ) |  |
| 6.5 | Max test pressure (kg/cm2 ) |  |
| 7.0 | Pressure Regulator/Vaporizer |  |
| 7.1 | Name of manufacturer |  |
| 7.2 | Model name/Identification No. |  |
| 7.3 | Type |  |
| 7.4 | Inlet pressure (kg/cm2 ) |  |
| 7.5 | Outlet pressure (kg/cm2 ) |  |
| 7.6 | No. of stages |  |
| 8.0 | LPG Filter |  |
| 8.1 | Name of manufacturer |  |
| 8.2 | Model name/Identification |  |
| 8.3 | Type |  |
| 8.4 | Inlet pressure (kg/cm2 ) |  |
| 8.5 | Outlet pressure (kg/cm2 ) |  |
| 9.0 | High Pressure Tubing |  |
| 9.1 | Name of manufacturer |  |
| 9.2 | Model name/Identification No. |  |
| 9.3 | Type |  |
| 9.4 | Working pressure (kg/cm2 ) |  |
| 9.5 | Max. test pressure (kg/cm2 ) |  |
| 9.6 | Outer diameter/Inner Diameter |  |
| 9.7 | Protection quality (material used) |  |
| 10.0 | Low Pressure Tubing |  |
| 10.1 | Name of manufacturer |  |
| 10.2 | Model name/Identification No. |  |
| 10.3 | Type |  |
| 10.4 | Working pressure (kg/cm2 ) |  |
| 10.5 | Max test pressure (kg/cm2 ) |  |
| 10.6 | Outer diameter/Inner Diameter |  |
| 10.7 | Protection diameter |  |

Table 21 of AIS-007 (Revision 5)

| 11.0 | Gas-Air Mixer |  |
| --- | --- | --- |
| 11.1 | Name of manufacturer |  |
| 11.2 | Type and Drawing |  |
| 11.3 | Venturi Size |  |
| 12.0 | Selector Switch |  |
| 12.1 | Name of manufacturer |  |
| 12.2 | Model name/Identification No. |  |
| 12.3 | Type |  |
| 13.0 | Wiring Harness (for LPG System) |  |
| 13.1 | Name of manufacturer |  |
| 14.0 | Interfacing Unit (for closed loop engines) |  |
| 14.1 | Name of manufacturer |  |
| 14.2 | Model name/Identification No. |  |
| 14.3 | Type |  |
| 15.0 | Timing advancer |  |
| 15.1 | Name of manufacturer |  |
| 15.2 | Model name / Identification No. |  |
| 15.3 | Type |  |
| 16.0 | Brief Description of System Including Dimensional Layout for Cylinder and other kit component installations, ventilation details etc. |  |
| 17.0 | Current limiting Device (Fuse) |  |
| 17.1 | Name of manufacturer |  |
| 17.2 | Identification No. |  |
| 17.3 | Voltage/current rating |  |
| 17.4 | Type |  |
| 18.0 | Compartment/Sub-compartment/Gas tight housing |  |
| 18.1 | Name of manufacturer |  |
| 18.2 | Identification No. |  |
| 18.3 | Type |  |
| 19.0 | Conduit |  |
| 19.1 | Name of manufacturer |  |
| 19.2 | Identification No. |  |
| 19.3 | Inner & outer diameter |  |
| 19.4 | Type |  |
| 20.0 | Details of Seat/Upholstery/roof and side lining |  |
| 20.1 | Name of manufacturer |  |
| 20.2 | Identification No. |  |
| 20.3 | Type |  |

Table 21 of AIS-007 (Revision 5)

| 21.0 | Details of non-moisture retaining hard rubber/equivalent material padding/ lining provided for inner side of the cylinder mounting band(s) |  |
| --- | --- | --- |
| 21.1 | Name of manufacturer |  |
| 21.2 | Identification No. |  |
| 21.3 | Type |  |
| 22.0 | Battery cut off switch (if applicable) Provided Y/N |  |
| 22.1 | Name of the manufacturer |  |
| 22.2 | Identification No. |  |
| 22.3 | Type |  |
| 23.0 | Any other information (not covered) |  |

Table 22 of AIS-007 (Revision 5)

TECHNICAL SPECIFICATION OF BUS CODE RELATED PARAMETERS 
TO BE SUBMITTED BY BUS MANUFACTURER OR BUS BODY BUILDER 
(To be used for approval of BUS BODY in lieu of Annex I of AIS-052 (Rev. 1))

| 1.0 | Details of Bus manufacturer / Bus Body Builder |  |
| --- | --- | --- |
| 1.1 | Name & Address : |  |
| 1.2 | Telephone No : |  |
| 1.3 | Fax. No. : |  |
| 1.4 | E mail address : |  |
| 1.5 | Contact person : |  |
| 1.6 | Name of model : |  |
| 1.7 | Name of variants, if any: |  |
| 1.8 | Type and General commercial description (s) : |  |
| 1.9 | Plant/(s)of manufacture : |  |
| 1.10 | Details of Bus Manufacturing facility Accreditation |  |
| 1.10.1 | Category of Bus Body Builder |  |
| 1.10.2 | Details of provisional certificate issued by the Zonal Accreditation Board(ZAB), ( Certificate Number and date ) |  |
| 1.10.3 | Details of final certificate issued by the National Accreditation Board (ZAB), ( Certificate Number and date ) |  |
| 1.11 | Details of the base CMVR Compliance Certificate issued to the Chassis ( Certificate Number and date ) |  |
| 2 .0 | Vehicle Chassis Characteristics |  |
| 2.1 | Chassis types approved for Body installation : |  |
| 2.2 | Type of Control (normal control/Full forward control etc.) : |  |
| 2.3 | Number of Axles and wheels : |  |
| 2.4 | Chassis (overall drawing) : |  |
| 2.5 | Frame Type : |  |
| 2.6 | Cross sectional view : |  |
| 2.7 | Position and arrangement of engine: |  |
| 2.8 | Dimension (in mm) (Specify drawing reference) : |  |
| 2.8.1 | Length mm : |  |
| 2.8.2 | Width mm : |  |
| 2.8.3 | Height (Unladen) mm : |  |
| 2.8.4 | Wheel base mm : |  |

Table 22 of AIS-007 (Revision 5)

| 2.8.5 | Wheel track mm : Front : Rear : |  |
| --- | --- | --- |
| 2.8.6 | Body overhang mm : Front end : Rear end : |  |
| 2.9 | Category of vehicle : |  |
| 2.9.1 | As per IS 14272 Part 1 : |  |
| 2.9.2 | As per IS 11852 Part 2 : |  |
| 3.0 | Body : |  |
| 3.1 | Type of Body : (Type I, Type II, Type III & Type IV) |  |
| 3.2 | Comfort Category : (NDX, SDX, DLX & ACX) |  |
| 3.3 | Dimension drawing and photograph of the vehicle with representative body : |  |
| 3.4 | Range of vehicle dimension (overall) : |  |
| 3.5 | Dimension drawing of the body depicting chassis connecting members : |  |
| 3.6 | Material used for construction : |  |
| 3.6.1 | Structural Material : |  |
| 3.6.2 | Size of sections : |  |
| 3.7 | Method of construction : (Brief construction method) |  |
| 3.8 | Area for Passenger (m2) : For seated passengers: For standing passengers: |  |
| 3.9 | Number of passengers : Seated : Standing : |  |
| 3.10 | Number of Passenger seats : (As per Seat Layout) |  |
| 3.11 | Passenger capacity : Maximum (Including driver) : Crew (Including driver) : |  |
| 3.12 | Number of Service doors : |  |

Table 22 of AIS-007 (Revision 5)

| 3.13 | Number of emergency exits : |  |
| --- | --- | --- |
| 3.14 | Number of escape hatches : |  |
| 3.15 | Volume of luggage compartments (m3): |  |
| 3.16 | Area of luggage Transportation on roof (m2) : |  |
| 4.0 | Clearance |  |
| 4.1 | Minimum road clearance : |  |
| 4.2 | Road clearance from floor (for buses) : |  |
| 4.3 | Approach angle : |  |
| 4.4 | Departure Angle : |  |
| 4.5 | Ramp-over Angle : |  |
| 5.0 | Weights |  |
| 5.1 | Vehicle kerb weight kg : Front axle : Rear axle : Total : |  |
| 5.2 | Gross vehicle weight kg : |  |
| 5.3 | Maximum permissible axle weights kg Front axle: Rear axle: |  |
| 5.4 | Reference mass kg : |  |
| 6.0 | Vehicle Stability & Roll Over |  |
| 6.1 | Max. stable inclination ( Laden Condition ) Left ( deg : Right ( deg : |  |

| 6.2 | Superstructure Strength / Roll Over Strength compliance established (Yes / No ) |  |
| --- | --- | --- |
| 6.2.1 | Center of Gravity of the bus in vehicle unladen condition (X-Y-Z, mm) |  |
| 6.2.2 | Drawings of superstructure ( LH, RH, Front, Rear, Roof ) |  |
| 6.2.3 | Drawing indicating details of residual space |  |
| 7.0 | Tyres |  |
|  | No. and arrangement of wheels : Front : Rear : Other : |  |

Table 22 of AIS-007 (Revision 5)

|  | Inflation pressure – Unladen : Front : Rear : Other |  |
| --- | --- | --- |
|  | Inflation pressure – Laden : Front : Rear : Other : |  |
| 8.0 | Body Panels |  |
| 8.1 | Outer Panels : |  |
| 8.1.1 | Material : |  |
| 8.1.2 | Thickness : |  |
| 8.2 | Inner Panels : |  |
| 8.2.1 | Material : |  |
| 8.2.2 | Thickness : |  |
| 8.3 | Roof Panels : |  |
| 8.3.1 | Material : |  |
| 8.3.2 | Thickness : |  |
| 8.4 | Floor Panels : |  |
| 8.4.1 | Material : |  |
| 8.4.2 | Thickness : |  |
| 8.4.3 | Type of anti-slip coating : |  |
| 9.0 | Service Doors |  |
| 9.1 | No. of Service Doors : |  |
| 9.2 | Position of Service Doors : |  |
|  | Dimension of Service Door : - Front Height : Width : - Rear Height : Width : - Middle Height : Width : |  |
| 10.0 | Emergency Exit |  |
| 10.1 | No. of Emergency Doors : |  |
| 10.2 | Position of Emergency Doors : |  |

Table 22 of AIS-007 (Revision 5)

| 10 3 | Dimension of Emergency Door : - Ist Height : Width : - IInd Height : Width |  |
| --- | --- | --- |
| 11.0 | Window |  |
| 11.1 | Window (other than Emergency exit) |  |
| 11.1.1 | Dimension of Window aperture along with the detailed drawing showing the dimensions |  |
| 11.1.2 | Height of upper edge of window aperture from gangway floor (mm) |  |
| 11.1.3 | Type of window |  |
| 11.1.4 | Compliance to AIS-068 (Yes/No): |  |
| 11.2 | Emergency Windows |  |
| 11.2.1 | No. of Emergency Windows : |  |
| 11.2.2 | Position of Emergency Windows : |  |
| 11.2.3 | Area (HxW in sq. m) : |  |
| 12.0 | Escape Hatch |  |
| 12.1 | No. of Emergency Hatches : |  |
| 12.2 | Position of Emergency Hatches : |  |
| 12 3 | Area (HxW in sq. m) |  |
| 13.0 | Steps |  |
| 13.1 | Height of Ist Step : |  |
| 13.2 | Height of Other Steps : |  |
| 13.3 | Depth of steps : |  |
| 14.0 | Floor : |  |
| 14.1 | Floor Height from the ground (unladen): |  |
| 14.2 | Slope of floor : |  |
| 15.0 | Gangway |  |
| 15.1 | Height : |  |
| 15.2 | Width (diameter of gauging device – lower cylinder) : |  |
| 15.3 | Width (diameter of gauging device – upper cylinder) : |  |

Table 22 of AIS-007 (Revision 5)

| 16.0 | Handrails & Handholds : |  |
| --- | --- | --- |
| 16.1 | Position (attach dimension layout) : |  |
| 16.2 | No. of Handholds : |  |
| 16.3 | Diameter of Handholds : |  |
| 16.4 | Type of anti-slip coating / covering : |  |
| 17.0 | Stepwell Guard : |  |
| 17.1 | Height from the floor : |  |
| 17.2 | Projection from the side wall : |  |
| 18.0 | Seats |  |
| 18.1 | Driver/Co-driver or Front Passenger Seat |  |
| 18.1.1 | Make |  |
| 18.1.2 | Type |  |
| 18.1.3 | Identification Number |  |
| 18.1.4 | Seat Drawing no. |  |
| 18.2 | Passenger Seats : |  |
| 18.2.1 | Make |  |
| 18.2.2 | Type |  |
| 18.2.3 | Identification Number (S) |  |
| 18.2.4 | Seat Drawing no. |  |
| 18.2.5 | Seat Layout(S) : Enclose the Layout Drawings |  |
| 18.2.6 | Seat width : |  |
| 18.2.7 | Width of available space for one seating position : |  |
| 18.2.8 | Height of backrest : |  |
| 18.2.9 | Width of Armrest : |  |
| 18.2.10 | Depth of Seat cushion (base) : |  |
| 18.2.11 | Seat Pitch : |  |
| 18.2.12 | Seat base height : |  |
| 18.2.13 | Torso angle : |  |
| 18.2.14 | Seat base thickness : |  |
| 18.2.15 | Seat back thickness : |  |
| 18.2.16 | Clearance space for seated passengers facing partition : |  |
| 18.2.17 | Free Height over seating position : |  |
| 18.2.18 | Seat anchorage layout drawing ( with anchorage cross section and hardware used details) |  |

Table 22 of AIS-007 (Revision 5)

| 19.0 | Cabin Luggage Rack : |  |
| --- | --- | --- |
| 19.1 | Width from side wall : |  |
| 19.2 | Height from Roof : |  |
| 20 .0 | Driver Partition : |  |
| 20.1 | Dimension of partition with respect to rear edge of driver seat : (rear most position of driver seat) |  |
| 21.0 | Driver’s Work Area : |  |
| 21.1 | Width from the right side wall : |  |
|  | Distance of driver partition from the driver seat back : |  |
|  | Distance from H-point to Roof Top : |  |
|  | Distance between Heel Point and H-Point : |  |
|  | Distance of H-Point from Floor : |  |
|  | Distance of lower end of steering wheel from driver seat back : |  |
|  | Thigh clearance of Steering Wheel |  |
| 22.0 | External Projections |  |
| 22.1 | Ornaments : |  |
| 22.2 | Projection for head light : |  |
| 22.3 | Radiator grills (Applicable of on external surface) : |  |
| 22.4 | Gap between individual elements : |  |
| 22.5 | Radius of curvature of individual element : |  |
| 22.6 | Body Panel ( In case of radius of curvature of folds in body panels are less than 2.5mm the scaled drawing of folds contour and H value as per Annex A of SS29/IS 13942 is required (to be submitted) : |  |
| 22.7 | Radius of curvature of lateral Rain/Air deflector: Hinges : Handles : |  |
| 23.0 | Power Operated Service door |  |
| 23.1 | Name of the Manufacturer : |  |
| 23.2 | Identification : |  |
| 23.3 | Position of control : |  |

Table 22 of AIS-007 (Revision 5)

| 24 0 | Automatic Service door |  |
| --- | --- | --- |
| 24.1 | Name of the Manufacturer : |  |
| 24.2 | Identification : |  |
| 24.3 | Position of controls : |  |
| 24.4 | Control Circuit (schematic diagram) : |  |
| 25.0 | Emergency Door – Warning Device |  |
| 25.1 | Name of the Manufacturer : |  |
| 25.2 | Identification : |  |
| 25.3 | Position of device : |  |
| 26.0 | Door locks and hinges |  |
| 26.1 | Door lock : |  |
| 26.1.1 | Name of Manufacturer : |  |
| 26.1.2 | Identification mark : |  |
| 26.2 | Door hinge : |  |
| 26.2.1 | Name of Manufacturer : |  |
| 26.2.2 | Identification mark : |  |
| 27.0 | Safety glass |  |
| 27.1 | Front wind shield (laminated) : |  |
| 27.1.1 | Make |  |
| 27.1.2 | Identification : |  |
| 27.1.3 | Type (flat/curved, clear/tinted) : |  |
| 27.1.4 | Thickness mm : |  |
| 27.1.5 | No. of pieces : |  |
| 27.1.6 | Radius of curvature (If curved) : |  |
| 27.2 | Side Windows: |  |
| 27.2.1 | Make |  |
| 27.2.2 | Identification |  |
| 27.2.3 | Type (flat/curved, clear/tinted, toughened) : |  |
| 27.2.4 | Thickness mm : |  |
| 27.2.5 | Radius of curvature (If curved) : |  |
| 27.3 | Rear Window: |  |
| 27.3.1 | Make |  |
| 27.3.2 | Identification |  |
| 27.3.3 | Type (flat/curved, clear/tinted, toughened) : |  |
| 27.3.4 | Thickness mm : |  |
| 27.3.5 | Radius of curvature (If curved) : |  |

Table 22 of AIS-007 (Revision 5)

| 28.0 | Rear view mirror |  |
| --- | --- | --- |
| 28.1 | Left : |  |
| 28.1.1 | Name of Manufacturer : |  |
| 28.1.2 | Type : |  |
| 28.1.3 | Dimension & radius of curvature : |  |
| 28.1.4 | Identification Mark: |  |
| 28.2 | Right : |  |
| 28.2.1 | Name of Manufacturer : |  |
| 28.2.2 | Type : |  |
| 28.2.3 | Dimension & radius of curvature : |  |
| 28.2.4 | Identification Mark: |  |
| 28.3 | Inside : |  |
| 28.3.1 | Name of Manufacturer : |  |
| 28.3.2 | Type : |  |
| 28.3.3 | Dimension & radius of curvature : |  |
| 28.3.4 | Identification Mark: |  |
| 28.4 | Sketch showing mounting arrangement of mirrors |  |
| 29.0 | Wind Screen Wiper |  |
| 29.1 | Type : |  |
| 29.2 | No. of wipers : |  |
| 29.3 | Wiper motor : |  |
| 29.3.1 | Name of Manufacturer : |  |
| 29.3.2 | Type and identification : |  |
| 29.3.3 | Rated voltage : |  |
| 29.3.4 | Frequency of wiping : |  |
| 29.4 | Wiper arm : |  |
| 29.4.1 | Length : |  |
| 29.4.2 | Name of Manufacturer : |  |
| 29.4.3 | Identification Mark: |  |
| 29.5 | Wiper blade : |  |
|  | Length : |  |
| 29.5.2 | Name of Manufacturer : |  |
| 29.5.3 | Identification Mark: |  |
|  | Rubber material : |  |
| 29.6.1 | Type of fixing (As per IS 7827) : |  |
| 29.6.2 | Drawing indicating the seat back angle, seat travel, H point, Rake angle ,F dimension And steering wheel position as per AIS-011 |  |

Table 22 of AIS-007 (Revision 5)

| 30.0 | Wind Screen Washer |  |
| --- | --- | --- |
| 30.1 | Name of Manufacture: : |  |
| 30.2 | Type : |  |
| 30.3 | Number of nozzles : |  |
| 30.4 | Spray Area : |  |
| 30.5 | Identification Number: |  |
| 31.0 | Equipment for occupant's safety |
| 31.1 | Driver Seat belt : |  |
| 31.1.1 | Name of Manufacture: : |  |
| 31.1.2 | Type : |  |
| 31.1.3 | Number : |  |
| 31.1.4 | Identification Number: |  |
| 31.2 | Driver Seat belt anchorage : |  |
| 31.2.1 | Name of Manufacturer : |  |
| 31.2.2 | Type : |  |
| 31.2.3 | Number : |  |
| 31.3 | Head restraint : |  |
| 31.3.1 | Name of Manufacturer : |  |
| 31.3.2 | Type : |  |
| 31.4 | Passenger Seat : |  |
| 31.4.1 | Name of Manufacturer : |  |
| 31.4.2 | Type : |  |
| 31.4.3 | Frame structure Material : |  |
| 31.4.4 | Section size: |  |
| 31.4.5 | Pad material: |  |
| 31.4.6 | Upholstery : |  |
| 31.4.7 | Identification Number: |  |
| 32.0 | Bumper |  |
| 32.1 | Front Size: |  |
| 32.2 | Rear Size: |  |
| 32.3 | Clearance between bumper & body : |  |
| 33.0 | Fuel filler |
| 33.1 | Aperture : |  |
| 33.2 | Position : |  |

Table 22 of AIS-007 (Revision 5)

| 34.0 | Fire Extinguisher |
| --- | --- |
| 34.1 | Number : |  |
| 34.2 | Type : |  |
| 34.3 | Capacity : |  |
| 34.4 | Name of Manufacture: : |  |
| 35.0 | First Aid Equipment |  |
| 35.1 | Number : |  |
| 35.2 | Contents : |  |
| 36.0 | Towing devices |  |
| 36.1 | Type : |  |
| 36.2 | Name of manufacturer : |  |
| 36.3 | Capacity : |  |
| 36.4 | Identification Number |  |
| 37.0 | Automotive bulbs : |  |
| 37.1 | Head lamp bulb (main and dip) |  |
| 37.1.1 | Make |  |
| 37.1.2 | Designation as per AIS-034 |  |
| 37.2 | Parking Lamp bulb – Front |  |
| 37.2.1 | Make |  |
| 37.2.2 | Designation as per AIS-034 |  |
| 37.3 | Parking Lamp bulb - Rear |  |
| 37.3.1 | Make |  |
| 37.3.2 | Designation as per AIS-034 |  |
| 37.4 | Direction indicator lamp bulb - front |  |
| 37.4.1 | Make |  |
| 37.4.2 | Designation as per AIS-034 |  |
| 37.5 | Direction indicator lamp bulb – rear |  |
| 37.5.1 | Make |  |
| 37.5.2 | Designation as per AIS-034 |  |
| 37.6 | Direction indicator lamp bulb – side |  |
| 37.6.1 | Make |  |
| 37.6.2 | Designation as per AIS-034 |  |
| 37.7 | Front Position Lamp bulb |  |
| 37.7.1 | Make |  |
| 37.7.2 | Designation as per AIS-034 |  |

Table 22 of AIS-007 (Revision 5)

| 37.8 | Rear Position Lamp ( tail lamp )Bulb |  |
| --- | --- | --- |
| 37.8.1 | Make |  |
| 37.8.2 | Designation as per AIS-034 |  |
| 37.9 | Stop lamp bulb |  |
| 37.9.1 | Make |  |
| 37.9.2 | Designation as per AIS-034 |  |
| 37.10 | Number plate lamp bulb |  |
| 37.10.1 | Make |  |
| 37.10.2 | Designation as per AIS-034 |  |
| 37.11 | End out Marker bulb |  |
| 37.11.1 | Make |  |
| 37.11.2 | Designation as per AIS-034 |  |
| 37.12 | Reversing lamp bulb |  |
| 37.12.1 | Make |  |
| 37.12.2 | Designation as per AIS-034 |  |
| 37.13 | Stop Lamp Bulb (S3) |  |
| 37.13.1 | Make |  |
| 37.13.2 | Designation as per AIS-034 |  |
| 37.14 | Front Fog Lamp Bulb |  |
| 37.14.1 | Make |  |
| 37.14.2 | Designation as per AIS-034 |  |
| 37.15 | Rear Fog Lamp Bulb |  |
| 37.15.1 | Designation as per AIS-034 |  |
| 37.16 | Side Marker Lamp Bulb |  |
| 37.16.1 | Make |  |
| 37.16.2 | Designation as per AIS-034 |  |
| 38.0 | Head Lamp |  |
| 38.1 | Name of Manufacturer : |  |
| 38.2 | Type and Identification : |  |
| 38.3 | Number and colour : |  |
| 39.0 | Tail lamp |  |
| 39.1 | Name of Manufacturer : |  |
| 39.2 | Type and Identification : |  |
| 39.3 | Number and colour : |  |

Table 22 of AIS-007 (Revision 5)

| 40.0 | Parking lamp |  |
| --- | --- | --- |
| 40.1 | Front : |  |
| 40.1.1 | Name of Manufacturer : |  |
| 40.1.2 | Type and Identification : |  |
| 40.1.3 | Number and colour : |  |
| 40.2 | Rear : |  |
| 40.2.1 | Name of Manufacturer : |  |
| 40.2.2 | Type and Identification : |  |
| 40.2.3 | Number and colour |  |
| 41.0 | Stop lamp |  |
| 41.1 | Name of Manufacturer : |  |
| 41.2 | Type and Identification : |  |
| 41.3 | Number and colour : |  |
| 42.0 | Reversing lamp |
| 42.1 | Name of Manufacturer : |  |
| 42.2 | Type and Identification : |  |
| 42.3 | Number and colour : |  |
| 43.0 | Direction indicator lamp |  |
| 43.1 | Front : |  |
| 43.1.1 | Name of Manufacturer : |  |
| 43.1.2 | Type and Identification : |  |
| 43.1.3 | Number and colour : |  |
| 43.2 | Rear : |  |
| 43.2.1 | Name of Manufacturer : |  |
| 43.2.2 | Type and Identification : |  |
| 43.2.3 | Number and colour : |  |
| 43.3 | Side : |  |
| 43.3.1 | Name of Manufacturer : |  |
| 43.3.2 | Type and Identification : |  |
| 43.3.3 | Number and colour : |  |
| 43.4 | Type of flasher : |  |
| 44.0 | Number Plate Lamp |  |
| 44.1 | Name of Manufacturer : |  |
| 44.2 | Type and Identification : |  |
| 44.3 | Number and colour : |  |

Table 22 of AIS-007 (Revision 5)

| 45.0 | Emergency signaling equipment |  |
| --- | --- | --- |
| 45.1 | Front : |  |
| 45.1.1 | Name of Manufacturer : |  |
| 45.1.2 | Type and Identification : |  |
| 45.1.3 | Number and colour : |  |
| 45.2 | Rear : |  |
| 45.2.1 | Name of Manufacturer : |  |
| 45.2.2 | Type and Identification : |  |
| 45.2.3 | Number and colour : |  |
| 45.3 | Side : |  |
| 45.3.1 | Name of Manufacturer : |  |
| 45.3.2 | Type and Identification : |  |
| 45.3.3 | Number and colour |  |
| 46.0 | Reflector |  |
| 46.1 | Rear : |  |
| 46.1.1 | Name of Manufacturer : |  |
| 46.1.2 | Type and Identification : |  |
| 46.1.3 | Number and colour : |  |
| 46.1.4 | Area : |  |
| 46.2 | Side : |  |
| 46.2.1 | Name of Manufacturer : |  |
| 46.2.2 | Type and Identification : |  |
| 46.2.3 | Number and colour : |  |
| 46.2.4 | Area : |  |
| 47.0 | Top light |  |
| 47.1 | Name of Manufacturer: : |  |
| 47.2 | Type and Identification : |  |
| 47.3 | Number and colour : |  |
| 48.0 | Internal Lighting & Illumination |  |
| 48.1 | Driver Cab lighting : |  |
| 48.1.1 | Type : |  |
| 48.1.2 | Name of Manufacturer : |  |
| 48.1.3 | Number : |  |
| 48.1.4 | illumination intensity : |  |

Table 22 of AIS-007 (Revision 5)

| 48 .2 | Passenger Compartment Lighting |  |
| --- | --- | --- |
| 48.2.1 | Type : |  |
| 48.2.2 | Name of Manufacturer : |  |
| 48.2.3 | Number : |  |
| 48.2.4 | Illumination intensity : |  |
| 48.3 | Other Area Lighting |  |
| 48.3.1 | Type : |  |
| 48.3.2 | Name of Manufacturer : |  |
| 48.3.3 | Number : |  |
| 48.3.4 | Illumination intensity : |  |
| 49.0 | Electrical Circuit |  |
| 49.1 | Circuit Diagram (attach details): |  |
| 50.0 | Electrical Cables |  |
| 50.1 | Name of Manufacturer : |  |
| 50.2 | Conductor Cross section : |  |
| 50.3 | Insulation Class : |  |
| 51.0 | Fuse |  |
| 51.1 | Type & Make : |  |
| 51.2 | Name of Manufacturer : |  |
| 52.0 | Master switch for electrical : |  |
| 52.1 | Type & Make : |  |
| 52.2 | Name of Manufacturer : |  |
| 53.0 | Flammability Test as per IS 15061:2002 (as applicable ) |  |
| 53.1 | Seat and its accessories |  |
| 53.1.1 | Name of Manufacturer : |  |
| 53.1.2 | Material Grade |  |
| 53.1.3 | Material Type |  |
| 53.1.4 | Component Part No. and Batch No. |  |
| 53.1.5 | Identification Code |  |
| 53.1.6 | Drawing No. |  |
| 53.2 | Interior lining of the roof |  |
| 53.2.1 | Name of Manufacturer : |  |
| 53.2.2 | Material Grade |  |
| 53.2.3 | Material Type |  |
| 53.2.4 | Component Part No. and Batch No. |  |

Table 22 of AIS-007 (Revision 5)

| 53.2.5 | Identification Code |  |
| --- | --- | --- |
| 53.2.6 | Drawing No. |  |
| 53.3 | Interior lining of side walls |  |
| 53.3.1 | Name of Manufacturer : |  |
| 53.3.2 | Material Grade |  |
| 53.3.3 | Material Type |  |
| 53.3.4 | Component Part No. and Batch No. |  |
| 53.3.5 | Identification Code |  |
| 53.3.6 | Drawing No. |  |
| 53.4 | Interior lining of rear walls |  |
| 53.4.1 | Name of Manufacturer : |  |
| 53.4.2 | Material Grade |  |
| 53.4.3 | Material Type |  |
| 53.4.4 | Component Part No. and Batch No. |  |
| 53.4.5 | Identification Code |  |
| 53.4.6 | Drawing No. |  |
| 53.5 | Separation walls |  |
| 53.5.1 | Name of Manufacturer : |  |
| 53.5.2 | Material Grade |  |
| 53.5.3 | Material Type |  |
| 53.5.4 | Component Part No. and Batch No. |  |
| 53.5.5 | Identification Code |  |
| 53.5.6 | Drawing No. |  |
| 53.6 | Floor |  |
| 53.6.1 | Name of Manufacturer : |  |
| 53.6.2 | Material Grade |  |
| 53.6.3 | Material Type |  |
| 53.6.4 | Component Part No. and Batch No. |  |
| 53.6.5 | Identification Code |  |
| 53.6.6 | Drawing No. |  |
| 53.7 | Luggage racks |  |
| 53.7.1 | Name of Manufacturer : |  |
| 53.7.2 | Material Grade |  |
| 53.7.3 | Material Type |  |
| 53.7.4 | Component Part No. and Batch No. |  |
| 53.7.5 | Identification Code |  |

Table 22 of AIS-007 (Revision 5)

| 53.7.6 | Drawing No. |  |
| --- | --- | --- |
| 53.8 | Heating and ventilation pipe |  |
| 53.8.1 | Name of Manufacturer : |  |
| 53.8.2 | Material Grade |  |
| 53.8.3 | Material Type |  |
| 53.8.4 | Component Part No. and Batch No. |  |
| 53.8.5 | Identification Code |  |
| 53.8.6 | Drawing No. |  |
| 53.9 | Thermal and or acoustic function |  |
| 53.9.1 | Name of Manufacturer : |  |
| 53.9.2 | Material Grade |  |
| 53.9.3 | Material Type |  |
| 53.9.4 | Component Part No. and Batch No. |  |
| 53.9.5 | Identification Code |  |
| 53.9.6 | Drawing No. |  |
| 53.10 | Luminaries. |  |
| 53.10.1 | Name of Manufacturer : |  |
| 53.10.2 | Material Grade |  |
| 53.10.3 | Material Type |  |
| 53.10.4 | Component Part No. and Batch No. |  |
| 53.10.5 | Identification Code |  |
| 53.10.6 | Drawing No. |  |
| 54.0 | Rear Under run protective Device (RUPD) fitment as per IS 14812:2000 |  |
| 54.1 | Height of lower edge from ground (mm) |  |
| 54.2 | Width of the device (mm) |  |
| 54.3 | Location of Point P1 and P2 (mm) |  |
| 54.4 | Overall width of rear axle |  |
| 54.5 | Material |  |
| 54.6 | Drawing of the RUPD with dimensions |  |
| 54.7 | Installation drawing showing rear extremity of bus , chassis ROH (mm) and chassis cross section details |  |
| 55.0 | Lateral Protective Device (LPD) fitment as per IS 14682:1999 |  |
| 55.1 | Drawing of the LPD with dimensions |  |
| 55.2 | Installation drawing of the LPD with installation dimensions |  |
| 55.3 | Material |  |

Table 22 of AIS-007 (Revision 5)

| 56.0 | Interior fitting compliance as per AIS-047 established - Yes/No |  |
| --- | --- | --- |
| 57.0 | Interior Fittings as per AIS-047, as applicable |  |
| 57.1 | Instrument Panel (Dash Board) |  |
| 57.2 | Make |  |
| 57.3 | Identification No. / Part No. |  |
| 57.4 | Material |  |
| 57.5 | Drawing showing the mounting details, over all size and all control switches with dimensions |  |
| 57.6 | Additional details for interior fitting tests to be given (if test is already conducted, this information need not be submitted). |  |
| 57.6.1 | Instrument Panel Variants with photographs (With / without Airbag, Music system, AC ) |  |
| 57.6.2 | Material used for instrument Panel |  |
| 57.6.3 | Drawings |  |
| 57.6.3.1 | Instrument Panel mounting (With hardware details) |  |
| 57.6.3.2 | ‘H’ point co-ordinates for each seating position |  |
| 57.6.3.3 | Cross sectional drawings for each projection more than 3.2 |  |
| 57.6.3.4 | Cross sectional Drawing of Gear shift lever |  |
| 57.6.3.5 | Drawing of Grab handle with cross section |  |
| 57.6.3.6 | Drawing of Sunvisor with details of metal wire used |  |
| 57.6.3.7 | Drawing of lamp assembly mounted at roof |  |
| 57.6.4 | Name of manufacturer of the Interior fitting components |  |
| 57.6.4.1 | Instrument Panel |  |
| 57.6.4.2 | Sun Visor |  |
| 57.6.4.3 | Roof Light |  |
| 57.6.4.4 | Grab Handle |  |
| 57.6.4.5 | Gear Lever |  |
| 57.6.4.6 | Hand Brake Lever |  |
| 57.6.4.7 | Seats (Need not be specified if done already) |  |
| 57.6.4.8 | Seat Belts (Need not be specified if done already) |  |
| 57.6.4.9 | Music System (if provided) |  |
| 57.6.4.10 | Cigarette lighter (if provided) |  |
| 58.0 | Any other additional information the Bus manufacturer /Bus body builder would like to declare |  |
| Foot Note:- The technical specification details for Sr. Nos.7.0 ( tyres ) , 28.0 ( RVM), 29.0 ( Wiper), 31.0 ( seat belt and seat belt anchorages), 37.0 (automotive bulbs),38.0 (head lamp), 39.0 (tail lamp), 40.0 (parking lamp), 41.0 (stop lamp) , 42.0 (reversing lamp), 43.0 (indicator lamp), 44.0 (number plate lamp), 45.0 (emergency signaling equipment), 46.0 (reflector), 47.0 (top light), 53.0 (Flammability), 54.0 (RUPD), 55.0 (LPD), and 56.0 (Interior fittings ) need not be filled by the applicant, if there is no change in basically approved specification issued during the certification of chassis (Drive away chassis/Cowl & chassis/Cab & Chassis/Chassis with FES) |

Table 22A of AIS-007 (Revision 5)

(To be submitted by the Bus manufacturer or the Bus Body Builder along with Table 22)

| Rule No. | Subject | Name of the Manufacturer ( Please give information for every supplier / vendor under the same para, separate lines ) | TAC No. / BIS License No / Test Report No. as applicable. (indicate validity date ) ( Application Ref No. allotted by concerned Test Agency, If approval is in the process ) | Possible date of submission of required approval, if the same is in process |
| --- | --- | --- | --- | --- |
| 100 | Safety Glass |  |  |  |
|  | Windscreen |  |  |  |
|  | Side |  |  |  |
|  | Rear |  |  |  |
| 101 | Windscreen Wiping System |  |  |  |
|  | Wiping Syste |  |  |  |
|  | Washing System |  |  |  |
|  | Wiper Blade |  |  |  |
| 104 | Reflex Reflector |  |  |  |
|  | Rear, Red |  |  |  |
|  | Side, Amber |  |  |  |
| 119(1) | Horns |  |  |  |
| 119(1) | Horn installation |  |  |  |
| 124/ 1 | Automotive Bulbs |  |  |  |
|  | Bulbs for Headlamp (main/dipped ) |  |  |  |
|  | Bulbs for Front position lamp |  |  |  |
|  | Bulbs for Front parking lamp |  |  |  |
|  | Bulbs for Rear position lamp |  |  |  |
|  | Bulbs for rear parking lamp |  |  |  |
|  | Bulbs for Stop lamp |  |  |  |
|  | Bulbs for Reversing lamp |  |  |  |
|  | Bulbs for Front Direction indicator lamp |  |  |  |
|  | Bulbs for Rear direction indicator lamp |  |  |  |
|  | Bulbs for Side repeater lamp |  |  |  |
|  | Bulbs for Hazard warning lamp |  |  |  |
|  | Bulbs for High mount stop lamp |  |  |  |
|  | Bulbs for Top light lamp |  |  |  |

Table 22A of AIS-007 (Revision 5)

|  | Bulbs for Number plate lamp |  |  |  |
| --- | --- | --- | --- | --- |
|  | Bulbs for Front fog lamp |  |  |  |
|  | Bulbs for Rear fog lamp |  |  |  |
|  | Bulbs for Side marker lamps |  |  |  |
| 124(20) | Installation of Lighting and Light Signaling devices |  |  |  |
| 124/2 | Hydraulic Brake Hose, if applicable |  |  |  |
| 124/3 | Hydraulic Brake Fluid, if applicable |  |  |  |
| 124/7 | Fuel Tank (metallic) or Fuel Tank (plastic) |  |  |  |
| 124/8 | Wheel Rims |  |  |  |
| 124/12 | Bus Window Retention test |  |  |  |
| 124/14 | Wheel fastener(s), Hub Caps |  |  |  |
| 124/16 | Door Locks & Hinges |  |  |  |
|  | Door Locks |  |  |  |
|  | Passenger Door(s) |  |  |  |
|  | Driver door |  |  |  |
|  | Emergency exit (if provided) |  |  |  |
|  | Door Hinges |  |  |  |
|  | Passenger Door(s) |  |  |  |
|  | Driver door |  |  |  |
|  | Emergency exit (if provided) |  |  |  |
| 124/17 | Hood Latch |  |  |  |
| 124/20 | Lighting, Signaling & Indicating Systems : |  |  |  |
|  | Head Light : |  |  |  |
|  | Fog Light : |  |  |  |
|  | Rear License Plate Light : |  |  |  |
|  | Rear Position Light |  |  |  |
|  | Tail Light : |  |  |  |
|  | Stop Light : |  |  |  |
|  | Directional Indicator Light: |  |  |  |
|  | Front : |  |  |  |
|  | Rear : |  |  |  |
|  | Side : |  |  |  |
|  | Parking Light : |  |  |  |
|  | Reversing Light : |  |  |  |
|  | High Mounted Stop Light : |  |  |  |

Table 22A of AIS-007 (Revision 5)

| 124/20 | Installation of Lighting and Signaling systems |  |  |  |
| --- | --- | --- | --- | --- |
| 124/36 | Strength of superstructure of passenger vehicles. |  |  |  |
| 124/37 | Flammability requirements for M3 category vehicles. |  |  |  |
|  | Seat and its accessories |  |  |  |
|  | Interior lining of the roof |  |  |  |
|  | Interior lining of side walls |  |  |  |
|  | Interior lining of rear walls |  |  |  |
|  | Separation walls |  |  |  |
|  | Floor |  |  |  |
|  | Luggage racks |  |  |  |
|  | Heating and ventilation pipe |  |  |  |
|  | Thermal and or acoustic function |  |  |  |
|  | Luminaries |  |  |  |
| 124/1A | Vehicle Rear Under run Protective device & Lateral Protective Device |  |  |  |
| 125/1A | Safety Belt and Safety Belt Anchorages |  |  |  |
| 125(1) | Rear View Mirror |  |  |  |
|  | Main Mirror large ( Class-II ) |  |  |  |
|  | Main Mirror small ( Class-III ) |  |  |  |
|  | Close proximity Mirror ( Class-V ) |  |  |  |
|  | Close proximity Mirror ( Class-V ) |  |  |  |
| 125/(2) | Installation of Rear View Mirror |  |  |  |
| 125/1C | Seats ( Driver seat, Co-driver seat and passenger seat ) |  |  |  |
| 125(6) | Seat Anchorages ( Driver seat, Co-driver seat and Passenger seat ) |  |  |  |
| 138 | Warning Triangles |  |  |  |

| Table 23 of AIS-007 (Revision 5) |
| --- |
| ADDITIONAL TECHNICAL SPECIFICATION OF HYBRID / ELECTRIC VEHICLES TO BE SUBMITTED BY VEHICLE MANUFACTURER (To be used for approval of Hybrid / Electric Vehicles in lieu of Annex G of AIS-102 (Part 1) and Annex B of AIS-102 (Part 2) |
| 1.0 | General Description of Vehicle |
| 1.1 | Vehicle Model |
| 1.2 | Vehicle Type |
| 1.3 | Drawing and /or photographs of the vehicle |
| 1.4 | Type of hybrid vehicle (Externally chargeable/Not externally chargeable) |
| 1.5 | Mode selection switch provided: Yes/No |
| 1.5.1 | If yes the modes available |
| 1.5.2 | In the case of Externally Chargeable HEV’s |
| 1.5.2.1 | The hybrid mode which can be proven to have the highest electricity consumption |
| 1.5.2.2 | The hybrid mode which can be proven to have the highest fuel consumption |
| 1.5.3 | In the case of Not Externally Chargeable HEV’s, the mode which is automatically set after turn on of the ignition key (normal mode) |
| 2.0 | Description of the Traction Battery |
| 2.1 | Trade Name and Mark of the Battery |
| 2.2 | Kind of Electro – Chemical Couple |
| 2.3 | Nominal Voltage , V |
| 2.4 | Battery Maximum Thirty Minutes Power (Constant Power Discharge), kW |
| 2.5 | Battery Performance in 2 h Discharge (Constant Power or Constant Current ) |
| 2.5.1 | Battery Energy , kWh |
| 2.5.2 | Battery Capacity , Ah in 2 h |
| 2.6 | End of Discharge Voltage Value , V |
| 2.7 | Provision of ventilation for battery Yes / No |
| 2.7.1 | Brief description of the ventilation system adopted in the vehicle. (Refer AIS-038 clause 3.1.1). Provide drawing if necessary. |
| 2.7.2 | Brief description of the ventilation system adopted in the battery compartment. (Refer AIS-038 clause 3.1.2). Provide drawing if necessary. |
| 2.8 | On-board Indication of battery state of charge (Applicable if there is a “pure electric mode” |
| 2.8.1 | Details of indication when state of charge of the battery reaches a level when the manufacturer recommends re-charging. |
| 2.8.1.1 | Indication format. |
| 2.8.1.2 | Relationship of state of charge indicator and the indication. |
| 2.8.1.3 | Make |

Table 23 of AIS-007 (Revision 5)

| 2.8.1.4 | Model |
| --- | --- |
| 2.8.2 | Indication of state of charge of battery reaches a level at which driving vehicle further may cause damage to batteries |
| 2.8.2.1 | Indication format. |
| 2.8.2.2 | Relationship of state of charge indicator and the indication. |
| 2.9 | Battery Mass, kg |
| 2.10 | Brief description of maintenance procedure, if any |
| 3.0 | Description of the Drive Train |
| 3.1 | General |
| 3.1.1 | Make |
| 3.1.2 | Type |
| 3.1.3 | Use : Mono motor / multi motors (number) |
| 3.1.4 | Transmission Arrangement parallel / transaxial / others |
| 3.1.5 | Test Voltage , V |
| 3.1.6 | Motor Nominal Speed , Min -1 |
| 3.1.7 | Motor Maximum Speed, Min –1 or by default reducer outlet shaft / gear box speed (specify gear engaged ) |
| 3.1.8 | Maximum Power Speed , Min –1 and km/h |
| 3.1.9 | Maximum Power , kW |
| 3.1.10 | Maximum Thirty Minutes Power, kW |
| 3.1.11 | Maximum Thirty Minutes speed km/h |
| 3.1.12 | Range |
| 3.1.13 | Speed at the beginning of the range, Min –1 |
| 3.1.14 | Speed at the end of the range , Min –1 |
| 3.2 | Traction Motor |
| 3.2.1 | Make |
| 3.2.2 | Working Principle |
| 3.2.2.1 | Direct current / alternating current / number of phases |
| 3.2.2.2 | Separate excitation / series / compound |
| 3.2.2.3 | Synchron / asynchron |
| 3.2.2.4 | Coiled rotor / with permanent magnets / with housing |
| 3.2.2.5 | Number of Poles of the Motor |
| 3.2.3 | Motor power curve (kW) with motor RPM (min-1) / vehicle speed in km/h |
| 3.3 | Power Controller |
| 3.3.1 | Make |
| 3.3.2 | Type |
| 3.3.3 | Control Principle : vectorial / open loop / closed / other (to be specified ) |

Table 23 of AIS-007 (Revision 5)

| 3.3.4 | Maximum effective current supplied to the Motor, A |
| --- | --- |
| 3.3.5 | Voltage range use , V to V |
| 3.4 | Cooling System motor : liquid / air controller : liquid / air |
| 3.4.1 | Liquid cooling equipment characteristics |
| 3.4.1.1 | Nature of the liquid , circulating pumps , yes / no |
| 3.4.1.2 | Characteristics or make(s) and type(s) of the pump |
| 3.4.1.3 | Thermostat : setting |
| 3.4.1.4 | Radiator : drawing(s) or make(s) and type(s) |
| 3.4.1.5 | Relief valve : pressure setting |
| 3.4.1.6 | Fan : Characteristics or make(s) and type(s) |
| 3.4.1.7 | Fan : duct |
| 3.4.2 | Air-cooling equipment characteristics |
| 3.4.2.1 | Blower : Characteristics or make(s) and type(s) |
| 3.4.2.2 | Standard air ducting |
| 3.4.2.3 | Temperature regulating system yes / no |
| 3.4.2.4 | Brief description |
| 3.4.2.5 | Air filter : make(s) type(s) |
| 3.4.3 | Maximum temperatures recommended by the manufacturer: |
| 3.4.3.1 | Motor Outlet: oC |
| 3.4.3.2 | Controller inlet : oC |
| 3.4.3.3 | At motor reference point(s) oC |
| 3.4.3.4 | At controller reference point(s) oC |
| 3.5 | Insulating Category : |
| 3.5.1 | International Protection (IP)-Code : |
| 3.6 | Lubrication System Principle: Bearings : friction / ball Lubricant : grease / oil Seal : yes / no Circulation : with / without |
| 4.0 | Charger (Applicable only for Externally Chargeable HEV’s ) |
| 4.1 | Charger : on board / external |
| 4.1.1 | Trademark , model, rating |
| 4.2 | Description of the normal profile of charging system: |
| 4.3 | Specifications of mains: |
| 4.3.1 | mains : single phase/ three phase |
| 4.3.2 | Nominal Voltage (V) & frequency (Hz) with tolerances : |

Table 23 of AIS-007 (Revision 5)

| 4.4 | Reset period recommended between the end of the discharge and the start of the charge |
| --- | --- |
| 4.5 | Recommended duration of a complete charge |
| 4.6 | In case of on-board charger |
| 4.6.1 | Continuous rating of charger socket (A) : |
| 4.6.2 | Time rating (h) of charger socket, if any : |
| 4.6.3 | Whether soft-start facility Yes / No : |
| 4.6.4 | Maximum initial in-rush current (A) |
| 5.0 | Electrical Details of Vehicle for Functional Safety |
| 5.1 | Schematic diagram showing the electrical layout giving all major electrical items along with their physical location in the vehicle. It shall include batteries, power-train components, protection fuses, circuit breakers etc. (Reference in AIS-038 clause 3.1.3) |
| 5.2 | Specifications of circuit breakers/ fuses used for protection of batteries / power-train (Reference in AIS-038 clause 3.1.3) |
| 5.2.1 | IS / IEC specifications |
| 5.2.2 | Rating (A) |
| 5.2.3 | Opening time (ms) |
| 5.3 | Working voltage V (Reference in AIS-038 clause 3.2) |
| 5.4 | Schematic highlighting physical location of live parts having working voltage greater than 60 V DC or 25 V AC (Reference in AIS-038 clause 3.2.1.2) |
| 5.5 | Electric cables / connectors / wiring harness (Reference in AIS-038 clause 3.2.2.2) |
| 5.5.1 | IEC protection class |
| 5.5.2 | Insulation material used |
| 5.5.3 | Conduits provided Yes / No |
| 5.6 | List of exposed conductive parts of on-board equipment. (Reference in AIS-038 clause 3.2.2.3) |
| 5.6.1 | Any potential equalization resistance used to electrically connect these parts Yes/ No |
| 5.6.2 | If yes, give details |
| 5.7 | List of failures due to which the vehicle will come to standstill (Reference in AIS-038 clause 3.3.6) |
| 5.8 | List of conditions under which the performance of vehicle is limited and how. (Reference in AIS-038 clause 3.3.13 ) |
| 5.9 | Declaration regarding Design guidelines followed with respect to various requirements |
| 6.0 | Electrical energy consumption of Vehicle in W-h/km, as per clause 5.5.1 of AIS-039 |
| 7.0 | Special gear shifting pattern if any |

ANNEX I

(See introduction)

COMMITTEE COMPOSITION *

Automotive Industry Standards Committee

| Chairman |  |
| --- | --- |
| Shri Shrikant R. Marathe | Director, The Automotive Research Association of India, Pune |
| Members | Representing |
| Representative from | Ministry of Road Transport & Highways (Dept. of Road Transport & Highways), New Delhi |
| Representative from | Ministry of Heavy Industries & Public Enterprises (Department of Heavy Industry), New Delhi |
| Shri S. M. Ahuja | Office of the Development Commissioner, MSME Ministry of Micro, Small & Medium Enterprises, New Delhi |
| Shri P. C. Joshi | Bureau of Indian Standards, New Delhi |
| Director/ Shri D. P. Saste (Alternate) | Director , Central Institute of Road Transport, Pune |
| Director | Indian Institute of Petroleum, Dehra Dun |
| Director | International Centre for Automotive Technology |
| Director | Vehicles Research & Development Establishment, Ahmednagar |
| Representatives from | Society of Indian Automobile Manufacturers (SIAM) |
| Shri T. C. Gopalan | Tractor Manufacturers Association, New Delhi |
| Shri U. S. Harite | Automotive Components Manufacturers Association of India, New Delhi |

Member Secretary

Mrs. Rashmi Urdhwareshe

Sr. Deputy Director

The Automotive Research Association of India, Pune

* At the time of approval of this Automotive Industry Standard (AIS)

# Text boxes

Note : The number of rows shown are illustrative. The actual number of rows will depend on the number of changes.